## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Part 1: Distribution and differentiation of body dimensions
Module 2 – Learning ergonomics - Part 1

## Slide 2: Distribution and differentiation of body dimensions
Overview
Body height
Eye height
Working height
Ergonomic requirement characteristics for the user-oriented dimensional design of products and workplaces
Body height classes and distribution of percentiles
Factors influencing the variance in body dimensions
Operator population
Geometric design of products with consideration for the widest anthropometric variance within the operator population
Sources of data for body dimensions and normative references
Field of fixation
Depth of reach
Distribution of body dimensions
© Michael Hüter
Notes: Various body dimensions must be considered during the design of machines, products and workplaces.
The following will be considered below:
Body height classes and body dimensions
Factors influencing the variance in body dimensions
Influence of different operator populations upon the design of products
Different body heights give rise to ergonomic requirement characteristics for the user-oriented design of products and workplaces. These requirements will also be addressed below.
Certain data sources and standards, which will also be referred to, are available as tools for this purpose (see Slide 14 ff.).

## Slide 3: Objectives of design
Requirement categories of the user-oriented dimensional design of products and workplaces:
    Safety (observance of safety distances, personal protective equipment)
    Reachability, functional reliability in human-machine interface (e.g. in relation to the actuation of manual controls)
    Adequate freedom of movement (accessibility for parts of the body, space envelopes, active areas)
    Physiologically favourable postures (adaptation to changing loads)
Notes: Design objectives in which body dimensions are an element
For machinery, production workplaces and consumer goods
Working life, leisure, living environment, gerontological technology, information technology, mobility

## Slide 4: Objectives of design (2)
    Determining of individual and group-specific design dimensions in consideration of the anthropometric variance of the users
    User-friendly products for everyday use (e.g. optimization of usability, convenience)
    Optimization of the visual geometry (visual dimensions, angles of view, fields of view)
© Michael Hüter
Notes: Design objectives in which body dimensions are an element
For machinery, production workplaces and consumer goods
Working life, leisure, living environment, gerontological technology, information technology, mobility

## Slide 5: Body height classes – distribution of percentiles
Image source: : Kamusella: http://ergotyping.net/index.php?title=Ergonomie-Grundlagen:_Anthropometrie
Division of body heights into body height classes (values for the 18-65 age group in mm to DIN 33402-2:2007)
Males
Females
5th percentile
50th percentile
5th percentile
95th percentile
50th percentile
95th percentile
Female
Male
90% of females
95% of the male and female operator population
1535
1855
1625
1650
1720
1750
Notes: In anthropometrics:
The discipline of measurement of the human body and of its dimensional relationships
Quantitative determining and description of individual body dimensions
Statistical processing of the data
Consideration of dimensional developments for the comparison of different groups
Application:
Garment industry (fashion, dedicated clothing for occupational groups, protective clothing and equipment)
Ergonomics (dimensional design of workplaces, technical work equipment, consumer products)
Percentiles are stated for body dimensions
Percentile (quantile) = relative cumulative frequency of a group
Percentile: one-hundredth values, thus:
Division into 100 parts of equal size; divided by 1% segments
Percentile values reflect the distribution of the measured values and indicate, for a given body dimension, the proportion in percent of persons of a random population sample that do not exceed the stated percentage value or are smaller than the stated percentile.
For example, the 95th percentile of the height of males aged 18 to 65 in Germany is 1,855 mm. This means that 95% of this population group are shorter than or equal to 1,855 mm, and 5% are taller (DIN 33402-2 Supplement 1).

## Slide 6: Percentile distribution in the unisex model – body dimension distribution
Image source: Kamusella: http://ergotyping.net/index.php?title=Ergonomie-Grundlagen:_Anthropometrie
5th percentile female
95. percentile
unisex
50. percentile
unisex
5th percentile
unisex
95th percentile male
95. percentile female
50th percentile male
50th percentile female
5th percentile male
Body height dimensions:
⇒ Normal distribution
Discrete values distributed symmetrically around the mean
Width, depth and circumferential body dimensions
⇒ Skewed distribution
Abnormal distribution
Notes: Males and females were combined in a random sample. The usual percentile values of 5, 50, 95 thus represent body dimensions of men and women independent of sex. The unisex model encompasses substantially fewer persons between P5 and P95. Design for the 5th and 95th percentiles fails to consider short women and tall men respectively.
 Influence upon stress and comfort
Sex-specific percentiles should therefore be considered wherever possible
Text field top right animated

## Slide 7: Body dimensions to DIN 33402-2 – excerpt
© Michael Hüter
Notes: Original excerpt from DIN 33402-2:2007, a purely national standard, for certain body dimensions. Current endeavours are for body dimensions to be retained in a purely national standard only where they are not already standardized at European or national level. Agreement has already been reached on the definitions; the hurdle must however first be overcome of each country providing its own values for the dimension concerned. DIN 33402-2:2007 contains body dimensions of the residential population within the Federal Republic of Germany, i.e. the population examined is not defined on the basis of nationality.

## Slide 8: Sources of data for body dimensions and normative references
"European human being"
Values for body dimensions according to "Arbeitswissenschaftliche Erkenntnisse Nr. 108"
Based upon: Arbeitswissenschaftliche Erkenntnisse Nr. 108, Bundesanstalt für Arbeitsschutz und Arbeitsmedizin, Dortmund 1998
© Michael Hüter
Measurement number: (fig.) | Measurement description: |  | Percentile | 
 |  | 5 | 50 | 95
9 | seat height (body seat height, stem length) | 790 | 905 | 985
10 | eye level | 680 | 790 | 860
11 | shoulder height | 510 | 623 | 695
12 | shoulder-elbow-length | 288 | 346 | 410
13 | elbow height | 190 | 243 | 280
14 | thigh height | 112 | 146 | 170
15 | elbow-wrist-length | 240 | 279 | 318
16 | elbow-to-elbow breadth | 390 | 478 | 540
17 | shoulder (bideltoid) breadth | 395 | 474 | 485
18 | shoulder (biacromial) breadth | 320 | 380 | 425
19 | hip breadth | 333 | 368 | 440
20 | popliteal height | 380 | 444 | 495
21 | abdominal depth | 195 | 237 | 350
22 | knee height | 460 | 530 | 602
Notes: Comment that these values are from BAuA findings; the values embody a unisex model, i.e. the data are presented for both men and women. All test subjects in a random sample studied were merged irrespective of sex and evaluated as a single group.
A European standard (harmonized B2 standard) containing anthropometric data for the calculation of access dimensions (EN 547-1/2/3) is available. Body dimensions in this series of standards are provided for the 5th, 50th, 95th and 99th percentile for combined male and female populations from European studies. (Population groups of at least 3 million within Europe were considered.)

## Slide 9: Factors influencing the body dimensions
Sex | e.g. body height (50th percentile, german, 18-65 Y.) Male  female approx. 13 cm
Age | e.g. body height (50th percentile) 20-24  60-64 1765 mm  1685 mm (difference approx. 8 cm)
Secular acceleration (Increase in body height, comparison between generations) | Increase per decade in the past: approx. 1 cm Current reduction in acceleration Increasing body mass and corpulence
Ethnic differences | e.g. body height Northern Europeans > Southern Europeans approx. 8 cm
Differences in proportions (Ratio of trunk length to crotch height) | Long-trunked and short-trunked individuals
Notes: Influencing factors: sex, age, secular acceleration, ethnic differences (population) and proportional differences
Secular acceleration: a development that is accelerated compared to the average value
This is evident in two directions:
a) Accelerated and increased growth in height of a younger generation compared to an earlier generation. The reason: socio-economic living conditions (improvements in health conditions, food of high quality, drop in the frequency and severity of disease during the growth phase)
The secular acceleration is now approaching a limit value asymptotically. The value of 1 cm per decade is therefore no longer applicable (gradual stagnation).
  The secular trend in Germany is particularly notable among taller people; shorter persons remain on the short side.
  Observe the age of the anthropometric data.
  b) Positive secular trend in body weight
  Proportional differences: ratio of trunk length to crotch height
  Short trunk, long legs
  Long trunk, short legs
Last two text fields animated

## Slide 10: International body dimensions – ethnic differences
Image Source: Kamusella: http://ergotyping.net/index.php?title=Ergonomie-Grundlagen:_Anthropometrie
5th percentile female – 95th percentile male
South-east Africa North America Australia
Japan South-east Europe Germany N. Europe
Notes: The image shows the 5th percentile for females and the 95th percentile for males for seven countries or continental regions.

## Slide 11: Differences in proportions – body proportion types
Trunk/leg length, arm length
Image source: Kamusella: http://ergotyping.net/index.php?title=Ergonomie-Grundlagen:_Anthropometrie
short arms
long arms
mean-length arms
Long-trunked individual
Mean-length arms
Short-trunked individual
Mean-length arms
Mean proportion
Mean-length arms
Notes: Disproportionalities within distributions must also be considered. For example, some individuals have a long trunk and short legs, others a short trunk and long legs, whilst sharing the same body height. Comparable disproportionalities are also observed in arm lengths.
Ratio of trunk length to crotch height:
  Short trunk, long legs
  Long trunk, short legs
This is for example relevant to the variance in the position of the eye point between persons of identical body height but with different body proportions.
One study for eample has shown that truck drivers in Germany deviate from the male population as a whole in eight of their body dimensions: for example, their proportions exhibit a tendency towards short legs (Brandenburgische Umweltberichte 10, 2001).

## Slide 12: Proportion types: representative individuals
Anthropometric variance within the operator population for:
Image source Kamusella: http://ergotyping.net/index.php?title=Ergonomie-Grundlagen:_Anthropometrie
Long leg: short-trunked
Long leg: short-trunked
M95: 95th percentile male
F5: 5th percentile female
Reference point for all users
Position of controls
SEAT
PEDAL
SEAT
Reference point for all users
Notes: Specifications for example for the seat adjustment ranges and pedal adjustment ranges are shown here for long-trunked and short-trunked individuals between the 5th and 95th percentile. The ideal position of manual controls (steering wheel) is also determined by the body dimensions. Use of geometric reference points (fixing)
If in the example on the right, all users are fixed with respect to the eye point, the result is seat-height adjustment and adjustment for height and depth of the pedals and hand controls.
In the left-hand image, all users are to have pedal contact with the ball of the foot, resulting in a need for vertical and horizontal seat adjustment; the steering wheel must also be adjustable in its height and distance.
The point of sight (e.g. for view of traffic lights) is an issue, since the anthropometric diversity gives rise to major differences.

## Slide 13: Somatotypes in combination with proportion types
Geometric design of products in consideration of the widest anthropometric variance within the operator population:
Image source: Kamusella: http://ergotyping.net/index.php?title=Ergonomie-Grundlagen:_Anthropometrie
Short corpulent woman (short legs and arms)
Tall slim man (long legs and arms)
Tall slim woman (long legs and arms)
Small corpulent man (short legs and arms)
Variation series 1
Example:
Variation series 1:
Very tall, long legs, slim  Very short, short legs, corpulent
Notes: Somatotype: physique type
(slim, muscular, corpulent)
Left-hand image: at an identical heel point, the seat and steering wheel must permit horizontal and vertical adjustment.
Right-hand image: the position of the steering wheel can be left unchanged for the two reference persons, whereas the seat must permit horizontal and vertical adjustment.
Further variants exist besides the variation series 1 shown in the example.
Dimensions for corpulence change in the course of a lifespan and exhibit higher values particularly among older individuals. This must be considered in the design.

## Slide 14: User group – design dimensions – body dimension
Image source: Kamusella: http://ergotyping.net/index.php?title=Ergonomie-Grundlagen:_Anthropometrie
Anthropometric realities
Sex, age group
Population group/nationality
Body dimension percentiles
Acceleration stage etc.
Requirements presented by specific regulations (e.g. body height limit for pilots)
Definition of the target group
Work task, purpose
Design objective; design parameters
Work requirements (motor, visual)
Safety requirements
Posture
Selection of body dimension(s) based upon the design dimension
Consideration of the age of the data sources, scope, regulations governing measurement
Specification of the design dimension
Determining of the design dimension
Selection of the percentile dimension
Consideration of positive and negative correction values
E.g. stretched/relaxed posture, footwear, items of equipment, clothing
Regulations for calculation of design dimensions Consideration of reference systems
Insertion points, reference points; location, orientation
Notes: Ergonomic solutions are developed for a target group the characteristics of which must be delimited as precisely as possible. The design object exhibits design properties (e.g. seat width) that are characterized by aspects that include the anthropometric properties of the user group. The geometrical relationship between the design dimensions (design parameters) is defined by their location and movement within a reference system (e.g. the seat reference point to the heel point; system of coordinates fixed within the vehicle). Restrictive dependencies exist for anthropometrically defined design dimensions in the form of percentiled body dimensions and ranges of joint movement. This reference system influences which body dimensions are considered by the design dimension. For example, should the reference system lie on the front edge of a machine bench and the maximum reach (immediately in front of the body) is to be defined, the distance from the shoulder joint to the front edge of the machine must first be determined as a function of the trunk depth, in order for the distance comprising the upper arm-forearm length plus the distance to the palm of the hand to be determined from this pivotal point. The complete area of reach is dependent upon the mobility of the shoulder joint and collar bone. The design dimensions (e.g. the range of seat adjustment) are generally determined by calculation based upon one or more body dimensions in consideration of the necessary percentile and allowances on either side.

## Slide 15: Work in a distribution warehouse
Before:
Unfavourable working heights, resulting in constrained postures during retrieval and scanning of the goods
Module 2 – Learning ergonomics - Part 1

## Slide 16: Work in a distribution warehouse
After:
Adjustment of the working heights, resulting in an upright working posture during retrieval and scanning of the goods

## Slide 17: Work in a distribution warehouse: comparison of trunk postures
Before installation of the loading stand:
After use of the loading stand:
Postures involving inclination of the trunk
Forward inclination of the trunk [°] (angle classes)
Forward inclination of the trunk [°] (angle classes)
Angle range [°]
Angle range [°]
Duration of measurement: 00:08:37
Duration of measurement: 00:31:40
Time component [%]
Time component [%]
Notes: Reduction of the time spent with a trunk inclination within the range between 20° and 90° from approximately 20% to around 2% of the time.

## Slide 18: Important literature for Module 2-1
EN 349 Safety of machinery – Minimum gaps to avoid crushing of parts of the human body
EN 547-1 Safety of machinery – Human body measurements – Part 1: Principles for determining the dimensions required for openings for whole body access into machinery
EN 547-2 Safety of machinery – Human body measurements – Part 2: Principles for determining the dimensions required for access openings
EN 547-3 Safety of machinery – Human body measurements – Part 3: Anthropometric data
EN 614-2 Safety of machinery – Ergonomic design principles – Part 2: Interactions between the design of machinery and work tasks
EN ISO 7250-1 Basic human body measurements for technological design – Part 1: Body measurement definitions and landmarks
DIN 33402-1 Ergonomie - Körpermaße des Menschen – Teil 1: Begriffe, Messverfahren
DIN 33402-2 Ergonomie - Körpermaße des Menschen – Teil 2: Werte
DIN 33402-2 Beiblatt 1 Körpermaße des Menschen – Teil 2: Werte; Beiblatt 1: Anwendung von Körpermaßen in der Praxis
Notes: The German and non-German populations are no longer distinguished by nationality in DIN 33402
DIN 33402-2 Ergonomics – Human body dimensions – Values
 Anthropometric data of the population resident in the Federal Republic of Germany (including the migrant population)
 By sex
 18-65 age bracket
 Confidence range 5th to 95th percentile

## Slide 19: Important literature for Module 2-1
DIN 33402-3 Körpermaße des Menschen – Teil 3: Bewegungsraum bei verschiedenen Grundstellungen und Bewegungen
DIN 5566-1 Schienenfahrzeuge - Führerräume – Teil 1: Allgemeine Anforderungen
DIN 5566-2 Schienenfahrzeuge – Führerräume – Teil 2: Zusatzanforderungen an Eisenbahnfahrzeuge
EN ISO 3411 Earth-moving machinery – Physical dimensions of operators and minimum operator space envelope
EN ISO 14738 Safety of machinery - Anthropometric requirements for the design of workstations at machinery
DIN Taschenbuch 390 Körpermaße und Körperkräfte
EN ISO 15537 Principles for selecting and using test persons for testing anthropometric aspects of industrial products and designs
Anthropologischer Datenatlas (1986) in: Flügel B., Greil H., Sommer K. (1986): Anthropologischer Atlas. Grundlagen u. Daten
Notes: Body dimensions of Europeans (1998) in:
Arbeitswissenschaftliche Erkenntnisse Nr. 108, Bundesanstalt für Arbeitsschutz und Arbeitsmedizin, Dortmund 1998
European:
 P5 and P95 limit percentiles:
 Northern region: limit for 95th percentile
 Southern region: limit for 5th percentile
 Limit percentiles, not differentiated by sex
 18-60 age bracket

## Slide 20: Important literature for Module 2-1
Körpermesswerte des Europamenschen (1998) in: Arbeitswissenschaftliche Erkenntnisse Nr. 108, Bundesanstalt für Arbeitsschutz und Arbeitsmedizin, Dortmund 1998
For further standards, see KAN-Paxis - NoRA: Searching for standards
Notes: Body dimensions of Europeans (1998) in:
Arbeitswissenschaftliche Erkenntnisse Nr. 108, Bundesanstalt für Arbeitsschutz und Arbeitsmedizin, Dortmund 1998
European:
 P5 and P95 limit percentiles:
 Northern region: limit for 95th percentile
 Southern region: limit for 5th percentile
 Limit percentiles, not differentiated by sex
 18-60 age bracket

## Slide 21: Important literature for Module 2-1
BULLINGER, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
Gebhardt, H.; Schäfer, A.; Lang, K.-H. (2009): Anthropometrische Daten in Normen – Bestandsaufnahme und Bedarfsanalyse unter besonderer Berücksichtigung des Arbeitsschutzes. KAN-Bericht 44. Hrsg.: KAN Sankt Augustin.
Gebhardt, H.; Mühlemeyer, C. (2012): Anforderungen an einen gegliederten Prüffinger nach DIN EN 60529 auf der Grundlage aktueller anthropometrischer Daten. Gutachten (KAN GA 49). Hrsg.: KAN Sankt Augustin.
Greil, H.; Voigt, A.; Scheffler, C. (2007): Optimierung der ergonomischen Eigenschaften von Produkten für ältere Arbeitnehmerinnen und Arbeitnehmer – Anthropometrie. Fb. 1299. Hrsg.: Bundesanstalt für Arbeitsmedizin und Arbeitsschutz Dortmund/Berlin/ Dresden
JÜRGENS, H. W.; MATZDORFF, I.; WINDBERG, J. (1998): Internationale anthropometrische Daten als Voraussetzung für die Gestaltung von Arbeitsplätzen und Maschinen. 1. Auflage. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Arbeitswissenschaftliche Erkenntnisse, 108).
Notes: Body dimensions of Europeans (1998) in:
Arbeitswissenschaftliche Erkenntnisse Nr. 108, Bundesanstalt für Arbeitsschutz und Arbeitsmedizin, Dortmund 1998
European:
 P5 and P95 limit percentiles:
 Northern region: limit for 95th percentile
 Southern region: limit for 5th percentile
 Limit percentiles, not differentiated by sex
 18-60 age bracket

## Slide 22: Important literature for Module 2-1
KIRCHNER, J.-H.; BAUM, E. (1990): Ergonomie für Konstrukteure und Arbeitsgestalter. München: Carl Hanser.
KIRCHNER, A.; KIRCHNER, J.-H.; KLIEM, M.; MÜLLER, J. M. (1990): Räumlich-ergonomische Gestaltung: Handbuch. Bremerhaven: Wirtschaftsverlag NW (Schriftenreihe der Bundesanstalt für Arbeitsmedizin und Arbeitsschutz Fb. 632).
LANGE, W.; WINDEL, A. (12. Auflage, 2008): Kleine ergonomische Datensammlung. Dortmund: Bundesanstalt für Arbeitsschutz und Arbeitsmedizin.
SCHEFFLER, C.; SCHÜLER, G. (2013): „Rohfassung eines Leitfadens für die richtige Auswahl und Anwendung anthropometrischer Daten“. KAN-Studie 51. Hrsg.: VFA, Sankt Augustin.
Notes: Body dimensions of Europeans (1998) in:
Arbeitswissenschaftliche Erkenntnisse Nr. 108, Bundesanstalt für Arbeitsschutz und Arbeitsmedizin, Dortmund 1998
European:
 P5 and P95 limit percentiles:
 Northern region: limit for 95th percentile
 Southern region: limit for 5th percentile
 Limit percentiles, not differentiated by sex
 18-60 age bracket

## Slide 23: Impressum
Autor of this module:
Dr.-Ing. Christiane Kamusella
Faculty of Mechanical Science and Engineering Institute of Technical Logistics and Work Sciences
Chair of Labour Sciences
Christiane.Kamusella@tu-dresden.de
Initiated and funded by:
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de http://ergonomie.kan-praxis.de