## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Part 2: Visual data for anthropometric design
Module 2 – Learning ergonomics

## Slide 2: Visual data for anthropometric design
Vertical field of fixation
Horizontal field of fixation
© Michael Hüter
Overview
Visual axis
Viewing distance
Central and peripheral vision
Visual regions and their significance
Relationship between character height and viewing distance
Notes: Visual data are of particular importance for the dimensional design of workplaces. All relevant information, work equipment and work items should be positioned such that they are within the field of fixation. On the machining centre for example, the machining workplace must be positioned suitably so as to permit observation.
For this reason, the concepts above all of visual axis, viewing distance and field of fixation are explained in this chapter, and reference is made to peripheral and central vision and to the relevance of different visual regions.

## Slide 3: Important parameters of visual geometry – visual axis
Visual axis = visual line (line linking the eye with the viewed object)
      Peripheral detection tasks: visual axis as per the direction of view
 Perception of stimuli (existence of signals)
      Monitoring tasks: Normal visual axis dependent upon the posture
Relaxed eyes:
      Angle of visual axis to the horizontal: approx. 10°-15°
      Relaxed head:
      Angle of visual axis to the horizontal, standing: approx. 15°-20°; sitting: approx. 25°
Visual axis determined externally
Notes: Visual axis: line connecting a fixated object and the centre of the fovea centralis; corresponds approximately to the visual line (link between the fixated object and the mechanical centre of rotation of the eye)
Peripheral detection tasks: the operator is warned by the system
During peripheral detection tasks, the direction of view (deflection of the visual axis) is dependent upon the centre of attention to be observed; the task is to detect the existence of a signal
Around the visual axis, particular attention must be paid here to the field of fixation (see following slides)
Monitoring tasks: the operator actively seeks information (e.g. reading of displays, VDT work)
During monitoring tasks, the visual axis must be located along a visual line below the horizontal (eye and head muscles in a relaxed posture, hence below the horizontal)
The user actively looks for information from this relaxed position

## Slide 4: Total deflection of the normal visual axis:
0°
Normal visual axis in a seated position: head and visual angle 35°-40°
Normal visual axis in a standing position: head and visual angle 25°-35°

## Slide 5: Important visual geometry parameters – visual axis
Manual process control
    Upright forward seating position
    Deflection of visual axis from the horizontal: approx. 35°
  Automatic process control
    Rearward seating position
    Deflection of visual axis from the horizontal:
    35° – (10° to 15°)
    Rearward inclination of the trunk
Notes: During automatic process control, the emphasis lies upon the task of process observation, which is performed in a relaxed rearward seating posture
The rearward seating posture causes the eye point to move backwards and slightly downwards; the visual axis rotates upwards by the angle of the trunk inclination
In order to ensure a perpendicular view of the surface of the control desk arrangement, the inclination of the surface must be adjusted to this posture

## Slide 6: Important visual geometry parameters – viewing distance
The viewing distance is dependent upon:
Form of the visual task
Illuminance
Viewer's personal visual faculty
Size, form and colour of the viewed object
Structure (texture) and contrast of the surroundings of the viewed object

## Slide 7: Guide values for preferred viewing distances:
120-250 mm: ultra-fine work (ultra-small parts, watches, electronic components)
250-350 mm: fine work (radio and TV equipment)
Up to 500 mm: moderately coarse work (reading of displays, work on machinery)
> 500-1500 mm: coarse work (packing, grinding work)
> 1500 mm: distance vision

## Slide 8: Connection symbol hight – viewing distance
Recognizability of symbols: vertical size of the viewed object
Consider: viewing distance only one influencing factor
Further: illuminance, contrast, legibility of symbols
Height of viewed object h in mm
Viewing distance S in mm
Visual angle in minutes
•
h = S · tan α
α in minute of arc °)
 Ideal : 18` - 22`
 Permissible : 15`- 18`
Dimension of the visual angle
Notes: Height of the object h: extent of the object, apperent size
Symbol sizes that are selected so as to be easily identifiable at the viewing distance are dependent upon the visual angle.
Set visual angles are refered to the verticle size of the viewed object for monitors, control room technology, display of machines etc.
Visual angle:
Angle the apex of which is at the eye and the legs of which encompass the object being viewed.
At a given viewing distance:
Visual angle white < visual angle black < visual angle coloured
 Symbol height white < symbol height black < symbol height coloured
Visual angle in minutes: ideal range: 18´-22´
This can be used to determine a symbol size at a specified viewing distance.
Conversely, if the symbol size is known, the viewing distance to the eye can be calculated at which the symbol should be located.
The resolving capacity is also stated in terms of a visual angle, and indicates the ability to perceive two points situated close to each other as being separate. The points require a minimum distance.
The smallest angular interval (resolving capacity) at which two points can be perceived as separate is, under ideal conditions, at a visual angle of approximately 1´; the average proportions are rather 2`
The reciprocal of the resolvableness is the visual acuity (Visus)
right example animated

## Slide 9: Visual region – central vision: fixation
Fixation:
Intentional viewing of an object with the fovea centralis
Duration of fixation ≥ 0.3 sec. at the point of fixation
Distance to the fixation point Visual acuity 3 degrees 50%
6-7 degrees 25%
Fovea centralis: point on the retina with the highest resolution  Central vision: 100% visual acuity
Main direction of vision at 1 degree from the fixation point
Notes: Central vision:
Fixation occurs = the view rests on one point (for approximately 0.3 seconds or longer)
Formation of a stimulus on the fovea centralis: 100% sharpness region
Sharp vision owing to photopic vision by means of the cones
With the pupil at maximum width and with adequate light
Extraction of detail information
At a distance from the centre of fixation of (for example) 3°, the visual acuity has already dropped to 50%

## Slide 10: Visual region – central vision vs. peripheral vision
Characteristic | Central system – fixation | Peripheral system
Absolute sensitivity to light | Low | High
Colour sensitivity | High | Low
Visual acuity (spatial resolving capacity) | High | Low
Sensitivity to movement (temporal resolving capacity) | Low | High
Specialization | Perception of details | Movement, change
Function | Analysis of content of viewed matter | "Alarm reflex", control of viewing movements "Orientation reflex", movement and change have highest priority
Notes: When tasks are assigned to central and peripheral vision, preference is given to the latter.
If a new object suddenly appears or movement occurs within the visual periphery, processes concerning the transmission and processing of information from the central visual region are blocked and reorientation of the head and eye initiated, in order for the object to be fixated.
The observer continually uses the information received peripherally in order to select fixation points.
Peripheral vision:
Occurs in the remaining region of the retina
Reduced visual acuity compared to the fovea
Delivers "only" orientation and background information
Simultaneous perception of all points of the field of view (perception through movement and/or contrast)
Low spatial resolution capacity
High temporal resolution capacity, therefore very sensitive to movements
Retinal periphery: = "wide-angle early-warning system"

## Slide 11: Visual region - field of view, colour field of view
19° green
20° red
26° yellow
27° blue
Source: DIN 15996 Bild- u. Tonbearbeitung in Film-, Video- u. Rundfunkbetrieben
Colour field of view < light-dark field of view
blue > yellow > red > green
Fields of view, left, right and binocular for light stimuli
Binocular horizontal colour field of view
central
+
peripheral vision
the spatial portion of an environment that can be perceived without movement of the head and eyes
Notes: The field of view describes the portion of the visual environment that can be perceived with fixed eyes. It encompasses central and peripheral (foveal) vision.
 Field of view = the spatial portion of an environment that can be perceived without movement of the head and eyes
Binocular field of view: left-hand image, inner frame (extension to the left/right: approx 60°; upwards: approx. 55°; downwards: approx. 45°)
Peripheral system
Peripheral field of view: perception of movement only
Location of visual objects to be monitored simultaneously
Binocular field of view: stereoscopic vision; at the edge (right eye, left eye) monocular (one-eyed) vision only
 There are zones of one-eyed (monocular) vision and zones in which both eyes overlap (binocular vision).
Bottom right-hand text field animated
Presentation of the colour field of view based upon presentations at http://www.multimedia-beratung.de/ergonomie/theorie/grundlagen/gesichtssinn.htm

## Slide 12: Visual region – maximum and ideal field of fixation
0°
35°
35°
15°
15°
Normal visual line with tense head posture
22°
38°
15°
0°
15°
± 15° Ideal field of fixation
Further visual region: extended field of fixation: with movement of the head and eyes, thus enlarged by movement of the head
Notes: Field of fixation:
Encompasses all points fixable by eye movement alone, without movement of the head
Distinction is drawn between horizontal and vertical field of fixation, according to axis of extension
The maximum possible field of fixation is not exploited, since the head is moved unconsciously in the direction of view before it is reached
Areas which are to be covered by eye movements alone must therefore be dimensioned according to the ideal field of fixation, with consideration for the viewing distance
Ideal field of fixation:
Viewing movements of approximately 15° either side of the visual line
Location of observed objects which must be fixated frequently
Location of hazard or warning displays
For example: reading of symbols in a line; tracking the needle of a display; registering the flashing of warning signals; visual monitoring of display states involving frequent changes in view; very rapid switching between viewed locations
Further visual fields:
Extended field of fixation:
The segment of the visual space that can be fixated with the body stationary and with movement of the head and eyes
The field of fixation, extended by head movement
Arrangement of objects that must be viewed rapidly in sequence
Location of the normal visual line below the horizontal, dependent upon the body (see illustration on Slide 2):
Shown here with head in a stressed neutral/zero position
Deflection of the visual line by 15° only
Maintaining the field of ± 15° in view comfortably with the eyes, no head movement required (eye movement within the comfort range)

## Slide 13: Examples
Source: IFA Institut für Arbeitsschutz der Deutschen Gesetzlichen Unfallversicherung, Sachgebiet Ergonomie
Examples – Visual Display Units in Control Rooms
M. Bockelmann, F. Nachreiner, P. Nickel: https://www.baua.de/DE/Angebote/Publikationen/Berichte/F2249.html
Crane operator's workplace
Fork-lift-truck operator's workplace

## Slide 14: Fork-lift truck with rotating cab
Rotating cab for fork-lift trucks: can be rotated through up to 180°
Provides the driver with a completely clear field of fixation; the load can be transported safely
Reversing with bulky loads no longer requires twisting of the trunk
Jungheinrich: winner of the 2007 German OSH prize
example: example: fork-lift truck

## Slide 15: Important literature for module 2-2
EN 894-2 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Part 2: Displays
EN ISO 14738 Safety of machinery – Anthropometric requirements for the design of workstations at machinery
EN ISO 9241-5 Ergonomic requirements for office work with visual display terminals (VDTs) – Part 5: Workstation layout and postural requirements
DIN 15996 Bild- und Tonbearbeitung in Film-, Video- und Rundfunkbetrieben – Grundsätze und Festlegungen für den Arbeitsplatz
EN ISO 11064-5 Ergonomic design of control centres – Part 5: Displays and controls
For further standards, see KAN-Paxis - NoRA: Searching for standards

## Slide 16: Important literature for module 2-2
Bockelmann, M.; Nachreiner, F.; Nickel, P. (2012): Bildschirmarbeit in Leitwarten. Handlungshilfen zur ergonomischen Gestaltung of Arbeitsplätzen nach der Bildschirmarbeitsverordnung. F 2249. Dortmund: Bundesanstalt für Arbeitsschutz und Arbeitsmedizin 2012
KIRCHNER, J.-H.; BAUM E. (1990): Ergonomie für Konstrukteure und Arbeitsgestalter. Munich: Carl Hanser.
LANGE, W.; WINDEL, A. (12th edition, 2008): Kleine ergonomische Datensammlung. Dortmund: Bundesanstalt für Arbeitsschutz und Arbeitsmedizin.
MARQUART, S. (1997): Handbuch der Ergonomie. Weiden: Schuch.
MARTIN, H. (1994): Grundlagen der menschengerechten Arbeitsgestaltung. Handbuch für die betriebliche Praxis. Cologne: Bund-Verlag
SACHS, S.; TEICHERT, H.-J.; RENTZSCH, M. (1994): Ergonomische Gestaltung mobiler Maschinen. Handbuch für Konstrukteure, Planer, Ergonomen, Designer und Sicherheitsfachkräfte. 1st edition. Landsberg: Ecomed.
SCHMIDTKE, H. (1993): Ergonomie. 3rd edition. Munich: Carl Hanser.

## Slide 17: Impressum
Author: Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by:
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de http://ergonomie.kan-praxis.de