## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Part 3: Tools for workplace and product design
Module 2 – Learning ergonomics

## Slide 2: The point is…
Dimension tables
Standardized calculation methods
Dimensional guideline recommendations
Template somatography
Computer-somatography (digital human model)
Virtual human model
© Michael Hüter
Eye height
Working height
Notes: A range of tools are available to support the design of workplaces and products such that consideration is given to diversity in human body dimensions (such as body heights and eye heights), and optimum workplace and product dimensions are thus attained for handling (for example working heights, depths of reach and fields of fixation on machining centres). These tools will be described below.
You will be introduced to:
Dimension tables
Standardized calculation methods
Dimensional guideline recommendations
Template and video-CAD somatography
Computer-somatography (digital human models)
Virtual human models

## Slide 3: Tools for workplace and product design
Dimension tables
Standardized calculation methods
Dimensional guideline recommendations
Template somatography
Computer somatography (digital human models in desktop systems)
Virtual human model in Powerwall and CAVE projection systems
Procedures/tools
Anthropometric realities of the operator population
Work requirements
Posture
Influencing variables, e.g.:
Notes: Dimension tables:
Generally in the form of anthropometric databases, see Module 2-1
For the graphical presentation of the human form (in accordance with technical drawing rules), body dimensions for certain body-height classes are stated in the form of joint-to-joint dimensions
Statement of clothing allowances
Standardized calculation methods generally include:
Design algorithms for the calculation of design measurements as a function of task-related requirements for visual monitoring and fine-motor co-ordination, with the aid of standardized dimension tables and guideline values and in consideration of percentile values for certain types of workplace (standing, seated)
Calculation formulae encompass the determining for example of legroom and footroom measurements and of seat and working surface heights, with reference to anthropometric data
Dimensional guideline recommendations generally include:
Statement of working heights for seated and standing tasks as a function of the work requirements for various body heights of male and female users
Interpolation of selected design dimensions (workbench height, seat height, working height) as a function of body height and requirements height
Template somatography and digital human models: see next slide
Virtual reality (VR) is the presentation and simultaneous perception of reality and its physical properties in an interactive, virtual environment, generated by computer in real time
CAVE: Cave Automatic Virtual Environment
Room for projection of a three-dimensional, illusory world in virtual reality
Cube with up to 6 projection screens
For example: generation of a complete and realistic impression of a car interior
Ergonomic analyses with subjective evaluation of visibility conditions, control interaction, sequences of operations, up to and including simple driving scenarios
Time and cost savings:
Results, for example from examination of collisions, assembly tests or crash analyses, are available for product optimization more quickly with VR prototypes than in the past

## Slide 4: Tools for workplace and product design
Use of body dimensions to determine design dimensions
Example: space requirements of a seated workplace
Example: design according to individual design objectives
Kamusella, Chr.: http://ergotyping.net/index.php?title=Anthropometrie:_Ableitung_von_Gestaltungsmaszen_aus_Koerpermaszen (in german)
Tools for the determining of design dimensions
Example: support for standing at a machine workstation
Kamusella, Chr.: http://www.ergotyping.net/index.php?title=Anthropometrie:_Hilfsmittel_zur_Ermittlung_von_Gestaltungsmaszen (in german)
Adjustment of the driver's seat in a service bus:
Brütting, M.; Böser, Chr.; Knipfer, Chr.; Ellegast, R.: http://fahrersitz.ifa.dguv.de/ (in german)

## Slide 5: Template somatography, employing templates of the body contour
Example: Kiel dummy
6 body heights; scales of: 1:2 und 1:5
      Very short female (1st percentile),
      Short male (5th percentile),
      Short female (5th percentile),
      Male of medium height (50th percentile),
      Tall female (95th percentile) ,
      Tall male (95th percentile)
  Dimensions to DIN 33408
  Most important joints (wrist, elbow, neck, knee, shoulder, hip and ankle joints) moveable in two dimensions: moveable elements, cam joints
© Michael Hüter
Notes: Tip: if possible, show body contour templates
Template somatography:
Somatography is the graphical representation of the human form
Several forms of template exist
Well-known examples of body contour templates are the Kiel dummy (1975), the Bosch templates (1978), the drawing templates to DIN 33408:2008, the Burg-Giebichenstein template (1986) and the Jenik template
Marking:
2D templates for the human form
In consideration of anthropometric dimensions (differentiation by percentile and sex)
In various views (plan, front elevation, side elevation)
With fixed or movable joints
In various scales
Paper-and-pencil method
Scale drawing of the design object is required
Body contour template is placed over the model/drawing.
The templates support package designs
Joints simplified by statement of the joint centre points (point joints)
Different body positions can be represented
Bosch template:
4 body heights; scale: 1:10
  Short female
  Female of medium height, short male
  Tall female, male of medium height
  Tall male
Rigid template
Indication of movement angle
Design of assembly workplaces
Kiel dummy:
6 body heights; scales of 1:1 and 1:5
  Very short female (1st percentile)  Short male (5th percentile)
  Short female (5th percentile)  Male of medium height (50th percentile)
  Tall female (95th percentile)  Tall male (95th percentile)
Moveable joints, link joints for shoulder, hip, knee
Jenik template:
Unisex types in sizes of 1500 mm, 1630 mm, 1760 mm and 1900 mm on a scale of 1:10

## Slide 6: Template somatography: sample applications
© Michael Hüter
What happened?
Acute failure of ergonomics!

## Slide 7: Template somatography: sample applications
Forestry planting plough: adaptation of seat position for F5 and M95
Postal delivery bicycle:
Adaptation of the frame size and facility for saddle and handlebar adjustment for F5 and M95
Source : Kamusella, Christiane:
Verbesserte Marktchancen durch eine ergonomische Produktgestaltung– In: Arbeitsschutz aktuell, Heft 1/1999, S. 12-16
© Michael Hüter
Notes: Example uses of template somatography
Postal delivery bicycle, right:
Customer specification: bicycle in one frame size only, no wheels of different size
Consequently: frame size for the 50th percentile men and women
Handlebars with height adjustment and with handlebar stem that can be adjusted for angle
Saddle adjustable for height
Forestry planting plough, left:
Frame size after modification: frame made narrower in order to reduce the required spread of users' legs
Seat adjustment: alternatively, at lower cost and technically simpler: adjustable footrest
Stretched arm of the 5th percentile woman (red template): indication of the area of reach in which plant boxes should be arranged (a short person must be able to reach everywhere)

## Slide 8: Seat reference points and their application
Hip point (H point)
Point on the median plane of a human being located at the theoretical intersection of the trunk axis and the longitudinal thigh axis projected onto the plane
H point/seating reference point/R point
Eye ellipse point line
© Michael Hüter
Notes: In order to provide uniform starting and orientation criteria for the design and positioning of seats and other interior elements of a mockup, binding reference points exist, which however differ from one sector to another. These reference points are then used to determine defined dimensions.
The H point (hip point) is very often used for this purpose.
Other sectors employ different points, which however are related to the hip point.
The SIP (seat index point, see next slide) is used for example for agricultural and construction machinery.
H point: design reference point for the ergonomic design of driving positions, application: vehicle design
Package design
Specification of the interior dimensions, e.g. criteria for limitation of the area of reach: presentation/determining of enveloping surfaces of the area of reach and its reference planes
Vision analysis: reference to eye points/to the eye ellipse
R point
Seat reference point defined by the vehicle manufacturer
At a specified adjustment position of the driver's seat and a specified trunk inclination, the R point lies at the H point
Determined by means of the SAE H point measurement machine
The eye ellipse is not easy to determine; it is not generally used.

## Slide 9: Further seat reference points and their application
Seat index point, SIP
Lies within a tolerance range of ±10 mm around the measured H point
Applications: agricultural and construction machinery
Seat reference point, SRP
Pivotal point between the backrest and squab of the seat Applications:
Railbound vehicles
Agricultural and forestry towing vehicles
Design eye point, DEP
Insertion point for pilots' seats
All pilots' eye points must coincide with the DEP
From there, the line of sight is defined
Notes: Seat index point, SIP
The SIP relates to the seat, the H point to the human being
Point on the mid vertical longitudinal axis of the seat at which the theoretical axes of the human trunk and the thigh intersect
Measured by means of a simple, rigid measuring facility
Lies within a tolerance range of ±10 mm around the measured H point
Publications in technical data sheets for the seats
Defined with reference to the machine; is not altered by the adjustment/vibration range of the seat
Applications: agricultural and construction machinery
Seat reference point (SRP)
Pivotal point between the backrest and squab of the seat
No explicit reference to the H point, since the displacement differs according to the seat type (e.g. hard or soft upholstery, form of the seat hollow etc.)
Application: railbound vehicles, agricultural and forestry towing vehicles, airliner passenger seats
Design eye point, DEP (also ERP = eye reference point)
Insertion point for pilots' seats
All pilots' eye points must coincide with the DEP
The line of sight is defined based upon the DEP

## Slide 10: Seat reference points - example of seat index point for construction machinery
SIP = H point
A human model (or template) is placed on the seat
SIP of the seat and H point of the human model are congruent
Source : Kamusella, Christiane (2008): Bestimmung der Koordinaten des SIP in Bezug zum Sitz (Hilfskonstruktion). Unveröffentlichtes Material, TU Dresden, Arbeitswissenschaft
Notes: In order to provide uniform starting and orientation criteria for the design and positioning of seats and other interior elements of a mockup, binding reference points exist, which however differ from one sector to another. These reference points are then used to determine defined dimensions.
The H point (hip point) is very often used for this purpose.
Other sectors employ different points, which however are related to the hip point.
The SIP (seat index point, see next slide) is used for example for agricultural and construction machinery.
H point: design reference point for the ergonomic design of driving positions, application: vehicle design
Package design
Specification of the interior dimensions, e.g. criteria for limitation of the area of reach: presentation/determining of enveloping surfaces of the area of reach and its reference planes
Vision analysis: reference to eye points/to the eye ellipse
R point
Seat reference point defined by the vehicle manufacturer
At a specified adjustment position of the driver's seat and a specified trunk inclination, the R point lies at the H point
Determined by means of the SAE H point measurement machine
The eye ellipse is not easy to determine; it is not generally used.

## Slide 11: Categories of digital human models
Source: Kamusella http://ergotyping.net/index.php?title=Anthropometrie:_Hilfsmittel_zur_Ermittlung_von_Gestaltungsmaszen#Menschmodelle
Notes: Biomechanical-kinetic models: describe movements of the human body in consideration of velocities, forces, moments and body masses
Anthropometric-kinematic models: are based upon anthropometric data and simulate movements of the body and of limbs without consideration of their causes (body forces)
Virtual reality: the IDO:Review tool permits realistic, three-dimensional presentation of digital models. In practice, this means that the 3D glasses give the user the impression of actually standing in front of the vehicle or of being within it. Objects can be hidden and unhidden, grasped, moved and measured.
In order to generate an impression of immerion, special output devices are required for the presentation of virtual environments. The most familiar forms of this equipment are the head-mounted display, large projection screens, and the CAVE. In order to create a spatial impression, two images are generated from different perspectives and presented (stereo projection). Different technologies exist for presenting each image to the desired eye. A distinction is drawn between active (such as LC shutter glasses) and passive (such as polarized filters or Infitec) technologies. Special input devices are required for interaction with the virtual world. Examples are the Spacemouse, data glove, wand and Flystick. Standard input devices such as keyboards or mice are however also used in some cases, as are highly specialized devices. Tracking systems are used to detect the position of objects in the real world.
(http://de.wikipedia.org/wiki/Virtuelle_Realit%C3%A4t)
Examples for digital human models
Manufacturing planning, digital factory: Jack provides a virtual environment for interactive design and optimization of manual tasks. In a 3D model of the real production environment, the work sequence can be defined by means of a virtual human model. (http://www.human-solutions.com/automotive_industry/ramsis_empower_de.php)
Ramsis: a 3D human model for ergonomic analysis and for supporting the design of products and workplaces, particularly in relation to vehicles; scientific generation of the ergonomic principles for Ramsis at Munich Technical University, Institute of Ergonomics, now a commercial product of Human Solutions GmbH; property of an automotive industry consortium
AnyBody:
Developed by AnyBody Technology A/S, Denmark
Ergonomic and biomechanical analyses
Static and dynamic models
Modelling of the skeleton and the muscles
Calculation of muscle and joint forces
Applications: automotive industry, aeronautics, aerospace, medicine/rehabilitation, sport, health protection
(See http://www.anybodytech.com)

## Slide 12: Digital human models – example of CharAT Ergonomics
Selected sequences for determining process and user characteristics of the operator's view by means of the CharAT Ergonomics human model and virtual view dynamics in digital prototyping
© Michael Hüter
Notes: Example: CharAT Ergonomics
Product of Virtual Human Engineering GmbH (core software); further development as an ergonomics tool in conjunction with TU Dresden Technical University, Labour Sciences Development of ergotyping tools at the Chair of Labour Sciences
Example application within a study project sponsored by the DFG German Resarch Foundation concerning the dynamic field of view on mobile machinery (TU Dresden, Chair of Labour Science in conjunction with the Chair of Construction Machines and Conveying Technology)
Data aggregation in the planning tool by means of the CharAT Ergonomics digital human model
The aggregated data comprise:
Position inputs for machine dynamics and environmental objects
Body movement data (dynamic body angles) via the CUELA measurement system of the IFA, Sankt Augustin
Eye tracking data for determining the directions of fixation for both eyes

## Slide 13: Digital human models – example of CharAT Ergonomics
Source: Kamusella, Chr.; Einsatz digitaler Ergonomiewerkzeuge –Anwendungsbeispiele. Handout at the meeting entitled "Digitale Ergonomie", held in Dresden on 14 November 2012 by the Federal institute for Occupational Safety and Health (BAuA)
Source: Gröllich, D. (2013):
Development of preventive design strategies for reducing physical stresses during airliner production. Unpublished material/concluding presentation, TU Dresden, Chair of Labour Sciences
Notes: Example: CharAT Ergonomics
Product of Virtual Human Engineering GmbH (core software); further development as an ergonomics tool in conjunction with TU Dresden Technical University, Labour Sciences Development of ergotyping tools at the Chair of Labour Sciences
Image, left: TU Dresden, Labour Science: ergotyping tools developed for the CharAT Ergonomics human model (view, body forces, load handling, posture)
Example shown: posture analysis according to RULA during the turning over of roof tiles
Image, right: TU Dresden, Labour Science: study of a chair concept in the form of a multifunctional unit for adaptation to assembly points with poor access during airliner production
Studies involving pressure measurement mats and the digital human model

## Slide 14: Digital human models – Example of CharAT Ergonomics
© Michael Hüter
Notes: Example: CharAT Ergonomics
Product of Virtual Human Engineering GmbH (core software); further development as an ergonomics tool in conjunction with TU Dresden Technical University, Labour Sciences Development of ergotyping tools at the Chair of Labour Sciences
Virtual 3D support in order to avoid undesirable risks during the development of new systems or equipment for the health sector
 Example: anthropometric adjustment to the medical personnel

## Slide 15: Digital human models – example category of virtual reality
© Michael Hüter
Notes: Example: ViveHuman in ViveLAB
Product of vivetech ltd. (www.vivetech.com)
ViVeLab is a complex collaborative online system for the virtual trialling and testing of production planning solutions and for simulating reciprocal influences between human beings and machines. This simulation tool can be used to model planning changes and analyse their effects in real time. ViVeLab uses cloud computing technology with powerful video streaming in order for users to perform virtual test tasks for products and design in a virtual test laboratory, in which they can cooperate with other experts in the cloud.

## Slide 16: Digital human model – further examples
RAMSIS https://www.human-solutions.com/en
Human Builder (formerly Safeworks) https://www.3ds.com/products-services/delmia/
Jack (formerly Any-Man/ eM-Human) https://www.plm.automation.siemens.com/de_de/Images/Jack_Human_tcm73-62436.pdf
DYNAMICUS https://www.ifm-chemnitz.de/produkte/mensch-technik-interaktion/alaskadynamicus/
AnyBody http://www.anybodytech.com
SANTOS https://www.santoshumaninc.com/
EMA https://www.imk-automotive.de/about-us.html
Casimir https://www.woelfel.de/en/products/seating-comfort/casimirautomotive.html
VADE https://vrcim.wsu.edu/pages/virtual-assembly/vade.html
ICIDO:Ergonomics https://virtualreality.esi-group.com
ViveTech LTD. https://vivetech.com/

## Slide 17: Important standards for Module 2-3
DIN Taschenbuch 390 Körpermaße und Körperkräfte
DIN 33408-1 Körperumrißschablonen, Teil 1: Für Sitzplätze
ISO 15534-3 Ergonomic design for the safety of machinery – Anthropometric data
EN ISO 15536-1 Ergonomics – Computer manikins and body templates – General requirements
EN ISO 15536-2 Ergonomics – Computer manikins and body templates – Part2: Verification of functions and validation of dimensions for computer manikin systems
EN ISO 14738 Safety of machinery – Anthropometric requirements for the design of workstations at machinery
EN 1005-4 Safety of machinery – Human physical performance – Part 4: Evaluation of working postures and movements in relation to machinery
DIN 33406 Arbeitsplatzmaße im Produktionsbereich - Begriffe, Arbeitsplatztypen, Arbeitsplatzmaße

## Slide 18: Important standards for Module 2-3
DIN EN ISO 3411:2009-01 Erdbaumaschinen - Körpermaße von Maschinenführern und Mindestfreiraum
DIN ISO 4130:1979-04 Straßenfahrzeuge - 3-dimensionales Bezugssystem und primäre Bezugspunkte - Definitionen
DIN EN ISO 5353:1999-03 Erdbaumaschinen sowie Traktoren und Maschinen für Land- und Forstwirtschaft - Sitzindexpunkt
DIN 5566-1:2006-09 Schienenfahrzeuge – Führerräume - Allgemeine Anforderungen
DIN 5566-2:2006-09 Schienenfahrzeuge – Führerräume - Zusatzanforderungen an Eisenbahnfahrzeuge
ISO 6549:1999-12 Straßenfahrzeuge - Methode zur Bestimmung von H- und R-(Sitzbezugs)Punkten
DIN EN 70020-1:1993-02 Straßenfahrzeuge – Kraftfahrzeugbau – Begriffe von Abmessungen
SAE J826 H-Point Machine and Design Tool Procedures and Specifications
Weitere Normen finden Sie unter https://nora.kan-praxis.de

## Slide 19: Important literature for Module 2-3
BRÜTTING, M.; BÖSER, Chr.; KNIPFER, Chr.; ELLEGAST, R. (2012): Sitzmemory am Busfahrerarbeitsplatz. IFA Report 3/2012. Hrsg.: Deutsche Gesetzliche Unfallversicherung e. V. (DGUV)
BUBB, H. (2007): Digitale Mensch-Modelle. In: K. Landau (Hg.): Lexikon der Arbeitsgestaltung. Stuttgart: Gentner und ergonomia Verlag, pp. 454–458.
BUBB, H. (2009): Menschmodelle (digital). In: Medizinisches Lexikon der beruflichen Belastungen und Gefährdungen, Definitionen – Vorkommen – Arbeitsschutz, pp. 674–677
OTTO, S. (1994): Wartbarkeitsstudie mit Hilfe von 3D-CAD-System CATIA und dem Ergonomiesystem ANTHROPOS an einem Flugzeug. Degree thesis. Hamburg: Fachhochschule Hamburg.

## Slide 20: Important literature for Module 2-3
SCHRADER, K. (2003): Entwurf und Realisierung eines Ergonomie-Mock-Ups unter Verwendung von Methoden der virtuellen Realität. Dortmund: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Publications of the Bundesanstalt für Arbeitsschutz, Article 587, also Technische Universität Braunschweig, Diss., 9/2003).
SEITZ, T. (2003): Videobasierte Messung menschlicher Bewegungen konform zum Menschmodell RAMSIS. Disseration. Munich: Technische Universität München.
STEGER, D. (2004): Motion Capture mit optisch-magnetischem Trackingsystemen in VR-Applikationen. Degree thesis. Chemnitz: Technische Universität Chemnitz.
TECHMATH AG (EDS.) (2001): RAMSIS in CATIA. Handbuch Version 3.7. Kaiserslautern.

## Slide 21: Impressum
Author: Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de https://ergonomie.kan-praxis.de