## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Part 4: Anthropometric requirements concerning workplace design/ functional dimensions
Module 2 – Learning ergonomics.

## Slide 2: The point is…
Workplace type: seated
Safety distances
Maximum and minimum
gaps
Active area
Area of reach
Body space envelope
Workplace types
© Michael Hüter
Workplace type: standing
Notes: Proper design of working areas at workplaces/on machines/on products is essential if operation is to be safe and ergonomically correct. Inadequate safety distances or openings that are dangerously large (e.g. on safety grids) may lead to accidents. Workplaces/machines/products that are not designed ergonomically and the constrained postures to which they give rise during daily work may lead to work-related complaints (particularly musculoskeletal diseases) or even occupational diseases. For this reason, areas of reach and active areas, body space envelopes, safety distances, maximum and minimum distances and various types of workplace will be considered here in greater detail.

## Slide 3: Area of reach and active area
M 25
F 20
M 80
F 72
M 154
F 138
Dimensions in cm
M 25
F 20
M 80
F 72
M 154
F 138
© Michael Hüter
Area of reach
Active area
Males 50
Females 44
Notes: Area of reach:
A space segment described by the superimposition of horizontal and vertical envelopes during movement of the extremities
Physiological reach:
Arm extended, without simultaneous movement of the shoulder and body
Distance to the centre of the hand, with the hand in the grip position
Design of inside dimensions: the shortest user must be able to reach all points
Shortest user: 5th percentile of the operator population (for both females and males: short female)
The reach is required for example:
For the location of assembly trays at an assembly workplace
For the location of switches on a control desk
For the location of touchscreens
For the location of buttons, for example in a vehicle, where the user is wearing a seatbelt and is able to reach the control panel only by extending their arm
For the location of handles for the opening of hatches, windows etc.
Active area:
Area in which functions can be performed comfortably and safely
For example: movements of the lower arm, lower leg or foot
Reference dimension: 5th percentile of the operator population
Example applications:
Reachability of pedals with the feet in the seated position
Reachability of a joystick with the arms bent
Actuation of frequently used switches and buttons
Performance of very rapid movements, primarily by the lower arms
Fast reachability of the control elements, for example switches on the steering wheel of a vehicle

## Slide 4: Determining the area of reach on a switch panel
Determining the upper and lower actuation limit
Posture: Standing upright directly in front of the panel
Operator population: F 5 to M 95 (aged 18-59)
Based upon anthropometric dimensions:
(to DIN 33402-2)
Dimensions in mm (including 30 mm footwear)
Limit downwards: M 95
Limit upwards: F5
Location of actuating elements requiring frequent use (adjusters, writing implements, switches, buttons)
Borderline permissible location of manual controls requiring infrequent actuation
M 95
F 5
M 95
F 5
 | F 5 | M 95
Downward reach | 700 | 855
Upward reach | 1870 | 2235
Notes: Assuming actuation in an upright posture, the part of a panel housing the controls is constrained downwards by the reach of the tall male and upwards by the reach of the short female.
Deeper reaching is comfortably possible for the short female, and assured for the tall male by slight bending.
Reaching above the limit of F5 is possibly only for users taller than F5, and with progressive limitation.

## Slide 5: Space envelope (space requirement, compensatory movements)
Body space envelope for the postures of lying and squatting to DIN 33402-3
Access openings for trunk and
head to EN 547-3
A
A
© Michael Hüter
Notes: Space envelope – dimensions (space requirement, compensatory movements)
Aspect of space requirement, ability to perform the task: minimum dimensions, without consideration of comfort
Design of outside dimensions: the tallest user must be accommodated in all positions
95th percentile operator population
Observance of the posture
Example applications:
Accessibility of a shaft via a ladder
Dimensioning of manholes for maintenance purposes
Accessibility for head and shoulders for test tasks
Observance of allowances: for example for clothing, protective equipment, movement, etc.
Dimensioning of operating, repair and maintenance areas on machines, in consideration of the posture

## Slide 6: Reach (safety distances) – minimum and maximum distances
Maximum distances: Inability of limbs to pass at clear widths of profile openings
Minimum distances: Safe passage of body parts of a defined user group through existing danger zones
Maximum anatomical reach
<750mm
Unfavourable
>750mm
Favourable
a
a
1 10 100mm
6
Based on Neudörfer, A. (2002)
Minimum distance for the foot: 120 mm
Minimum distance for the finger: 25 mm
see EN 349
Notes: Safety distances:
Geometrical design measures for mechanical hazards
Avoidance of accessibility/reachability of danger zones with the upper limbs (reaching around, up or over)
Consideration of anthropometric dimensions and human biomechanical characteristics (compressibility of the limbs)
EN ISO 13857
 For machinery and equipment
 For persons aged 3 or over
 e. g. safety distance for reaching up: 2700 mm (before: 2500 mm)
Maximum anatomical reach:
Arm fully extended, with full involvement of the body and simultaneous movement of the shoulder
Distance to the tip of the middle finger
Reach of the tallest person (99th percentile) + safety allowance = safety distance
Maximum distances:
Inability of limbs to pass through properly dimensioned clear widths of profile openings
Minimum distances:
Safe passage of body parts of a defined user group through existing danger zones
EN 349
Achieved by variation of geometrical conditions (e.g. distances between axles, end positions of movable parts)
The greater the profile openings, the greater the additional safety distance of the protective structure from the danger zone

## Slide 7: Basic workplace types: standing workplace
M95
F5
M95
F5
M95 Unisexmodell
F5 M50/F50
With adjustment assistance Fixed workbench height variable standing height | Standing workplace Ideal Variable workbench height | Compromise Averaged fixed workbench height Bases upon M 50/F 50
Source: Kamusella: http://ergotyping.net/index.php?title=Anthropometrie:_Arbeitsplatzgrundtypen_Buero_und_Produktion
Notes: Standing workplace
Ideal variant:
Working height adjustable, to permit adaptation to the individual user
Adjustable range dimensioned at least according to the limit percentiles of the operator population: short female to tall male
Further variant:
Design with adjustment assistance
Working height designed based upon the tallest user of the operator population
Adjustment for shorter users by means of variable platform height (e.g. stepped platform)
Application possible and advantageous only:
Where the operator stands in one place for a longer period (e.g. loading of a machine with containers etc. also located on the platform)
Where the platform is so large that no risk of tripping or falling exists
Where this height adjustment enables very short users in particular to carry out the task more favourably
Design with compromises:
Averaged working height based on P50 unisex (right picture, gray person)
Reference dimension for the working height: hand height at the site of action in the physiological hand-arm position and in consideration of the viewing distance
 The elbow height is used as a reference dimension only where the site of action (the manual point of action) is identical to the bench height
Generally, fixed working heights should be provided: these should not be selected based upon the tallest user, since this would necessitate the use of platforms (with an associated risk of tripping). Instead:
 Compromise; define average working height:
 Based upon F5/M95 or upon F95/M5 (since F95 = M50 and M5 = F50)
Supports for standing may be used: relief for the circulation and supporting apparatus (absorb up to 60% of
the body weight)
Stress can also be reduced by well-cushioned footwear and floor mats

## Slide 8: Basic workplace types: seated workplace – standing/seated workplace
M95
F5
M95
F5
M95 Unisexmodell
F5 M50/F50
Seated workplace |  | Standing/seated workplace
With adjustment assistance Fixed workbench height based on M95 Variable seat height and footrest | Ideal Variable workbench height Variable seat height | With adjustment assistance Mean fixed workbench height M50/F50 variable seat height variable footrest
Source: Kamusella: http://ergotyping.net/index.php?title=Anthropometrie:_Arbeitsplatzgrundtypen_Buero_und_Produktion
Notes: Seated workplace compromise solution:
Fixed working height based upon the tallest user of the operator population
Reference dimension for working height above seat surface level: site of manual action in consideration of favourable limb positions
At office workplaces: generally elbow height (site of manual action almost identical to desk height);
Otherwise hand height in a physiologically favourable hand-arm position in consideration of the viewing distance
 Based upon the most frequent average site of action
Shorter users raised by means of seat height adjustment
Floor contact assured by means of footrests
Use of arm rests during repetitive activity of longer duration without major movement of the arms
Optimum design of a seated workplace:
Design the working height and seat height to be variable, in consideration of the tallest and shortest members of the operator population, by means of facility for adjustment of the dimensions
Standing/seated workplace:
Working height determined as for standing workplace
Calculation of the seat height (use of raised chairs) and of further dimensions for this (standing) working height

## Slide 9: Facility for adjustment of dimensions, area of reach and active area
Example of a forestry planting plough
Problem areas: Unfavourable postures:
Lumbar spine
Leg posture
Source: Kamusella, Christiane: Ergonomie und Arbeitsgestaltung – ein Überblick. Fachtagung Ergonomie des Sitzens. 2. Deutscher Stuhlbauertag 11.06.2010 Rabenau
Notes: A forestry planting plough, attached to the rear of a towing vehicle and towed across the area to be planted, consists essentially of a frame, a ploughshare, the pressure rollers and the balance weights.
A seat for the user is fitted in a fixed position to the frame; the feet can be supported only on fixed rests; the plant box is located beside the seat
During planting of the area, the user's task is to insert plants into the soil at regular intervals
This is performed with the trunk inclined steeply forwards and with the legs in an unfavourable posture
The equipment is not adapted to tall and short users
Evaluation of the posture:
The red-green-yellow bars in the diagram represent an evaluation of the posture according to the traffic-light principle: red should be avoided, green is the preferred range
Evaluation of the spine in the example: the red bars indicate particular stress upon the lumbar spine
The length of the bars indicates the exploitation of the joint angle range. If, for example, use is made of over 75% of a joint angle range, the evaluation for the affected joint is yellow, since the comfort range of the joint is exceeded

## Slide 10: Example forestry planting plough
Design
Planter distance piece
Moveable
various lengths
Plant box
easy reach
inclined
Seat and footrests:
adjustable
Reduction of the seat height
Seat with left-hand armrest
Area of reach
Source: Kamusella, Christiane: Ergonomie und Arbeitsgestaltung – ein Überblick. Fachtagung Ergonomie des Sitzens. 2. Deutscher Stuhlbauertag 11.06.2010 Rabenau
Notes: The frame width was reduced and the seat lowered and provided with horizontal adjustment, in order to reduce the forward inclination of the user.
In addition:
Adjustable footrests
Modification of the plant box geometry
Plant box fitted at an incline
Previously, the plant interval had to be estimated.
By the addition of a planter distance piece, the plants can now be inserted at regular intervals (bottom right)

## Slide 11: Example
Workplace office:
publisher: Gesellschaft Arbeit und Ergonomie - online e.V.: https://www.ergo-online.de/ergonomie-und-gesundheit/arbeitsplatzgestaltung/ (in german)
Sewing workplace:
Source: Ellegast, R. IFA Institut für Arbeitsschutz der Deutschen Gesetzlichen Unfallversicherung, Sachgebiet Ergonomie

## Slide 12: Ergonomic design of sewing workplaces
Problem:
High proportion of musculoskeletal complaints in the sewing industry
Lack of prevention concepts, particularly for ergonomic design
Systematic analysis of stresses at sewing workplaces, and development of ergonomic sewing workplaces


Module 2 Part 4 Example: sewing workplace
12
Notes: Film startet durch klicken auf das Bild.

## Slide 13: Development of an ergonomic sewing workplace
Properties:
Quick changes possible between seated and standing activity
Wide range of adjustments to the work level
Facilities for individual adjustment of arm rests
Extension of the footroom and legroom
Freely configurable pedal position
Module 2 Part 4 Example: sewing workplace
13

## Slide 14: Development of an ergonomic sewing workplace
Consideration for:
Variance in body dimensions within the user population
Ideal field of view and ergonomic areas of reach
Facility for adjustment to different sizes of sewing products and different types of sewing machine
14
Notes: Film startet durch klicken auf das Bild.

## Slide 15: Evaluation of the new workplace in the field
Comparative measurement (old vs. new sewing workplace)
Example: Frequency distributions (box plot over the working shift) of postures with a bent back in the toy industry
Measurement number
Seated workplaces (old)
Seated workplaces (new)
Standing workplaces (new)
Back flexion angle [°]
15

## Slide 16: Guidance document for use in the field: BGI 804-2
Explicit information on the design of:
Workplace dimensions
Workplace environmental factors
Aspects of work organization
Also: illustrative approved examples of ergonomic work design
https://osha.europa.eu/fop/germany/de/topics/archiv_gpa/2007/beitraege_2007/bgi-ergonomie.pdf
(in German)
16

## Slide 17: Important literature for Module 2-4
DIN Taschenbuch 390 Körpermaße und Körperkräfte
EN ISO 14738 Safety of machinery – Anthropometric requirements for the design of workstations at machinery
EN 547-2 Safety of machinery – Human body measurements – Part 2: Principles for determining the dimensions required for access openings
EN ISO 3411 Earth-moving machinery – Physical dimensions of operators and minimum operator space envelope
EN ISO 6682 Earth moving machinery – Zones of comfort and reach for controls
DIN 5566-1 Schienenfahrzeuge – Führerräume – Teil 1: Allgemeine Anforderungen
DIN 5566-2 Schienenfahrzeuge - Führerräume – Teil 2: Zusatzanforderungen an Eisenbahnfahrzeuge
DIN 15996 Bild- und Tonbearbeitung in Film-, Video- und Rundfunkbetrieben - Grundsätze und Festlegungen für den Arbeitsplatz

## Slide 18: Important literature for Module 2-4
DIN 33402-3 Körpermaße des Menschen - Bewegungsraum bei verschiedenen Grundstellungen und Bewegungen
DIN 33406 Arbeitsplatzmaße im Produktionsbereich - Begriffe, Arbeitsplatztypen, Arbeitsplatzmaße
DIN 33408-1: Körperumrissschablonen – Teil 1: Für Sitzplätze
EN ISO 13857 Safety of machinery – Safety distances to prevent hazard zones being reached by upper and lower limbs
EN 349 Safety of machinery – Minimum gaps to avoid crushing of parts of the human body
EN ISO 13850 Safety of machinery – Emergency stop – Principles for design
VDI/VDE 3546 Blatt 1 Konstruktive Gestaltung von Prozeßleitwarten; Allgemeiner Teil
VDI/VDE 3850 Blatt 1 Gebrauchstaugliche Gestaltung von Benutzungsschnittstellen für technische Anlagen - Konzepte, Prinzipien und grundsätzliche Empfehlungen
For further standards, see KAN-Praxis – https://nora.kan-praxis.de/en

## Slide 19: Important literature for Module 2-4
BULLINGER, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
GRANDJEAN, E. (1991): Physiologische Arbeitsgestaltung: Leitfaden der Ergonomie. 4th edition, Landsberg: Ecomed.
HETTINGER, T.; WOBBE, G. (EDS.) (1993): Kompendium der Arbeitswissenschaft: Optimierungsmöglichkeiten zur Arbeitsgestaltung und Arbeitsorganisation. Ludwigshafen (Rhein): Kiehl.
INSTITUT FÜR ANGEWANDTE ARBEITSWISSENSCHAFT E.V. (Eds.) (1989): Arbeitsgestaltung in Produktion und Verwaltung. Taschenbuch für den Praktiker. Cologne: Wirtschaftsverlag Bachem.
KIRCHNER, J.-H.; BAUM E. (1990): Ergonomie für Konstrukteure und Arbeitsgestalter. Munich: Carl Hanser.
KIRCHNER, A.; KIRCHNER, J.-H.; KLIEM, M.; MÜLLER, J. M. (1990): Räumlichergonomische Gestaltung: Handbuch. 1st edition. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Publications of the Bundesanstalt für Arbeitsmedizin und Arbeitsschutz, Article 632).
LANGE, W.; WINDEL, A. (2008): Kleine ergonomische Datensammlung. Dortmund: Bundesanstalt für Arbeitsschutz und Arbeitsmedizin.

## Slide 20: Impressum
Author : Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by:
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de https://ergonomie.kan-praxis.de