## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Part 5: Types of muscle work and defining parameters for physical strengths
Module 2 – Learning ergonomics – Part 5

## Slide 2: Overview
© Michael Hüter
Dynamic and static muscle work
Defining parameters for maximum static action forces
Data sources (e.g. standards)
Notes: Besides different body dimensions, variations in physical strength between human beings must also be considered during the design of workplaces and products. In the sense of DIN 33411 (Parts 3 to 5), physical strength is the strength associated with the human body (mass/muscle/action force). Action forces in this context are the forces exerted outwardly by a part of the body generating them.
Action forces occur for example when operating forces are exerted by the finger-hand system (forces >30 N) and also when greater forces are applied by the hand-arm system with the involvement of the muscles of the upper arm and shoulder (forces >40 N).
If for example control elements (switches, levers) are to be operated very frequently, the operating forces required for this purpose must be selected such that muscle fatigue does not arise (as was for example the case with typewriter keys before the advent of the modern computer keyboard). In the case of manually guided hand tools (screwdrivers, grinding machines, etc.), repetitive work, the weight of the tools, unfavourable hand postures, etc. may also give rise to muscle stresses. Besides favourable handle design, location of the centre of gravity of the tool, the avoidance of disrupting secondary forces and the location of the point of force application, factors relating to the task and the individual are also relevant.
If for example a work object is to be lifted and set down a hundred times a day, as shown here in the image, consideration must be given to the human physical strength. Corresponding design decisions can be taken. This chapter first explains the differences between dynamic and static muscle work, defining parameters for maximum static action forces and sources of data concerning body forces (such as normative data in the form of isodynes).

## Slide 3: Terminology
Physical force: Force arising in conjunction with the human
body (mass/muscle/action force)
Action force: Physical force exerted outwardly by a part of
the body (e.g. operating forces)
Dynamic muscle work:
Alternation of muscle contraction and relaxation
The muscle acts as a pump in the circulatory system
Muscle contraction: ejection of the blood
Relaxation: refilling with blood
Blood circulation level approximately 10 to 20 times that at rest
Sugar and oxygen are supplied, waste products flushed away
Notes: Mechanical work: tasks for the generation of forces/mechanical energy
Although mechanization and automation have considerably reduced these tasks, a number of tasks nevertheless remain which require not inconsiderable energetic work.
The task of ergonomics lies not in protecting human beings against physical activity in any form, but in designing the tasks concerned such that they can be completed sustainably without injury to health. Frequently, excessive strain is not immediately subjectively perceptible, but becomes apparent only in the longer term in the form of disease and injury (such as tenosynovitis, muscle disorders and injury to the spine)
 Diseases of the affected persons and considerable costs for medical treatment and as a consequence of lost working time
Terminology:
Static action force = positioning force Human physical force acting upon a static point of force application
Dynamic action force = movement force Human physical force transferred to moving objects (propulsion, braking, manipulation and operating forces)
Action force = physical force exerted away from the body, upon the environment, by a body part (whole body, arm, leg, hand, finger, knee, foot)

## Slide 4: Terminology
Static muscle work: Sustained state of contraction
(to EN 1005-1: ≥ 4 s)
No change in length of the active muscles
Posture constant over time
Compression of the blood vessels, choking of the blood flow
No removal of waste products  muscle fatigue causes pain; joints, tendons and ligaments suffer wear
At 60% FMAX the flow of blood is prevented  rapid muscle fatigue (min, s)
Notes: Conditions for maximum positioning forces:
Maximum possible deliberate exertion by intensive muscle contraction for 2 to 6 seconds  maximum force can be exerted only for a few seconds
Defined body and limb position
Exertion in a particular direction beginning at a defined point of force application
Sufficient counterforce from the body
If force is to be generated for sustained periods or repeatedly, breaks, forces of substantially lower dimension, and a favourable selection of the point of force application (and therefore lower forces to be applied) are decisive criteria for the avoidance of muscle fatigue and excessive stress upon the muscle system

## Slide 5: Terminology
Avoidance of muscle fatigue during static exertion, by:
Temporary complete muscle relaxation  breaks
Optimization of the application of force (direction of force, location, posture)
Selection of a suitable pace of work
Notes: Conditions for maximum positioning forces:
Maximum possible deliberate exertion by intensive muscle contraction for 2 to 6 seconds  maximum force can be exerted only for a few seconds
Defined body and limb position
Exertion in a particular direction beginning at a defined point of force application
Sufficient counterforce from the body
If force is to be generated for sustained periods or repeatedly, breaks, forces of substantially lower dimension, and a favourable selection of the point of force application (and therefore lower forces to be applied) are decisive criteria for the avoidance of muscle fatigue and excessive stress upon the muscle system

## Slide 6: Different forms of stress upon the muscle
 | Rest | Dynamic work | Static work
Characteristic | - | Alternation of muscle tension and relaxation | Sustained state of contraction
Required blood supply |  |  | 
Supply of blood |  |  | 
 |  | Example: turning a crank | Example: holding a load
based on: GRANDJEAN, E. (1991): Physiologische Arbeitsgestaltung: Leitfaden der Ergonomie. 4. Auflage Landsberg: Ecomed.
Notes: Dynamic work:
Circulating blood volume 10 to 20 times higher than at rest
Sugar and oxygen are supplied, waste products flushed away
Static work:
Blood vessels compressed, no flood flow
No removal of waste products  muscle fatigue causes pain; joints, tendons and ligaments suffer wear
At 60% FMAX, the flow of blood is prevented  rapid muscle fatigue

## Slide 7: Defining parameters for maximum static action forces
Value of the force, in N
Location of the force application point relative to the body e.g. polar co-ordinates: Vertical angle ; lateral angle ; arm reach R
Direction of force Tractive force; compressive force; abduction/adduction force along the force action line
© Michael Hüter
Abduction
pressure
Adduction tension
arm reach R
Notes: The physical force is defined by the following parameters: value of the force in Newtons, location of the point of force application in relation to the body, and direction of the line of force application relative to the direction of the physical force
The maximum force is dependent upon the location of the force's point of application relative to the human body and upon the vectorial components describing it (dimension and direction)
Point of application of the force, described by polar co-ordinates:
Height angle (side view) = angle between the shoulder joint and the line linking the shoulder and the hand (in the case of arm forces)
Lateral angle (plan view) = angle between the shoulder joint and the line linking the shoulder and the hand
Relative arm reach (in %) = quotient of the distance between the middle of the shoulder and the axis of the handle and extended arm (equal to 100%)

## Slide 8: Sources of data, max. action forces – normative data
Isodynes of horizontal maximum arm traction forces of males
(DIN 33411-4)
Isodynes Lines of equal force
(level, direction of force)
in one plane
© Michael Hüter
arm reach
Notes: Description of maximum forces – e.g. in DIN 33411-4 – in the form of isodynes
Isodyne = curve linking the points of application of action forces of the same type and magnitude in the vertical plane through a reference point (e.g. the shoulder joint point) in the motional range of the extremity under consideration (e.g. the arm)
The image on the left shows an adduction force being applied vertically from +30° to -60° in the azimuth angle plane of 0°, from arm strongly bent through to arm extended.
Azimuth angle = 0°, i.e. the handle and the shoulder joint point are equidistant from the body symmetry plane.
The values constitute maximum values attained by the action forces at a duration of exertion of a few seconds, and do not include influences of fatigue.
For dimensioning of actuating forces, the maximum forces must be reduced by person-specific and task-specific factors (see Module 2-6).

## Slide 9: Example
2 points of force application in the area of reach at which the maximum action force is 160 N
50% arm reach Height angle 30°
70% arm reach Height angle -30°
© Michael Hüter
Notes: Description of maximum forces – e.g. in DIN 33411-4 – in the form of isodynes
Isodyne = curve linking the points of application of action forces of the same type and magnitude in the vertical plane through a reference point (e.g. the shoulder joint point) in the motional range of the extremity under consideration (e.g. the arm)
The image on the left shows an adduction force being applied vertically from +30° to -60° in the azimuth angle plane of 0°, from arm strongly bent through to arm extended.
Azimuth angle = 0°, i.e. the handle and the shoulder joint point are equidistant from the body symmetry plane.
The values constitute maximum values attained by the action forces at a duration of exertion of a few seconds, and do not include influences of fatigue.
For dimensioning of actuating forces, the maximum forces must be reduced by person-specific and task-specific factors (see Module 2-6).

## Slide 10: Sources of data, max. action forces – normative data
DIN 33411-5: max. static action forces
Postures: standing, crouching, kneeling
On vertical and horizontal handles at a range of heights and distances from the body
One-handed, two-handed
For a range of test subject collectives
EN 1005-3: force limits for machinery operation
Consideration for the intended user population
Professional and domestic use
85% or 99% of the (male and female) European user population (aged 20-65) are able to work without exceeding their physical limits.
Fisometr.-max. e. g.: | Pushing Pulling (standing)
Professional use | 200 N 145 N
Domestic use | 119 N 96 N
Notes: Tabelle animiert

## Slide 11: Sources of data, max. action forces – further sources (examples)
Force atlas for assembly operations:
Quasi-static forces
Of the arm-shoulder-whole body system
      Postures: standing; sitting; kneeling; in each case working upright/overhead/bent over
      6 directions of force: one-handed and two-handed
  Of the finger-hand system
      8 hand-finger gripping and action foces
  see: www.kraftatlas.de
  Cabin attendants: Maximum action forces during pushing of a trolley http://www.dguv.de/ifa/publikationen/reports-download/bia-reports-2002-bis-2004/bia-report-5-2004/index.jsp
Notes: Quasi-static: forces < 1 s cannot be evaluated by means of the force atlas for assembly operations (extremely dynamic component).
The same applies to forces substantially > 6 s (static for a long duration, very quickly leading to muscle fatigue).
Cases of force exertion with a duration of 3-4 s can be readily analysed.

## Slide 12: Important literature for Module 2-5
DIN Taschenbuch 390 Körpermaße und Körperkräfte
DIN 33411-1 Körperkräfte des Menschen – Teil 1: Begriffe, Zusammenhänge, Bestimmungsgrößen
DIN 33411-3 Körperkräfte des Menschen – Teil 3: Maximal erreichbare statische Aktionsmomente männlicher Arbeitspersonen an Handrädern
DIN 33411-4 Körperkräfte des Menschen – Teil 4: Maximale statische Aktionskräfte (Isodynen)
DIN 33411-5 Körperkräfte des Menschen – Teil 5: Maximale statische Aktionskräfte, Werte
EN 1005-3 Safety of machinery – Human physical performance – Part 3: Recommended force limits for machinery operation
For further standards, see KAN-Praxis – NoRA: Searching for standards https://nora.kan-praxis.de/en

## Slide 13: Important literature for Module 2-5
BANDERA, J. E.; KERN, P.; SOLF, J. J. (1986): Leitfaden zur Auswahl, Anordnung und Gestaltung von kraftbetonten Stellteilen. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Publications of the Bundesanstalt für Arbeitsmedizin und Arbeitsschutz, Article 494).
BANDERA, J. E.; MUNTZINGER, W.; SOLF, J. J. (1989): Auswahl und Gestaltung von ergonomisch richtigen Fußstellteilen - Vols. I and II: Systematik und Fallbeispiele. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Publications of the Bundesanstalt für Arbeitsmedizin und Arbeitsschutz, Article 590 Vol. I).
GRANDJEAN, E. (1991): Physiologische Arbeitsgestaltung: Leitfaden der Ergonomie. 4th edition, Landsberg: Ecomed.
ROHMERT, W.; HETTINGER, T. (1963): Körperkräfte im Bewegungsraum. Berlin: Beuth.
ROHMERT, W. (1967): Untersuchung über Muskelermüdung und Arbeitsgestaltung. Berlin: Beuth.
WAKULA; BERG; SCHAUB; BRUDER; GLITSCH; ELLEGAST: Der Montagespezifische Kraftatlas: BGIA-Report 3/2009, DGUV 2009

## Slide 14: Impressum
Author: Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin https://www.kan.de/en/
https://ergonomie.kan-praxis.de/en