## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Part 6: Determining of permissible physical strengths
Module 2 – Learning ergonomics – Part 6

## Slide 2: Determining of permissible physical strengths
Force percentile
Factors influencing physical strengths
© Michael Hüter
Determining of permissible
physical strengths
Notes: The maximum body forces (action forces) cannot be taken as a basis for the operation of machinery. Instead, the "maximum permissible" physical forces must be considered as a function of the future user groups and the tasks, in order not to place excessive stress upon human beings. The factors influencing physical forces and the determining of permissible physical forces will therefore now be addressed.

## Slide 3: Force percentiles
Percentile percentage ranking describing a subset of a whole One hundredth value (division of force into 100 parts)
Use of percentile physical strength values
General objective: design of the forces transmissible to controls, tools or equipment in accordance with the 5th force percentile of the user group
Notes: The force value of the 5th percentile means that only 5% of the values measured in the test subject collective for the maximum static action force lie below this limit; 95% lie above it.
In other words, where design is based upon the 5th force percentile, only 5% of this user group are weaker, and 95% of the user group are able to exert this force (based upon a test subject group that is generally of the same sex and age).
A 50th force percentile means that 50% of the measured values lie above the median, 50% below it.

## Slide 4: Percentile values of static action forces
Cases critical to safety: exertion of force in conjunction with hazardous goods or emergency escape routes (safety doors, hatches with central locking wheels)
60% of the 1st percentile FMax/female (occasional)
15% of the 1st percentile FMax/female (continuous)
For planning analyses: 15th male force percentile
for existing case analyses: 50th male force percentile
Source: Schmidtke 1989
Source: BGIA-Report 3/2009
Notes: The force value of the 5th percentile means that only 5% of the values measured in the test subject collective for the maximum static action force lie below this limit; 95% lie above it.
In other words, where design is based upon the 5th force percentile, only 5% of this user group are weaker, and 95% of the user group are able to exert this force (based upon a test subject group that is generally of the same sex and age).
A 50th force percentile means that 50% of the measured values lie above the median, 50% below it.

## Slide 5: Physical strength values, percentiled
 = +30°  = +30° arm reach: 50%
Direction of force: Abduction and adduction
Force percentile: Force value:
5th percentile: 53 N
50th percentile: 93 N
95th percentile: 142 N
Source: ROHMERT, W.; BERG, K. ; BRUDER, R. ; SCHAUB, K. (1994): Kräfteatlas: Teil 1. Datenauswertung statischer Aktionskräfte. 1. Auflage. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Schriftenreihe der Bundesanstalt für Arbeitsmedizin und Arbeitsschutz Fb. 09.004).
=30°
=30°
Static action force of arms of males:
Notes: Static action forces are stated as percentile values (force percentiles) for the arm posture shown in the image: lateral angle 30°, vertical angle 30°, arm at an angle (approximately half arm length)
5th percentile means that:
Males with low physical strength can exert a maximum of 53 N at this particular force application point and for the force direction described
95% of males have greater physical strength than this
5% of males have lower physical strength, i.e. are able to exert less than 53 N
95th percentile means that:
5% of males have an even greater physical strength than this

## Slide 6: Force percentiles
EN 1005-3:2009-01 In accordance with EN 1005-3: professional and domestic use
Force limits for machines for professional use Isometric maximum force as the 15th percentile of the force values Fisometr.-max.prof. = FmaxP15
Force limits for machines for domestic use Isometric maximum force as the 1st percentile of the force values Fisometr.-max-häuslich = FmaxP1
According to the force atlas for assembly operations:
For example for standing straight:
F-max pushing force -B
    15th force percentile: 260 N
    50th force percentile: 340 N
Notes: Differences between domestic and professional use (described in EN 1005-3 in informative annex B 3.5)
Animation of lower part of the slide

## Slide 7: Factors influencing physical strengths
Person-specific factors | Task-specific factors
Age Sex Fitness Constitution Motivation State of health | Work/break regime Work environment factors Reach conditions, single-handed/bimanual Support for the body Frequency Duration Relationship between the force and the joint angle Relationship between the dynamic force and the velocity of movement Asymmetrical trunk/leg posture, awkward postures
Notes: Influencing factors are person-specific or task-specific:
Person-specific: besides age, sex, fitness, constitution and state of health, factors such as motivation may also have an influence (motivation leads in the short term to changes in performance capacity)
Task-specific:
Extreme climatic conditions such as cold cause muscles, tendons and ligaments to harden. This in turn influences their ability to stretch and contract. Injury to the muscle or the adjoining tendons and ligaments may occur
Under unfavourable gripping conditions, such as excessively wide handles, the spreading of the fingers may cause the ligaments to shorten, in turn impairing the mobility of the finger joints and the force that they are able to exert
The highest muscle force can be exerted at the mid muscle length (i.e. is dependent upon the joint angle); joint angles describe the position and deflection of the limbs in relation to each other. Through its influence upon the muscle length, the bending angle is therefore a measure of the muscle force. Mid-ranges of the joint movements are desirable, and provide the optimum leverage. For example, the greatest arm-bending force in the elbow can be exerted at a bending angle of 90° to 120°
The muscle force is also dependent upon the speed of movement:
  Very fast movements: only low forces can be exerted
  Slow movement: high forces can be exerted
  No movement: isometric contraction (constant muscle length): the maximum forces are exerted
  Approximately a medium speed of movement is desirable: medium forces

## Slide 8: Factors influencing physical strengths - person-specific
Age
Young people 70% to 90% Fmax
At approx. 30 years of age Fmax
At 60 years of age 40% to 82% Fmax
Sex
Fmax female = 60% to 72% of Fmax male
Fitness
Max. increase in muscle force: 10% per week
Muscle loss in the event of inactivity: 30% per week
Source: Bandera u.a 1989
Source: Rührmann, Schmidtke 1992
Notes: Young and older people have lower physical strength than 30-year-olds
The greatest strengths can be measured on people aged around 30; these are therefore assigned a value of 100%
Owing to their smaller muscle cross-section, females have lower muscle strengths than males
Training of previously poorly trained muscles enables an increase in muscle strength of up to 10% per week to be attained. (The training duration can be very short, for example 1 second)
When the muscles are completely inactive (e.g. when encased in plaster-of-Paris), the muscle force loss may be as high as 30% per week (three times the gain achieved by training)
 Consideration following the re-integration of staff following a longer illness, and when new employees are taken on

## Slide 9: Factors influencing physical strengths - task-specific
Duration
Endurance limit:
The highest possible performance that can be delivered over a full working day without additional rest breaks
Exceeding of the endurance limit: rest breaks necessary
Guideline data for the endurance limit:
Static force: Findiv 10% to 15% of Fmax
Dynamic force: Findiv 30% of Fmax
Notes: The supply of blood is restricted above as little as 15% of the maximum force, owing to the resulting internal muscle pressure. As a result, the maximum possible duration of work is limited
Static holding work at a level of 100% FMax is possible for a work duration of 6 seconds
For a sustained activity, only a proportion of the maximum force should therefore be planned
Since static stresses are more critical, the endurance limit lies in this case at 10% to 15% of the maximum force. (This assures muscle strain without fatigue for a longer period)
Example: when an individual is able to exert a personal maximum force of 300 N in the -B direction, they are able to work at approximately 30 N without fatigue for the duration of a shift (theoretically; this limit may drop over a longer period owing to the motivation factor).
Task-specific: work and break regime (see diagram): 20% of the maximum force can be exerted over 90% of a contraction time if breaks account for 10% of this total time

## Slide 10: Factors influencing physical strengths - task-specific
Reduction in the event of sustained contraction
F/Fmax • 100
t in
min
% of the maximum force (for static action forces)
Source: Schmidtke 1989
15
25
50
75
100
2
4
6
8
Fatigue
Endurance limit
Notes: A force of 15% of the maximum can be applied almost continually
Conversely, muscle fatigue rapidly sets in as soon as larger proportions of the maximum force are required to be exerted
For example, 40% of the maximum force can be exerted for only 2 minutes; the muscle then requires recuperation

## Slide 11: Determining of maximum recommended physical strengths
Standardized method to EN 1005-3
    Freduced= f (speed, frequency, time)
    Freduced= Fisometr.-max* reduction factors
  The following are considered:
    Speed of movement: reduction during rapid contraction movements
    Duration of work, in hours (including comparable tasks that impose stresses upon similar tissue structures)
    Frequency of operation (min-1) for a period of operation in minutes: distinction according to static and dynamic force exertion
  Frisk assessment= f risk x Freduced frisk : risc factor
  Comparison: risk assessment force with currently planned/existing force
  Example: frisk recommended ≥0,5; frisk to be avoided >0,7
Notes: Siemens method: this is used to evaluate individual homogeneous cases of force exertion, but is not suitable for evaluating cumulative stresses in complex work processes
Method to EN 1005-3: an additional reduction in the maximum forces to allow for factors specific to the individual is not necessary, since the maximum values already apply to the European population including females, males, older persons, younger persons, etc.
European standard EN 1005-3 (Safety of machinery – Human physical performance – Recommended force limits for machinery operation) states speed, frequency and time as reduction factors.
These reduction factors take the following aspects into account:
  The maximum force decreases during rapid contraction movements
  Repetition of movements in quick succession leads to fatigue; this is influenced by the duration of the discrete activity and the frequency with which it is performed
  Muscle fatigue also occurs with increasing duration of the work
  The reduced force F-reduced (maximum recommended force) is multiplied by a risk factor to produce a risk assessment force that is assigned to a risk zone: estimation of the risk of injury and disease
  This risk assessment force is compared with the current force value
  It can form a basis for recommendations for action  changes to the design of machinery; also for instruction handbooks for machinery
Bottom two text fields animated
  Die reduzierte Kraft F-reduziert (max. empfohlene Kraft) wird mit einem Risikofaktor multipliziert und ergibt eine Risikobewertungskraft, die in Risikozonen eingestuft wird: Abschätzung des Risikos von Verletzungen und Erkrankungen
  Diese Risikobewertungskraft wird mit dem aktuellen Kraftwert verglichen
  Daraus können Handlungsempfehlungen abgeleitet werden  Veränderungen am Entwurf der Maschinen; auch für Betriebsanleitungen für Maschinen

## Slide 12: Determining of permissible forces of the hand-arm system
Factor for age and sex
Factor for fitness
Source: BULLINGER, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
Fpermissible = kA • kB • kC • kD • Fmax
According to the Siemens method and derivatives – Edition H.-J. BULLINGER (see source)
Factor for the frequency of the dynamic force exertion
Factor for the holding duration during static force exertion
Maximum force: one-handed hand-arm force, seated
Notes: In order to determine permissible force limits, a base value is assumed:
Base value: maximum action force  from tables for the Siemens method and derivatives, in this case the Bullinger version
The force values apply here to one-handed hand-arm forces without involvement of the trunk, in a seated posture
The base value is determined in consideration of the location of the force application point (see Module 2-5, posture, force direction)
The base value is used in conjunction with reduction factors to calculate a permissible force limit which takes account of the operator population and the conditions
Reduction factors:
Factors relating to the operator population (age, sex, fitness)
Factors relating to the task (distinction between cases of static and dynamic force exertion)
The Schultetus method can be used:
To check the current actuation forces, by comparison between a permissible force value calculated for the existing conditions and the force that is actually required to be exerted
For dimensioning of actuation forces in the planning phase such that all operating conditions and the particular features of the operator population are considered, and excessive stress upon the user is thus avoided
To vary the actuation force by modification of the influencing variables and therefore to determine the options for design

## Slide 13: Pulling and pushing of trolleys on airliners
Problem:
Female cabin crew complain of high physical stresses during the pulling and pushing of trolleys.
Causes:
Gradient of the cabin floor
High loading (high weight)
Half-size trolley, susceptible to tipping
Handles inconvenient or not present
Module 2-6 Example: Trolley

## Slide 14: Pushing of trolleys
Examples of extreme stress:
Lifting of the heavy trolley at the beginning of pushing
Pushing whilst leaning strongly forward
The green arrows represent the reaction forces at the trolley
Module 2-6 Example: Trolley
14
Ergonomic design of work and work equipment

## Slide 15: Pulling of trolleys
Examples of extreme stress:
Holding the trolley at a low point leads to strong spinal curvature
Stabilizing of a wobbly table by lifting
The green arrows represent the reaction forces at the trolley
Ergonomic design of work and work equipment
Module 2-6 Example: Trolley
15

## Slide 16: Pulling and pushing of trolleys on airliners
Recommendations:
The green arrows represent the reaction forces at the trolley
Technology:
More stable trolleys
Ergonomically designed handles
Behaviour:
Pushing force only in the direction of movement
Back held straight
Pulling force only towards the almost fully extended arms
Module 2-6 Example: Trolley
Ergonomic design of work and work equipment

## Slide 17: Sources used
SCHMIDTKE, H. (1989): Handbuch der Ergonomie. Munich: Carl Hanser.
BANDERA, J. E. ; MUNTZINGER, W. F. ; SOLF, J. J. (1989): Auswahl und Gestaltung von ergonomisch richtigen Fußstellteilen - Vol. I: Systematik. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft, 1989 (publications of the Bundesanstalt für Arbeitsmedizin und Arbeitsschutz, Article 590 Vol. I).
RÜHMANN, HEINZPETER ; SCHMIDTKE, HEINZ (1992): Körperkräfte des Menschen. Cologne: O. Schmidt (from the Dokumentation Arbeitswissenschaft series, Vol. 31).
WAKULA, J. BERG, K., SCHAUB, Kh., BRUDER R., GLITSCH, U., ELLEGAST, R., 2009. Der Montagespezifische Kraftatlas. BGIA-Report 3/2009

## Slide 18: Important literature for Module 2-6
DIN Taschenbuch 390 Körpermaße und Körperkräfte
DIN 33411-1 Körperkräfte des Menschen - Begriffe, Zusammenhänge, Bestimmungsgrößen
DIN 33411-3 Körperkräfte des Menschen - Maximal erreichbare statische Aktionsmomente männlicher Arbeitspersonen an Handrädern
DIN 33411-4 Körperkräfte des Menschen - Maximale statische Aktionskräfte (Isodynen)
DIN 33411-5 Körperkräfte des Menschen – Teil 5: Maximale statische Aktionskräfte, Werte
EN 1005-1 Safety of machinery – Human physical performance – Part 1: Terms and definitions
EN 1005-2 Safety of machinery – Human physical performance – Part 2: Manual handling of machinery and component parts of machinery
EN 1005-3 Safety of machinery – Human physical performance – Part 3: Recommended force limits for machinery operation
EN 1005-4 Safety of machinery – Human physical performance – Part 4: Evaluation of working postures and movements in relation to machinery
EN 1005-5 Safety of machinery – Human physical performance – Part 5: Risk assessment for repetitive handling at high frequency

## Slide 19: Important literature for Module 2-6
BULLINGER, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
BONGWALD, O.; LUTTMANN, A.; LAURIG, W. (1995): Leitfaden für die Beurteilung von Hebe- und Tragetätigkeiten. Sankt Augustin: Hauptverband der gewerblichen Berufsgenossenschaften (HVBG).
HETTINGER, T. (1981): Heben und Tragen von Lasten. Gutachten über Gewichtsgrenzen für Männer, Frauen und Jugendliche. Wuppertal: self-published.
JÄGER, M.; LUTTMANN, A. LAURIG, W. (1989): Biomechanik der Lastenmanipulation. In: Konietzko, J.; Dupuis, H. (eds.): Handbuch der Arbeitsmedizin. Landsberg: Ecomed.
JÜRGENS, W.-W.; MOHR, D.; PANGERT, R.; SCHULTZ, K.; STEINBERG, U. (1996): Handlungsanleitung zur Beurteilung der Arbeitsbedingungen beim Heben und Tragen von Lasten. Saarbrücken: Länderausschuss für Arbeitsschutz und Sicherheitstechnik (LASI). (LASI publication LV 9).
SCHMIDTKE, H. (1989): Handbuch der Ergonomie. Munich: Carl Hanser.
ROHMERT, W.; BERG, K. ; BRUDER, R. ; SCHAUB, K. (1994): Kräfteatlas: Part 1. Datenauswertung statischer Aktionskräfte. 1st edition. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Publications of the Bundesanstalt für Arbeitsmedizin und Arbeitsschutz, Article 09.004).

## Slide 20: Impressum
Author: Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de http://ergonomie.kan-praxis.de/en