## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Part 7: Stress factors and biomechanical mechanisms of action
Module 2 – Learning ergonomics

## Slide 2: Overview
Hazards to the health of the spine
Intervertebral pressure and biomechanical models
Stress factors
Stress and strain determination
© Michael Hüter
Here is my spinal disc.
Do you have any medical conditions?
*groan*
Urgent need for action…
Notes: Stress upon the spine, arising for example during the loading of machines, is associated with different load factors and mechanisms of action. These in turn prompt design scenarios, as shown here on the slide.
This section addresses:
Hazards to the health of the spine
Intervertebral pressure and associated biomechanical models
Stress factors
Stress and strain determination

## Slide 3: Hazards to the health of the spine
Pressure distribution on the vertebral bodies
Healthy intervertebral disc Injured intervertebral disc
Intervertebral disc
Vertebral body with endplate
Vertebral joint
95% of intervertebral disc injuries:
L4/L5 or L5/S1
© Michael Hüter
Cervical
spine
Thoracic
spine
Lumbar
spine
Sacral
vertebra
Notes: The spine is not a rigid rod; it consists of a chain of discrete segments
Movements must be absorbed elastically
The spine has a dynamic compensation function:
a) Physical bending: form of a spring
b) Intervertebral disc: hydraulic shock absorber
Regression of the intervertebral discs begins at the end of the growth phase
Cause: sustained compression stress, particularly in the lower lumbar spine
A lack of blood vessels in the tissue promotes wear
The majority of intervertebral disc injuries occur at the transition between the 5th lumbar vertebra and the 1st sacral vertebra
A constant posture is disadvantageous and impairs the metabolism
Increased intervertebral disc compression and muscle activity/tone, even in a seated posture
Curvature of the spine causes slackening of the anterior longitudinal ligament (the longitudinal ligaments hold the intervertebral discs in position)
The posterior longitudinal ligament is overstrained by up to 20%
Unequal compression stress upon the intervertebral discs
Nutrition of the intervertebral discs is assured by alternation in stress and relief  therefore alternation in posture
Avoid spinal curvature with simultaneous load manipulation/exertion of forces: unbalanced distribution of pressure on the intervertebral discs, overload and damage are possible
 exertion of force/manipulation of loads should therefore be performed in an upright posture if at all possible
Avoid strong extension of the trunk (bending backwards) with simultaneous high stress: this causes shear forces which are associated with a high risk
Excessive compressive forces may lead to isolated overload: more infrequent, high compressive forces present a greater risk of injury than frequent stresses at a low level
 consequently, give preference to more frequent compressive forces at a lower level

## Slide 4: Estimation of the disc load as a function of the lifted weight
Ideal equilibrium of moment, lever arms considered
Example: Load weight 10 kg L1 = 50 cm L2 = 5 cm Fload = 100 N
Fspine = 1100 N
 It thus follows that a weight of 10 kg, held approximately 50 cm in front of the body, would correspond to a vertical load of 110 kg (not including the weight of the body itself)
Notes: The spine is placed under stress by the carrying of loads and the generation of forces. The level of stress however is generally substantially greater than the load weight or the generated force. This is due to the moment effect and the necessary stabilizing forces
Examination of the forces in the spine shows the compressive forces to be made up of the load weight and the muscle forces, in addition to the body weight
The acting muscle forces can be calculated in idealized form by means of the equilibrium of moment: they correspond to the ratio of the hand-to spine and muscle-to-spine lever arm lengths multiplied by the load weight
The moment of the load × lever arm (hand-to-spine lever length) is therefore generated by a load moment of equal magnitude on the extensor muscles (lever length: length of the spinous process) of the spine
Values assumed in the example: a weight of 10 kg carried at a medium distance from the body (L1=50 cm) at an assumed muscule-to-spine distance of 5 cm
The calculated muscle forces can be imagined as a weight of (50/5) × 10 kg = 100 kg (lever principle)
The compressive forces in the spine would then equate to 10 kg + 100 kg = 110 kg carried on the head (plus the effects of the weight of the parts of the body themselves, which are not considered here)
Strong strain, even in an upright posture, if force must be exerted or loads manipulated with the arms extended forwards  lever arms should be kept as low as possible; manipulation close to the body

## Slide 5: Schematic diagram of a 2-dimensional biomechanical model
Forces and lever arms on the upper body for calculation of the moment and force at the lumbar/sacral transition
Determining the compressive force on intervertebral disc L5/S1
F1-5: Weight-forces of the body segments
Fload: Weight-force of the load
Fmuscle: Resulting muscle force
d1-5: Distances between the points of application of the weight-forces of the body segments and the centre of the intervertebral disc
dload: Distance from the load centre to the centre of the intervertebral disc
dmuscle: Distance from the point of application of the resulting muscle force to the centre of the intervertebral disc
Fpressure: Compressive force on intervertebral disc L5-S1
Source : JÄGER, M.; LUTTMANN, A. LAURIG, W. (1989): Biomechanik der Lastenmanipulation. In: Konietzko, J.; Dupuis, H. (Hrsg.): Handbuch der Arbeitsmedizin. Landsberg: Ecomed.
© Michael Hüter
F pressure
F muscle
F Load
Notes: The model shows the forces and lever arms acting on the upper body from which the moment and force on the lumbar region/sacrum are calculated
The moments are made up of partial moments
The posture thus has an essential influence upon the overall lever arm and the forces applied at L5-S1
Parameters of loading of the lumbar spine:
Forward bending moment
Compressive and shear forces at the L5-S1 lumbar/sacral transition (contact force at L5-S1 with the components of pressure and shear force)
Exertion of forward bending moments via a load held in the hands and via body parts higher than L5-S1 with lever arms dependent upon the posture
Bending moment = straightening moment  calculation of a back muscle force from this moment
Sum of load, body weight and muscle forces = contact force on L5-S1

## Slide 6: Lumbar axial compressive forces: stress limits
Biomechanical risk assessment Age-dependent risk zones (traffic-light model)
Source: Jäger, M. et. al. (2001)
Age (years) | Risk of harm |  | 
Men | Low | Possible | Probable
20 | Fd  4,8 kN | 4,8 kN < Fd < 6,0 kN | Fd  6,0 kN
30 | Fd  4,0 kN | 4,0 kN < Fd < 5,0 kN | Fd  5,0 kN
40 | Fd  3,3 kN | 3,3 kN < Fd < 4,1 kN | Fd  4,1 kN
50 | Fd  2,6 kN | 2,6 kN < Fd < 3,2 kN | Fd  3,2 kN
 60 | Fd  1,8 kN | 1,8 kN < Fd < 2,3 kN | Fd  2,3 kN
"Dortmunder" guideline values
Notes: The vertebral body/intervertebral disc complex tolerates inner stresses only within certain limits. Exceeding of these limits may cause harm to the spine
 External forces must therefore be limited
Evaluation of the biomechanical stress resistance under compressive forces on L5-S1
Reference values exist for the strength of the spine (parameters for fracture resistance)
 "Dortmunder" guideline values
Stress limits for axial compressive forces: maximum values below which a risk of overload or harm is not presented  Limit value is a function of age; on average 3,500 N (75% of females, 99% of males are able to lift a load under this force)  Since females have a smaller vertebral surface area, their stress limits are lower than those for males  Females for example reach a force of 3,200 N during handling of a load of approx. 20 kg close to the body whilst leaning forward (see diagram on next slide)
Groups of individuals at particular risk are therefore women, older persons, persons with disabilities, young people
The lower table shows a strategy for biomechanical risk assessment according to the "traffic-light" model based upon the compressive force values according to Hecktor/Schaub/Jäger
Risk of harm:
Low: green
Possible: amber
Probable: red
Compressive forces can be estimated as a function of the body posture and arm reach (see next slide) and assigned to the above risk ranges.
This enables the need for action to be recognized and design measures to be reviewed.

## Slide 7: Lumbar axial compressive forces: relationship to posture and lever arm
Compressive force at the lumbar/sacral transition as a function of arm posture and forward inclination of the trunk
Close to body Medium reach Away from body
Compressive force on L5-S1 increases with increasing:
Load mass
Arm reach
Body angle  Close to body: 60° Medium distance: 45° Away from body: 30°
Source: Hartung, E.; Dupuis, H. (1994)
Notes: Slide 3 shows an approximate calculation of 1,100 N for the holding of a load of 10 kg with the arms extended forwards and the body in an upright posture
The diagrams show the compressive force curves for the relationship between the axial lumbar compressive force and the level of the load, arm posture and forward inclination of the trunk  Left-hand diagram: handling close to the body  Middle diagram: medium lever arm  Right-hand diagram: arms extended forward
The right-hand compressive force curves show values of approximately 2,000 N for the above stress case, since the calculation is based upon a two-dimensional biomechanical model with consideration for partial moments
The compressive force is seen to rise with increasing load weight and with a greater lever arm. The influence of the trunk inclination is at its greatest at approximately 60°. At 90° the force decreases again, since the load is closer to the spine. This is true only purely mathematically, however: a risk to the spine still exists at 90°, since distribution of pressure upon the vertebral bodies and upon the intervertebral disc is uneven (see Slide 2, top-left image).
The further the load is away from the body, the sooner a maximum compressive force is reached

## Slide 8: Compressive force on L5 – S1 during vertical lifting:
Static analysis: compressive force dependent upon lifting distance (change in trunk inclination)
Same load but different duration of execution: compressive force curves approximately the same
Dynamic analysis: effect of mass inertia: strong rise in compressive forces when duration execution is shortened: pressure force peaks, very harmful
Level of stress dependent upon lifting distance and speed of execution
Slow execution without external dictation of the pace of work is better than sudden, jerky execution
 time in s
Source: Jäger u.a. (2002)
distance
distance
0 0,5 1,0 1,5 2,0 0 0,5 1,0 1,5 2,0 0 0,5 1,0
Notes: Shows the influence of the lift distance and duration of the task upon the level of the compressive force
In static analysis, the level of the compressive force is dependent primarily upon the lift distance: specifically, low lift distances generate lower compressive forces than the overcoming of greater distances. This is due in particular to the greater change in the trunk inclination (lower for 10 cm to 50 cm than for 10 cm to 140 cm)
The compressive force curves for static analysis apply to lifting processes that are executed extremely slowly, i.e. over substantially more than 2 seconds  Disregarding the effect of the mass inertia
Static analysis (broken line): at the same load but with a different duration of execution, the resulting compressive force curves are approximately the same
Corresponding curves in adjacent diagrams assume the same compressive force values; the curves are however compressed horizontally owing to the shorter time axis
The dynamic analysis is therefore displayed over the static analysis; the latter shows the characteristic without the effect of the mass inertia
Dynamic analysis (unbroken line): effect of the mass inertia considered compressive forces rise strongly when the duration of execution is shortened: pressure force peaks which may be very harmful
The level of the stress is particularly dependent upon the lift distance and the speed of execution
Right-hand diagram: when the mass inertia and shorter durations of execution take effect, the compressive force peaks are increasingly strong
Consequently: slow execution without external dictation of the pace of work is better than sudden, jerky execution (workers should determine their own pace of execution, independent of machine pace)

## Slide 9: "Mainz-Dortmunder" Dose (MDD) model
Increase in the compression stress
See also: Die Deutsche Wirbelsäulenstudie, Part 1/ 2:
https://www.dguv.de/ifa/fachinfos/ergonomie/deutsche-wirbelsaeulenstudien/index-2.jsp
In general:
3. Lifting
2. Carrying
1. Handling on
the level
One-handed handling
Lifting, one-handed
4. Lifting, two-handed
3. Carrying in front of or to the side of the body
2. Carrying on both sides of the body
1. Two-handed handling
In consideration of the lever arm, arm position, trunk bending, the trend is as follows:
See also "Mainz-Dortmunder" Dose model Source: Jäger, Luttmann 1999 Source: Hartung, Schäfer 1999
Notes: As a general rule:
Of the operations stated, lifting of a load is the least favourable, since it is associated with a strong inclination of the trunk.
One-handed manipulation is less favourable than two-handed manipulation, since it is associated with lateral inclination and with additional unbalanced compressive stress upon the intervertebral discs.
Handling of a load on the same level is the most favourable operation, since it is performed in an upright posture.
When compressive forces are estimated according to the formulae of the Mainz-Dortmunder dose model however, the sequence of stress increase (rise in compressive force) differs when a more nuanced analysis is applied to the resulting lever arms, arm positions and trunk inclinations.
With increasing load weight, one-handed load handling on the level is then seen to be less favourable than lifting, i.e. the compressive forces are greater than during lifting, owing to the unfavourable arm position and the associated lever arm  the differences are not particularly great, but in purely mathematical terms nevertheless present.
See also: Deutsche Wirbelsäulenstudie:
Epidemiological study, realistic evaluation of occupational stresses upon the spine during case management of reported cases of occupational disease (occupational disease No BK 2108)

## Slide 10: General task-related stress factors
Notes: The level of stress depends not only upon the load mass and the load criteria, but also, to a greater degree and in a complex manner, upon the conditions of execution that are determined by the nature of the task
 The geometric conditions which determine the posture and movement have an influence upon the stress, as do the ambient conditions and those associated with the technical system

## Slide 11: Guideline values for load masses as a function of influencing factors
Notes: The designer is provided with guideline values and recommendations for the design of machinery and risk assessment of it, by means of which he can plan suitable solutions on his machine at operating points.
The guideline value for the reference mass as a function of the user population applies to handling of the load close to the body and in an upright posture.
The reference mass must be reduced as a function of the influences of lifting distance and frequency.
At as few as 12 lifting operations per hour, the reference mass must be reduced to 70% of its initial value.

## Slide 12: Factors influencing determining of the limit loads
LC: Load constant, as a function of the user population
Example: children and older people: 5 kg
General population, domestic context: 10 kg
Adult working population: 25 kg
HF: Horizontal factor: horizontal distance in cm between the middle of the hand and the middle of the foot at the start of lifting
VF: Vertical factor: vertical distance in cm between the middle of the hand and the floor at the start of lifting
DF: Difference factor: difference in the load height in cm between the start and end of lifting
AF: Asymmetry factor: angle of trunk torsion (twisting of the spine), in degrees
FF: Frequency factor for frequency and duration of the lifting processes
GF: Manipulability factor
Notes: For the manual handling of loads, the physical stress can be expressed in terms of a load limit which is to be determined. Consequently, the lower the stress, the more favourable the design conditions of execution are, the higher the load weight to be handled may be (up to a mass limit related to the operator population).
The load constant (mass limit specific to the operator population) constituting the maximum permissible load weight is dependent upon the user population, and therefore upon person-specific influences:
   Different values apply for example to children and older people than to the adult working population
  Precise data can be found for example in EN 1005-2
  (Further differentiation is made in the standard. It is known for example that only 70% of the female population are capable of handling 25 kg. A distinction is therefore also drawn within the working population.)
The load constant (LC), which therefore represents a reference mass, is reached when all task-related reduction factors are 1, i.e. there is no reduction in this mass limit.
This is the case when a load which can be handled easily is moved infrequently, manually, with an upright posture, close to the body, without twisting of the trunk and with a low lift interval.
All deviations from ideal circumstances of execution lead to a reduction in the load constants.
The individual reduction factors embody influencing and design factors for a specific handling situation.

## Slide 13: Example
Fettler's workplace
Source: IFA Institut für Arbeitsschutz der
Deutschen Gesetzlichen Unfallversicherung,
Sachgebiet Ergonomie
Technical aids for manual load handling
https://www.baua.de/DE/Angebote/Publikationen/Schriftenreihe/Sonderschriften/S75.html (in german)
Checklist Ergonomic machine design
https://www.dguv.de/ifa/praxishilfen/praxishilfen-maschinenschutz/checkliste-maschinenergonomie/index.jsp (in german)

## Slide 14
Fettler's workplace
  Work in a constrained posture
  High component of manual load handling
  Poor lighting at the workplace
Problems:
To start please click on the video

## Slide 15
Fettler's workplace
Measures:
Reduction of the tasks performed in a constrained posture (for example by adjustment of the height)
Reduction of manual load-handling tasks
Improvement of lighting at the workplace
To start please click on the video

## Slide 16
Fettler's workplace
Success of the measures:
Before
After

## Slide 17: Fettler's workplace
Success of the measures:
Before
After
kg
kg

## Slide 18: Reference to sources of the images
JÄGER, M.; LUTTMANN, A.; GÖLLNER, R. (2001): Belastbarkeit der Lendenwirbelsäule beim Handhaben von Lasten – Ableitung der „Dortmunder Richtwerte“ auf der Basis der lumbalen Kompressionsfestigkeit. In: Zbl. Arbeitsmed. 51 (2001) pp. 345-372
HECKTOR, K; SCHAUB, Kh.; JÄGER, M. (2014): Biomechanische Gefährdungsbeurteilung bei Montagearbeits-plätzen. In: Zeitschrift für Arbeitswissenschaft, No. 68 (2014)
HARTUNG, E.; DUPUIS, H. (1994): Verfahren zur Bestimmung der beruflichen Belastung durch Heben und Tragen schwerer Lasten oder extreme Rumpfbeugehaltung und deren Beurteilung im Berufskrankheiten – Feststellungs-verfahren. In: die BG, No. 7 (1994), pp. 452-458.
JÄGER, M.; GÖLLNER, R.; JORDAN, C.; THEILMEIER, A.; LUTTMANN, A. (2002): Belastung der Lendenwirbelsäule beim Heben und Umsetzen von Lasten. In: Zeitschrift für Arbeitswissenschaft, No. 56 (2002), pp. 93-105.
JÄGER, M.; LUTTMANN, A. u.a. (1999): Mainz-Dortmunder Dosismodell (MDD) zur Beurteilung der Belastung der Lendenwirbelsäule durch Heben und Tragen schwerer Lasten oder durch Tätigkeiten in extremer Rumpfbeugehaltung bei Verdacht auf Berufskrankheit. Teil 1: Retrospektive Belastungsermittlung für risikobehaftete Tätigkeitsfelder. In: Arbeitsmedizin. Sozialmedizin. Umweltmedizin, 34 (1999) No. 3, pp.101-111.
HARTUNG, E.; SCHÄFER, K. u.a. (1999): Mainz-Dortmunder Dosismodell (MDD) zur Beurteilung der Belastung der Lendenwirbelsäule durch Heben und Tragen schwerer Lasten oder durch Tätigkeiten in extremer Rumpfbeugehaltung bei Verdacht auf Berufskrankheit. Teil 2: Vorschlag zur Beurteilung der arbeitstechnischen Voraussetzungen im Berufskrankheiten-Feststellungsverfahren. In: Arbeitsmedizin. Sozialmedizin. Umweltmedizin, 34 (1999) No. 3, pp.112-122.

## Slide 19: Important literature for Module 2-7
DIN Taschenbuch 390 Körpermaße und Körperkräfte
EN 1005-1 Safety of machinery – Human physical performance – Part 1: Terms and definitions
EN 1005-2 Safety of machinery – Human physical performance – Part 2: Manual handling of machinery and component parts of machinery
EN 1005-3 Safety of machinery – Human physical performance – Part 3: Recommended force limits for machinery operation
EN 1005-4 Safety of machinery – Human physical performance – Part 4: Evaluation of working postures and movements in relation to machinery
ISO 11228-2 Ergonomics – Manual handling – Part 2: Pushing and pulling
ISO 11228-3 Ergonomics – Manual handling – Part 3: Handling of low loads at high frequency
For further standards, see KAN-Praxis – NoRA: Searching for standards

## Slide 20: Important literature for Module 2-7
  BERUFSGENOSSENSCHAFTLICHES INSTITUT FÜR ARBEITSSCHUTZ (eds.) (2004): Untersuchung der Belastung von Flugbegleiterinnen und Flugbegleitern beim Schieben und Ziehen von Trolleys in Flugzeugen. Sankt Augustin. (BIA Report 5/2004).
  BERUFSGENOSSENSCHAFTLICHES INSTITUT FÜR ARBEITSSCHUTZ (eds.) (2004): Ergonomie an Näharbeitsplätzen. Sankt Augustin. (BIA Report 7/2004).
  BONGWALD, O.; LUTTMANN, A.; LAURIG, W. (1995): Leitfaden für die Beurteilung von Hebe- und Tragetätigkeiten. Sankt Augustin: Hauptverband der gewerblichen Berufsgenossenschaften (HVBG).
  ELLEGAST, R. (1998): Personengebundenes Meßsystem zur automatisierten Erfassung von Wirbelsäulenbelastungen bei beruflicher Tätigkeit. Sankt Augustin: Hauptverband der gewerblichen Berufsgenossenschaften (HVBG). (BIA-Report 5/98).
  JÄGER, M.; LUTTMANN, A. LAURIG, W. (1989): Biomechanik der Lastenmanipulation. In: Konietzko, J.; Dupuis, H. (eds.): Handbuch der Arbeitsmedizin. Landsberg: Ecomed.

## Slide 21: Impressum
Author: Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by:
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de https://ergonomie.kan-praxis.de