## Slide 1: Anthropometric and biomechanical aspects of ergonomic design Module 2: Exercise 1 Definition of design dimensions with reference to relevant body dimensions

## Slide 2: Geometric design of an ultralight glider Minimum ergonomic requirements for the fuselage geometry
For the design specification of the mid-fuselage cross-section of a single-seat ultralight glider, the minimum ergonomic requirements for the height and width of the mid-fuselage are to be derived from the relevant body dimensions of the potential operator population.
Determine the corresponding minimum height H (from the seat squab) and the minimum width W in consideration of the criteria.
H
B
Notes: Please use the pdf-file as a student handout

## Slide 3: Criteria:
Operator population:
German pilots of both sexes aged 18 and over
Posture:
semi-reclining posture, trunk inclination 40° to the vertical
Lateral allowance:
allowance for movement of 50 mm on each side of the body, allowance for clothing: 10 mm on each side
Vertical allowance: movement allowance for the head of 50 mm

## Slide 4: Definition of design dimensions with reference to relevant body dimensions
Source of the values:
DIN 33402-2

## Slide 5: a) Design dimension of the mid-fuselage height
Strategy for a solution:
Relevant body dimension:
Reference person of the operator population:
Age bracket:
Minimum mid-fuselage height =
=
Notes: Note: cos 40° precise to 3 decimal places (0.766)

## Slide 6: b) Design dimension of the mid-fuselage width
Strategy for a solution:
Relevant body dimension:
Reference person of the operator population:
Age bracket:
Minimum dimension of the mid-fuselage width =
=

## Slide 7: Definition of design dimensions with reference to relevant body dimensions
40°
Source of the values: DIN 33402-2
Accelerated (younger users)

## Slide 8: a) Design dimension of the mid-fuselage height
Strategy for a solution:
Relevant body dimension: height seated (trunk length)
Reference person of the operator population: M95 (95th percentile male)
Age bracket: 18-25 (largest body dimension: height seated)
Minimum mid-fuselage height = cos 40° × height seated + allowance
= 754 mm + 50 mm
= 804 mm
In order to accommodate tall male pilots, the height from the surface of the seat squab to the cockpit ceiling should be at least 804 mm.
Notes: Note: cos 40° precise to 3 decimal places (0.766)
In this context, the mid-fuselage height should be considered only between the surface of the seat squab and the cockpit ceiling, since the space envelope beneath the seat is determined by technical constraints.
The allowances are derived from comfort aspects; the design regulations for gliders do not specify safety distances.
The greatest dimension of the operator population for the body dimension of the "height seated" should be taken from DIN 33402-2:2007-05; the age bracket should therefore also be referred to in addition to the percentile.
Allowance for proportion types can also be discussed: tall males with a proportionally long trunk have an influence upon the mean trunk height.
Beim Körpermaß „Stammlänge“ ist das größte Maß der Nutzergruppe aus DIN 33402-2 zu suchen, daher ist neben dem Perzentil auch die Altersgruppe heranzuziehen.
Zusätzlich diskutiert werden kann die Berücksichtigung von Proportionstypen: Große Männer des Proportionstyps Sitzriese haben einen langen Körperstamm und beeinflussen die Mittelrumpfhöhe.

## Slide 9
Source of the values: DIN 33402-2
maximum breadth (older users)

## Slide 10: b) Design dimension of the mid-fuselage width
Strategy for a solution:
Relevant body dimension:
width across elbows
Reference person of the operator population:
F95 (95th percentile female)
Age bracket:
61-65 (largest body dimension: width across elbows)
Minimum dimension of the mid-fuselage width
= width across elbows + allowance
= 570 mm + 2 × 50 mm + 2 × 10 mm
= 690 mm
The minimum width for pilots inside the cockpit should be at least 690 mm.

## Slide 11: Impressum
Author: Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de/en https://ergonomie.kan-praxis.de/en