## Slide 1: Work environment factors Part 1: Overview
Module 3 - Learning ergonomics

## Slide 2: What's it about?
Definition of the work environment
Stress/strain model
Work environment factors
Emissions/exposures
Measures for optimizing the stress
© Michael Hüter
Notes: Learning targets:
the students:
are familiar with the ergonomic stress/strain model;
are familiar with the ranking of measures, and with the reasons for this ranking;
have an overview of the influences upon the work environment;
are familiar with the physical principles behind influences upon the work environment;
are familiar with the statutory and normative principles for the implementation of ergonomic requirements;
are able to identify design approaches for the limitation of stresses.

## Slide 3: Definition of the work environment
The work environment of a work system is the spatial environment, which has in particular physical and chemical influences, but also biological influences, upon human beings.
Notes: Definition of the concept of work system:
According to REFA, a work system is described by the job and the task, input, output, working person, working equipment, workpiece, and environmental influences.
Where work processes are under consideration, the work system generally refers to the workplace.
The work environment constitutes a stress within the work system.
Suitable design measures may be taken to avoid negative impacts upon human beings, and even to attain positive impacts upon motivation and performance.
In order to describe the essential impacts of the influences upon human beings at the workplace, the basic concept of the stress/strain model will be introduced below.

## Slide 4: Stress/strain model
Individual Stresses
from the:
Task
(relating to the nature of the work)
Work environment
(relating to the situation)
Stress:
Level
Duration
Composition of the individual stresses:
Simultaneous
Successive
Individual
properties,
abilities,
skills
Individual strains
upon the:
Skeletal system
Tendons/ligaments
Muscles
Heart/cardiovascular system
Respiratory system
Sensory organs
Sweat glands
Central nervous system
Skin
Strain:
Subjective and
experienced by the person
Source: ROHMERT, W.: Das Belastungs-Beanspruchungs-Konzept. Zeitschrift für Arbeitswissenschaft, 38. Jg. (1984), H.4, S.193-200.
Notes: Strains
The stress-strain concept follows a principle similar to that in technical mechanics, in which stress is the sum of the external influences (e.g. forces) upon a component. Strain is interpreted as the tensions resulting from the stress. The tensions are dependent upon the level of the stress, and also upon the material properties and geometry of the component.
Definitions of work stress/work strain can also be found in EN ISO 6385.
Human work can be ranked according to an evaluation of the strain. This ranking is broken down into four criteria, namely: reasonableness, freedom from harm, freedom from impairment, and health and personality enhancement (based on Hacker).
Refer also to EN ISO 10075: Ergonomic principles related to mental work-load

## Slide 5: Work environment factors
© Michael Hüter
Climate
Radiation
Lighting
Colour
Hazardous substances
Noise
Mechanical vibration
Notes: This slide shows the factors of the working environment which will be described below. For consideration of the occupational environmental factors of hazardous substances and radiation, co-operation is required with specialists in these fields during the planning and design of installations and machinery. These factors will not therefore be considered in detail (refer if necessary to Module 3-6).

## Slide 6: Work environment factors in the case study on a machining centre
Case study: "Drive unit manufacturing cell"
Noise (units)
Climate (fan)
Hazardous substances (coolant)
Light (interior lighting)
Radiation (electromagnetic fields caused by servo motors)
Colour (design of the controls and casing)
© Michael Hüter
Notes: Explanation of the tasks taking place in the "drive unit manufacturing cell" case study
Cast components are supplied and machined. The casing covers are cut to size on a laser cutting machine.
The motor, transmission, control elements and clamping plate are placed in the casing at the assembly workplace, and mated. Finally, the finished drive unit is tested.
Obtain feedback by asking for suggestions. Click again to call up the environmental factors.
What particular environmental factors occur at the two other workplaces?
For example: light on the sheet-metal laser cutting installation; mechanical vibration on the helical conveyor and on the power screwdriver at the assembly workplace.

## Slide 7: Example: Institute for Occupational Safety and Health of the DGUV
Notes: Work environment factors: noise, light, hazardous substances (dust), mechanical vibration, climate (heat caused when protective clothing is worn during heavy physical work)

## Slide 8: Emissions/exposures
© Michael Hüter
Emissions
Radiation
Heat
Hazardous substances
Sound
Vibrations
Radiation
Heat
Sound
Hazardous substances
Exposure
Vibration
Notes: Machinery gives rise to a range of emissions (representing environmental factors), to which which in turn human beings are exposed. The task of design is to prevent or reduce the emissions. For this specific reason, the following modules will refer only to the possible technical solutions for optimizing the stress situation.

## Slide 9: Measures for optimizing the stress
T echnical solutions
take priority over
O rganizational measures
take priority over
P ersonal protective measures
Notes: This principle is described in the Machinery Directive and therefore obligatory.

## Slide 10: Technical solutions…
… are measures taken to prevent the generation, incidence or propagation of stresses at their source. These measures include:
    Selection of the substances and materials employed
    Design solutions, or
    The technology used

## Slide 11: Example of a technical solution
Laser cutting
Punching
instead of
© Michael Hüter
Reduced mechanical vibrations
Reduced
noise
Notes: Shaping of a steel metal part with laser cutting instead of punching (Reduced noise, reduced mechanical vibrations)

## Slide 12: Organizational measures…
… are measures taken to protect affected persons against a source of stress, such as:
Organizational and spatial separation of workplaces exposed to stronger work environment factors and those generating lower exposure
Reduction in the proportion of working time during which the workers are subject to the exposures
Changes to user instructions

## Slide 13: Example of organizational measures
User instructions for the handling of cooling lubricants
Notes: Besides the information on the hazardous substances, the procedures described in Section 14 of the German Hazardous Substances Ordinance must state information on appropriate precautions and measures to be taken at the workplace by the workers in the interests of their own safety and that of other workers. In addition, information must be provided on measures to be taken by the workers and in particular by rescue crews in the event of outages, accidents and emergencies, and for their prevention.

## Slide 14: Personal protective measures…
… are measures in which the individuals concerned are protected against the consequences of environmental stresses:
By personal protective equipment (PPE), or
By further personal protective measures such as danger warnings, safety instructions and occupational medical examinations
Personal protective measures are used only when all other measures fail to deliver the desired result or their implementation is not viable.
Notes: Personal protective equipment is e.g. a helmet or gloves

## Slide 15: Personal protective measures: example
Example: hearing protection
© Michael Hüter

## Slide 16: Important literature for Module 3-1
Machinery Directive 2006/42/EC
DIN-Taschenbuch 352 Anwendung von Ergonomie-Normen bei der Gestaltung von Maschinen
DGUV Information 209-068: Ergonomische Maschinengestaltung - Checkliste und Auswertung – Deutsche Gesetzliche Unfallversicherung DGUV Berlin. 2010
DGUV Information 209-069: Ergonomische Maschinengestaltung - Informationen zur Checkliste - Deutsche Gesetzliche Unfallversicherung DGUV Berlin. 2010
German Ordinance on work places (ArbStättV), 12 August 2004, last amended by Article 4 of the ordinance of 19 July 2010
BGHM-I 101: Mensch und Arbeitsplatz in der Holz- und Metallindustrie.
Berufsgenossenschaft Holz und Metall BGHM Mainz. 2013

## Slide 17: Important literature for Module 3-1
EN ISO 6385 Ergonomic principles in the design of work systems
EN ISO 10075-1 Ergonomic principles related to mental work-load –
Part 1: General terms and definitions
EN ISO 10075-2 Ergonomic principles related to mental work-load –
Part 2: Design principles
EN ISO 10075-3 Ergonomic principles related to menal workload –
Part 3: Principles and requirements concerning methods for measuring and
assessing mental workload
EN 614-1 Safety of machinery – Ergonomic design principles – Part 1:
Terminology and general principles
EN ISO 12100 Safety of machinery – General principles for design –
Risk assessment and risk reduction

## Slide 18: Important literature for Module 3-1
Bullinger, H.-J.: Ergonomie - Produkt- und Arbeitsplatzgestaltung. Stuttgart: B.G. Teubner 1994
Debitz, U.: Die Gestaltung von Merkmalen des Arbeitssystems und ihre Auswirkungen auf Beanspruchungsprozess. Hamburg: Verlag Dr. Kovac 2005
Grandjean, E.: Physiologische Arbeitsgestaltung – Leitfaden der Ergonomie. Landsberg: ecomed Verlagsgesellschaft mbH 1991
Höhn, K. et al.: Maschinennormung und Ergonomie (Article 1074). Dortmund: Publications of the Bundesanstalt für Arbeitsschutz und Arbeitsmedizin 2006
Koether, R. et al.: Betriebsstättenplanung und Ergonomie. Munich Vienna: Carl Hanser Verlag 2001
Lange, W.; Windel, A.: Kleine ergonomische Datensammlung. Dortmund: Bundesanstalt für Arbeitsschutz und Arbeitsmedizin 2006
SCHLICK, C.; BRUDER, R.; LUCZAK, H.: Arbeitswissenschaft. Berlin Heidelberg: Springer Verlag 2010
REFA: Ausgewählte Methoden zur Prozessorientierten Arbeitsorganisation. Darmstadt: REFA, 2002
SCHMIDTKE, H.; JASTRZEBSKA-FRACZEK, I.: Ergonomie. München Wien: Carl Hanser Verlag 2013

## Slide 19: Important literature for Module 3-1
Internet sources
www.nora.kan.de/en OSH standards search facility, a service of the
Commission for Occupational Health and Safety and Standardization (KAN)
https://www.dguv.de/ifa/index-2.jsp Institute for Occupational Safety and Health (IFA) of the German Social Accident Insurance (DGUV)
www.ergo-online.de Gesellschaft Arbeit und Ergonomie - online e.V.
Comprehensive collection of data on ergonomics, OSH and organization (in german)
https://www.baua.de/EN/ German Federal Institute for Occupational Safety and Health
www.bfs.de/EN German Federal Office for Radiological Protection
www.licht.de/en Information page of the Gesellschaft für gutes Licht

## Slide 20: Impressum
Author: Dipl.-Ing. Horst Böhmer
Chemnitz
horst.boemer@iapo-online.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de/en http://ergonomie.kan-praxis.de/en