## Slide 1: Work environment factors Part 2: noise
Module 3 – Learning ergonomics.

## Slide 2: Noise Overview
Definition of sound/noise
The significance of noise at the workplace
Physical principles
Measurement/weighting of sound
The effect of noise
Limit values
Technical solutions for protection against noise
© Michael Hüter

## Slide 3: Definition of sound/noise
Sound refers to vibrations in solid, liquid and gaseous media. Sound is an emission arising in the work system when machinery is operated.
Noise is defined as a sound event which is undesired, intrusive, and damaging to the hearing. For the worker, it constitutes a form of exposure.
Avoidance of the creation of sound is a task of machinery manufacturers.
The protection of workers against harmful exposure is the task of the operator.
Notes: The definition of noise includes a subjective interpretation. By contrast, sound is a phenomenon that can be quantified objectively (cf. DIN 1320).
German Ordinance on noise and vibration protection: In the sense of this ordinance, noise is any sound which may lead to impairment of hearing ability or to some other direct or indirect threat to the health and safety of employees.

## Slide 4: The significance of noise at the workplace
Reported and recognized cases of occupational disease in Germany (excerpt), 2012
Source: Deutsche Gesetzliche Unfallversicherung (DGUV)
Occupational diseases (formally recognized disease No) | Reported | Recognized
Total | 70,566 | 15,291
Of which: Discogenic disorders of the spine (2108-2110) | 5,878 | 528
Noise-induced hearing impairment (2301) | 10,979 | 6,586
Silicosis (4101) | 1,571 | 749
Skin diseases (5101) | 24,385 | 581
Notes: Noise-induced hearing impairment is, by a wide margin, the most frequently recognized occupational disease.
Knowledge of its causes and effects and the measures for protection against it are therefore particularly important. Noise may emanate from a wide variety of sources, such as machine tools or sources of energy.
A high-noise workplace (of which there are approximately 2.5 to 3.5 million in Germany) is defined as one in which noise is perceived as being undesired, disturbing or harmful owing to its duration or intensity.
recognized occupational diseases in Germany: http://www.dguv.de/de/Zahlen-und-Fakten/BK-Geschehen/Anerkannte-BKen/index.jsp
Occupational diseases (DGUV): http://www.dguv.de/de/Zahlen-und-Fakten/BK-Geschehen/Anerkannte-BKen/index-2.jsp

## Slide 5: Physical principles
Sound frequency range
Source: Institut für Arbeitswissenschaft und Technologiemanagement der Universität Stuttgart, Skript Arbeitsumgebungsgestaltung 2003
Notes: Sound is produced by mechanical vibration in elastic materials.
A distinction is drawn between airborne, structure-borne and water-borne sound.
Airborne sound is sound waves transmitted through the air in the form of variations in pressure.
Structure-borne sound is vibration within solid bodies. Vibration of the surfaces of solid bodies in turn causes airborne sound to be radiated.
According to the frequency range, a distinction is drawn between:
Infrasound at < 16 Hz, which is not audible to human beings, since its frequency is too low; at high sound pressure levels, it can be perceived in the form of structure-borne sound as vibration
Sound in the range from 16 Hz to 20 kHz is audible to human beings
Ultrasound from 20 kHz to 1 GHz is not audible to human beings, since its frequency is too high
Hypersound at > 1 GHz is waves with only limited capability of radiation

## Slide 6: Physical principles
Sound waves are pressure waves (fluctuations in air pressure) which propagate very rapidly and generate corresponding vibrations in the eardrum.
© Michael Hüter

## Slide 7: Sound propagation routes
© Michael Hüter
Notes: Structure-borne sound
Sound transmitted through solid substances is termed structure-borne sound. This sound becomes audible when it is radiated in the form of airborne sound. Insulation against structure-borne sound reduces its transmission to remote rooms.

## Slide 8: Sound parameters
Emissions parameters | Exposure parameters
Sound power level LWA | Sound pressure level LpA
Emissions sound pressure level LpA | Sound intensity I
Peak sound pressure level LpCpeak | Daily noise exposure level LEX; 8h
Notes: The sound power (Pac) of a sound source is an acoustic quantity. It describes the acoustic energy emitted from a sound source per unit of time. It is one of the values describing the acoustic energy, and is a mechanical quantity. Its unit is the Watt (W). The associated logarithmic value is the sound power level. The sound power level describes the noise emission of a source of sound.
The emission sound pressure level is determined at the workplace associated with the sound source.
The peak sound pressure level is the maximum value over the entire duration of measurement.
The sound pressure level is the most important quantity for describing the sound at a given point.
The sound intensity is the value describing the impact of a sound power upon a surface. All sound sources are considered for this purpose.
The daily noise exposure level (formerly described as the assessment level) is the A-weighted, local or personal equivalent continuous sound pressure level.

## Slide 9: Noise exposure measurement
Measurement of the sound exposure at the worker's ear
© Michael Hüter

## Slide 10: Sound measurement/ sound weighting
© Michael Hüter
(To DIN 45630-1:1971; Physical and subjective magnitudes of sound) )
A
D
C
20
50
100
200
500
1000
2000
5000
Hz
20000
-50
-40
-30
-20
-10
0
dB
20
Sound pressure correction L
Frequency f
B
A
D
B
C,
Notes: Weighted sound levels have become established as a dimension for the sound level. In weighted sound levels, sound pressures within the highest and lowest frequency ranges receive a lower weighting, owing to the lower sensitivity to noise in these ranges.
The weighted sound level in dB(A) is now generally used, since numerous psychological tests have demonstrated that the measured sound levels represent an adequate dimension for the disturbance effect.

## Slide 11: Decibels
The decibel is a relative, logarithmic unit of measurement. Statement of acoustic values in decibels generally permits a better representation than the ratio of an actual value to a baseline value.
Sound pressure level [dB]
px = Sound pressure, in micropascals
p0 = Reference sound pressure of 20 micropascals (hearing threshold at 1 kHz)
Notes: The reference sound pressure is derived from the weakest still perceptible sound pressure in the inner ear.
1 dB is the smallest difference that the ear is capable of distinguishing. A ten-fold increase in the sound pressure corresponds to an increase in 20 in the decibel value.

## Slide 12: Addition of sound sources
Source: Bullinger, H.-J.: Ergonomie - Produkt- und Arbeitsplatzgestaltung. Stuttgart: B.G. Teubner 1994
0
1
2
3
² L
dB
0
5
10
15
(L - L )dB
1
2
1,8
Example :
L = 85 dB
L = 82 dB
L = 85 dB + 1,8 = 86,8 dB
1
2
tot
L > L
1
2
L = L + L [dB]
1
ges
Notes: Levels in decibels cannot simply be added together.
If two sound-pressure levels are identical, their combined level is 3 dB higher than one of the discrete levels.
If the difference in level between two sources is less than 10 dB, the total value is assumed to approximate the value of the more intense of the two sources.

## Slide 13: The effect of noise
IFA audio example: hearing damage and its consequences
(click on symbol)
Temporary threshold shift (TTS)
Permanent threshold shift (PTS)
Noise damage
Irreparable damage to the inner ear
Non-permanent damage to the eardrum
Acute noise damage
At explosive increases in pressure
at sound pressure levels of 140 to 200 dB
Chronic noise damage
By levels of sound pressure over longer periods of exposure
Notes: TTS (Temporary Threshold Shift)
This occurs as a result of inadequate oxygen supply, and disappears again after 12 to 14 hours (for example following a concert).
PTS (Permanent Threshold Shift)
This causes irreparable degeneration of the hair cells in the ear.
Besides the effects of sound upon the hearing, the incidence of errors during work, particularly primarily mental work, also increases as a function of the ambient sound level. (Extra-aural effects – effects of noise upon the entire organism, even at lower sound pressure levels)

## Slide 14: Effect – deterioration of hair cells
© Michael Hüter
Eardrum
Ossicle
Auditory nerve
Cochlea
Healthy hair
cells
Deterioration of the hair cells as a result of exposure to noise

## Slide 15: Effect upon the organism
Mental reactions
Dilation of the pupils
Hearing damage/mechanical damage
Release of thyroid hormones
Cardiac palpitations
Release of adrenalin
Release of hormones from the adrenal cortex
Stomach and bowel movements
Muscle responses
Vasoconstriction

## Slide 16: Limit values
Applies to daily noise (LEX, 8h) and peak sound pressure (Lpc, peak) levels
 | German Ordinance on noise and vibration (2007) | EU Directive on noise
Lower action values | 80 dB (A) 135 dB (C) | 80 dB (A) 135 dB (C)
Upper action values | 85 dB (A) 137 dB (C) | 85 dB (A) 137 dB (C)
Exposure limit values | 85 dB (A) 137 dB (C) | 87 dB (A) 140 dB (C)
Provide hearing protection
Provide instruction to employees
General occupational medical advice
Provide occupational medical examinations
Mandatory wearing of hearing protection
Signing of high-noise areas
Restricted access to high-noise areas
Noise-abatement programme
Arranging of occupational medical examinations
Records of occupational medical examinations
Notes: Der Expositionsgrenzwert wird auf einen Bezugszeitraum von 8 Stunden normiert.
The exposure limit value is standardized against a reference period of eight hours.
The exposure limit value is defined as 87 dB (in consideration of the sound-reflection effect of the worker's personal hearing protector); the action values are defined by the EU directive as 80 dB (lower action value) and 85 dB (upper action value). National exposure limit values may be even stricter.
See also:
http://www.gesetze-im-internet.de/l_rmvibrationsarbschv/
http://www.gaa.baden-wuerttemberg.de/servlet/is/16050/2_1_17.pdf

## Slide 17: Limit values
© Michael Hüter
EN ISO 11690-1 Recommended practice for the design of low-noise workplaces containing machinery
The following target values should not be exceeded:
80 dB (A) Industrial workplaces
55 dB (A) Routine office work
  45 dB (A) Tasks requiring particular concentration
Notes: Automation in production causes changes in the content of work: tasks increasingly concern monitoring and control. The limit values in the German Ordinance on Noise and Vibration appear inadequate in this context. The noise levels at the workplaces must be evaluated in consideration of the tasks performed. For further information, refer to the ergonomic findings of the BAuA on screen work – noise abatement in production (AWE 125)

## Slide 18: Limit values
VDI Guideline 2058 Part 3 (assessment of noise in the working area with regard to specific operations)
The following assessment levels should not be exceeded:
70 dB (A) During simple or largely
automated office tasks and
comparable tasks
55 dB (A) During primarily mental
tasks; during particularly
challenging mental tasks: 30
to 40 dB (A)
© Michael Hüter
Notes: Automation in production causes changes in the content of work: tasks increasingly concern monitoring and control. The limit values in the German Ordinance on Noise and Vibration appear inadequate in this context. The noise levels at the workplaces must be evaluated in consideration of the tasks performed. For further information, refer to the ergonomic findings of the BAuA on screen work – noise abatement in production (AWE 125)

## Slide 19: Limit values
Source: BAuA/DGUV, training documentation for OSH professionals, 2006

## Slide 20: Technical solutions for protection against noise
Design measures
Reduction of sound emissions by reduction of the excitation forces and velocities and by design measures for the elimination of resonances
Avoidance of impulsive noise by the observance of maximum drop heights
Replacement of noisy machine components (e.g. electric drive rather than pneumatic)
Influencing of the forces giving rise to sound (e.g. changes to the frequency of a rotating part)
Avoidance of the potential for absorption of structure-borne noise
(damping of structure-borne noise, grey cast iron in place of steel)
Screening or encapsulation of parts of machinery emitting noise
Technological measures
Selection of low-noise work methods
Concentration of high-noise work equipment in working areas, and creation of low-noise areas
Quelle Lehder, G; Skiba, R.: Taschenbuch Arbeitssicherheit. Berlin: Erich Schmidt Verlag 2005
Notes: Measures for the avoidance of noise emissions
A distinction is drawn in technical noise abatement measures between
absorption and
reflection of airborne and structure-borne sound respectively.
Sound-absorbent lining of rooms influences only the reflected sound.

## Slide 21: Example of a technical solution for protection against noise
© Michael Hüter
Containment (damping of airborne noise) including insulation against structure-borne noise
Notes: Measures for the avoidance of noise emissions
A distinction is drawn in technical noise abatement measures between
absorption and
reflection of airborne and structure-borne sound respectively.
Sound-absorbent lining of rooms influences only the reflected sound.

## Slide 22: Example of a technical solution for protection against noise
© Michael Hüter
Noise-absorbent ceiling panelling

## Slide 23: Examples
© Michael Hüter
Noise abatement in concrete element manufacturing
Noise abatement on a circular saw

## Slide 24: Noise abatement in the manufacture of prefabricated concrete elements
Problem: the use of unbalance-type vibration generators (vibrating at approximately 50 to 100 Hz) to compact concrete generates strong vibration in the steel formwork.
Sound pressure levels reach 100-120 dB(A).
© Michael Hüter
Module-3-2 example:concrete funnel
24
Notes: A shop may contain up to 10 tables of this kind

## Slide 25: Noise abatement in the manufacture of prefabricated concrete elements
Solution: new compaction principle – compaction by agitation employing horizontal movement
© Michael Hüter
Module-3-2 example:concrete funnel
25
Notes: Past technologies all employed vertical vibration.
New concept: vibration and noise can be substantially reduced by means of horizontal vibration.

## Slide 26: Noise abatement in the manufacture of prefabricated concrete elements
Schematic diagram of a vibratory compactor
Concrete
Formwork
Vibrating
frame
Ground
Mounting
Unbalanced mass
Drive
© Michael Hüter
Mounting
Unbalanced mass vibrator
Module-3-2 example:concrete funnel
26

## Slide 27: Noise abatement achieved during manufacture of prefabricated concrete elements
68 dB(A)
107 dB(A)
Module-3-2 example:concrete funnel
27
Notes: A reduction in the sound pressure level has clearly been achieved; the noise is now in the order of that caused by speech.

## Slide 28: Noise abatement on circular saws
High workplace noise exposure during the sawing of:
- Wood L > 85 dB(A)
- Squared timber L > 90 dB(A)
- Plastic L > 95 dB(A)
- Metal L > 95 dB(A)
Problem:
Levels of 85 dB(A) and higher present a risk of hearing damage
© Michael Hüter
Module-3-2 example: circular saw
28

## Slide 29: Noise abatement on circular saws
Measure: Use of low-noise saw blades
© Michael Hüter
Sandwich saw blade with damping film
Module-3-2 example: circular saw
29

## Slide 30: Noise abatement on circular saws
Measure: Use of low-noise saw blades
Saw blade with laser incisions
© Michael Hüter
Module-3-2 example: circular saw
30

## Slide 31: Noise abatement on circular saws
Successful noise abatement
Sound spectra during the sawing of wood
Reduction in the A-level | 
Wood | Up to 12 dB(A)
Plastic | Up to 11 dB(A)
Aluminium | Up to 6 dB(A)
Module-3-2 example: circular saw
31

## Slide 32
© Michael Hüter

## Slide 33: Important literature for Module 3-2 (in German)
Lärm- und Vibrations-Arbeitsschutzverordnung, 19.Juli 2010
Arbeitsstättenverordnung – ArbStättV vom 12.08.2004, zuletzt geändert durch Artikel 4 der Verordnung vom 19.07.2010
Arbeitswissenschaftliche Erkenntnisse Nr. 125: Bildschirmarbeit - Lärmminderung in der Produktion, Hrsg.: Bundesanstalt für Arbeitsschutz und Arbeitsmedizin, Dortmund, 2003
Normenausschuss Akustik, Lärmminderung und Schwingungstechnik (NALS) im DIN und VDI www.nals.din.de
DIN-Taschenbuch 315/1 Messung der Geräuschemission von Maschinen - Bestimmung des Schallleistungspegels
DIN-Taschenbuch 315/2 Messung der Geräuschemission von Maschinen - Bestimmung des Emissions-Schalldruckpegels, Anwendung von Geräuschemissionswerten

## Slide 34: Important literature for Module 3-2
  DGUV Information 209-023: Lärm am Arbeitsplatz in der Metallindustrie. 2013
DIN 1320 Akustik - Begriffe
EN ISO 11690-1 Acoustics – Recommended practice for the design of low-noise workplaces containing machinery – Part 1: Noise control strategies
EN ISO 11690-2 Acoustics – Recommended practice for the design of low-noise workplaces containing machinery – Part 2: Noise control measures
VDI 2058 Blatt 3 Beurteilung von Lärm am Arbeitsplatz unter Berücksichtigung unterschiedlicher Tätigkeiten
DIN 45630-1 Grundlagen der Schallmessung; Physikalische und subjektive Größen von Schall

## Slide 35: Important literature for Module 3-2
  DIN 45645-2 Ermittlung von Beurteilungspegeln aus Messungen – Teil 2: Geräuschimmissionen am Arbeitsplatz
  VDI 2720 Schallschutz durch Abschirmung in Räumen und im Nahfeld
  VDI 3720 Blatt 2 Lärmarm Konstruieren, Beispielsammlung
  DIN EN ISO 11689 Acoustics – Procedure for the comparison of noise emission data for machinery and equipment
  EN ISO 3740 Acoustics – Determination of sound power levels of noise sources – Guidelines for the use of basic standards
For further standards, see KAN-Praxis – NoRA: Searching for standards

## Slide 36: Practical aids
Software tools from the Institute for Occupational Safety and Health of the DGUV (IFA)
https://www.dguv.de/ifa/fachinfos/laerm/softwarehilfen/index-2.jsp
Calculation of the noise exposure level
Software for the selection of hearing protection
ADM noise exposure calculator etc.
Noise calculator of the Institute of Occupational Health, Safety and Ergonomics (ASER) (in German)
www.institut-aser.de/out.php?idart=273

## Slide 37: About the ergonomics tuition modules
Author: Dip.-Ing. Horst Böhmer Chemnitz
E-Mail: horst.boehmer@iapo-online.de
Initiated and funded by:
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de http://ergonomie.kan-praxis.de