## Slide 1: Work environment factors Part 2: Mechanical vibration
Modul 3 – Learning ergonomics .

## Slide 2: Overview
© Michael Hüter
Terminology
Classification according to effect
Classification according to vibration type
Characteristics
Effect of vibration
Damage caused by vibration
Limit values
Technical solutions for protection against vibration

## Slide 3: Terminology
Mechanical vibration is caused (emitted) above all during the use of mechanical tools and vehicles.
Vibration is frequently coupled with noise. This is due to vibration and noise frequently sharing the same physical causes, such as unbalanced mass forces, shocks, and the interaction between workpiece and tool.
Notes: Vibration denotes both the emission from a machine, and the perception of it in the form of the worker's exposure. The perception of vibration in the human body is part of human haptic perception.

## Slide 4: Classification according to effect
Emissions caused by
Transport machinery
Earthmoving machinery
Trains
Ships
Aircraft
Hand-operated machines
Percussive drilling machines
Chainsaws
Sickle-bar mowers
Pneumatic drills
Stationary machines
Presses
Motors/ generators
Turbines
Installations
Notes: A distinction is drawn between:
1. mechanical vibration which endangers or could endanger the health and safety of the workers when transmitted to the human hand-arm system (hand-arm vibration), particularly causing injury to the bones or joints, circulatory disorders or neurological disorders; and
2. mechanical vibration which endangers or could endanger the health and safety of workers when transmitted to the entire body (whole-body vibration), particularly causing back pain and spinal injury.
Whole-body vibration may occur in a standing, sitting or lying posture.
Hand-arm vibration occurs in conjunction with a gripping action.

## Slide 5
Whole-body vibration
…lead to exposure
Hand-arm vibration
© Michael Hüter
Notes: A distinction is drawn between:
1. mechanical vibration which endangers or could endanger the health and safety of the workers when transmitted to the human hand-arm system (hand-arm vibration), particularly causing injury to the bones or joints, circulatory disorders or neurological disorders; and
2. mechanical vibration which endangers or could endanger the health and safety of workers when transmitted to the entire body (whole-body vibration), particularly causing back pain and spinal injury.
Whole-body vibration may occur in a standing, sitting or lying posture.
Hand-arm vibration occurs in conjunction with a gripping action.

## Slide 6: Classification according to vibration type
© Michael Hüter
Periodic vibration
e.g. motors, generators, presses

## Slide 7: Classification according to vibration type
© Michael Hüter
Stochastic vibration
e.g. vehicles
Notes: A distinction is drawn between:
1. mechanical vibration which endangers or could endanger the health and safety of the workers when transmitted to the human hand-arm system (hand-arm vibration), particularly causing injury to the bones or joints, circulatory disorders or neurological disorders; and
2. mechanical vibration which endangers or could endanger the health and safety of workers when transmitted to the entire body (whole-body vibration), particularly causing back pain and spinal injury.
Whole-body vibration may occur in a standing, sitting or lying posture.
Hand-arm vibration occurs in conjunction with a gripping action.

## Slide 8: Examples of vibration emissions
Spiral conveyor
(the emitted vibration acts
upon the entire body)
© Michael Hüter

## Slide 9: Examples of vibration emissions
Rotary hammer
(causes hand-arm vibration)
© Michael Hüter

## Slide 10: Characteristics
© Michael Hüter
Variables influencing the vibrational acceleration
Frequency-weighted acceleration (whole-body vibration)
Vibration total value (hand-arm vibration)
Frequency of the vibration
Vibration type
(whole-body vibration, hand-arm vibration)
Direction of vibration
(in accordance with the system of co-ordinates in relation to the body)
Acceleration amplitude (intensity) of the vibration
Notes: WBV: whole-body vibration
HAV: hand-arm vibration

## Slide 11: System of co-ordinates for vibration
© Michael Hüter
Physiological system of
co-ordinates for vibration
(in accordance with VDI Guideline 2057)

## Slide 12: System of co-ordinates for vibration
© Michael Hüter
Handle position
Flat rest for palm of hand

## Slide 13: Impact upon the human being
The impact of vibration is dependent upon its amplitude and frequency.
Low-frequency vibration in particular has a harmful effect upon human organ systems, since their resonant frequencies lie within this range.
Vibration of high amplitude and low frequency causes damage above all to the locomotor apparatus.
Vibration at high frequencies (for example on hand-operated machines) may lead to circulatory disturbances in the fingers.
In addition, vibration impairs reaction and dexterity, and can therefore lead to an increased accident hazard.
Notes: Sources of hand-arm vibration are of major significance in the working environment. Excessive exposure may lead to circulatory disorders in the fingers and to neurological and motor function disorders in the hand and arm.

## Slide 14: Resonant frequencies of the human body
Part of the body
Posture
Frequency range (Hz)
Whole body
Lying
1-2
Spine
Sitting
3-6
Stomach
Sitting
4-7
Stomach
Lying
4-8
Thorax
Sitting
4-6
Thorax
Lying
6-12
Hand-arm system
Forearm horizontal
8-20
Eyeball
Head upright
20-25
Cranial bone
Lying
50-70
Notes: Resonance means that the excitation frequency is identical to the natural frequency of the body or part of the body. For example, if the hand-arm system is excitated at 10-20 Hz, it resonates, since its natural frequency lies within this frequency range. Vibrations within the resonance range exert particularly strong mechanical stress upon the human body.

## Slide 15: Reaction to strong vibration
Source: Schnauber, H.; Herterich, J.: Auswirkung mechanischer Schwingungen auf den Menschen: Haufe Verlag 1989
Dyspnea (shortness of breath)
Difficulty breathing
Forced expiration
Pain in the thorax
Voluntary muscle contraction
Jaw resonance
Pain in the lower abdomen
Muscle tension
Backache
Headache
Throat complaints
Influence upon speech
Rectal irritation
Bladder irritation
General feeling of unease
Moderate complaints
Serious complaints

## Slide 16: Damage
Vascular disorders Disorders caused by temporary circulatory disturbances during exposure to hand-harm vibration, e.g. formally recognized occupational disease (BK) 2104, vibration white finger | Neurological disorders Tingling and numbness in the fingers, caused for example by crushing of nerves as in carpal tunnel syndrome
Disorders of the skeletal system Degenerative changes in bones and joints of the hand-arm system caused by shocks, e.g. formally recognized occupational disease (BK) 2103 | Muscular disorders Muscular asthenia, pain in the hands and arms caused by mechanical injury or damage to nerves
To EN ISO 5349-1
Notes: Further formally recognized occupational diseases caused by exposure to vibration:
BK 2107 – Avulsion fractures on vertebral processes
BK 2110 – Discogenic diseases of the lumbar part of the spine caused by exposure over many
years to primarily vertical whole-body vibration in a seated position

## Slide 17: Example of vibration white finger
Raynaud's syndrome = "vibration white finger"
© Michael Hüter
Notes: Chronic exposure to hand-arm vibration may cause permanent changes to bones and joints (BK 2103) and circulatory disorders in the hands (BK 2104). Raynaud's syndrome is a disorder of the blood vessels, characterized by spasmodic discolouration of the hands or feet.

## Slide 18
© Michael Hüter
I think I should see the doctor after all…

## Slide 19: Limit values
 | German Ordinance on noise and vibration protection
Action values HAV WBV | 2,5 m/s² 0,5 m/s²
Exposure limits HAV WBV | 5,0 m/s² z-axis 0,8 m/s² x-y-axis 1,15 m/s²
Take immediate measures and prevent the values from being exceeded
Organize regular occupational medical examinations
Inform workers and provide instruction on the hazards
Draw up and implement a vibration abatement programme
Offer occupational medical examinations to the workers
Notes: The exposure limit is standardized against a reference duration of eight hours (daily exposure).
The limit values are determined by measurements in accordance with EN ISO 5349 and with VDI 2057-1 and 2.

## Slide 20: Measurement of vibration
Measurement of hand-arm-vibration
© Michael Hüter

## Slide 21: Measurement of vibration
Measurement of hand-arm-vibration
© Michael Hüter

## Slide 22: Technical solutions for protection against vibration
Rotating instead of oscillating machine components
Belt drives instead of chain drives
Drilling instead of punching or hammer forging
Casting instead of forging
Pressing instead of impact forming
Electric drive instead of internal combustion engine
Optimum speeds
Avoid unbalances in rotating machine parts
Additional masses for reduction of the normal frequencies
Achieve low production tolerances

## Slide 23: Example of a technical solution for protection against vibration
Insulation close to the source
© Michael Hüter
Insulation remote from the source
Principle of insulation close to the source
Insulation of the vibration exciter
Principle of insulation remote from the source
Screening of the workplace to be protected

## Slide 24: Example of a technical solution for protection against vibration
© Michael Hüter
Technical solution
Involving special vibration-damping design of the handle and support against the reaction moment
Impact screwdriver

## Slide 25: Examples: Institute for Occupational Safety and Health of the DGUV
© Michael Hüter
Hand-operated machines
Fork-lift truck

## Slide 26: Health hazard presented by vibration
26

## Slide 27: Health hazard presented by vibration
Problem:
Strong exposure of the hand-arm system to vibration during work with paving breakers
The action value is exceeded after only between 3 and 43 minutes of exposure.
The exposure limit value is exceeded after between 13 minutes and 2 hours 50 minutes
27

## Slide 28: Technical protection against vibration
Solution
Decoupling of the impact mechanism from the housing of the device
Decoupling of the handles
Pneumatic
Steel springs
Rubber elements
Elastic mountings
28

## Slide 29: Technical protection against vibration
Result:
Substantially longer durations of use before the exposure limit value is exceeded
(tmax.> 8 h - 3 h)
(tmax.= 2,8 h - 13 min.)
29

## Slide 30: Health hazard presented by vibration
Problem:
Strong exposure of the hand-arm system to vibration during work with pneumatic grinding machines
The action value is exceeded after only approximately one hour of exposure.
The exposure limit value is exceeded after approximately 3.5 hours
30

## Slide 31: Technical protection against vibration
Solution :
Vibration attenuation by means of an autobalancing system
Schematic representation of the mode of operation to VDI 3831
31

## Slide 32: Technical protection against vibration
Result :
Substantially longer durations of use before the exposure limit value is exceeded
(tmax.> 8 h )
(tmax.= 3,5 h )
32

## Slide 33: Vibration abatement on fork-lift trucks
Problem: fork-lift truck drivers complain of pain in the region of the lumbar and thoracic spine during travel over ramps
33
Notes: The findings of the project were exploited for use in a European standard for fork-lift trucks (testing of seats for use in fork-lift trucks, termed "industrial trucks" in the standard).

## Slide 34: Vibration abatement on fork-lift trucks
Activities:
Testing of seats with a larger vibration amplitude, in the first instance in the laboratory; preliminary selection of two seats
Installation in the plant, measurement of the exposure, final selection by the employees
Results:
A 10% improvement in the vibration damping of the selected seats increases in operation to 20-30% (owing to driving style)
No bottoming at the ends of the spring travel
34
Notes: Fork-lift trucks are frequently fitted with unsprung seats. Over many years of occupational use, they may cause discogenic disorders of the lumbar spine. Measurement of the vibration exposure during various different uses of the fork-lift truck, as a function of the truck type, rated carrying capacity, tyre fitment and driver's seat.

## Slide 35: Important literature for Module 3-3
Lärm- und Vibrations-Arbeitsschutzverordnung, 19.Juli 2010
Vibrationsrichtlinie 2002/44/EG vom 25.06.2002
Normenausschuss Akustik, Lärmminderung und Schwingungstechnik (NALS) im DIN und VDI www.nals.din.de
http://www.nora.kan-praxis.de (OSH standards search)
VDI 2057 Blatt 1 Einwirkungen mechanischer Schwingungen auf den Menschen - Ganzkörperschwingungen
VDI 2057 Blatt 2 Einwirkungen mechanischer Schwingungen auf den Menschen - Hand-Arm-Schwingungen
VDI 2057 Blatt 3 Einwirkungen mechanischer Schwingungen auf den Menschen - Ganzkörperschwingungen an Arbeitsplätzen in Gebäuden
VDI 3831 Schutzmaßnahmen gegen die Einwirkung mechanischer Schwingungen auf den Menschen

## Slide 36: Important literature for Module 3-3
EN ISO 8041 Human response to vibration – Measuring instrumentation
EN ISO 14253 Mechanical vibration – Measurement and calculation of occupational exposure to whole-body vibration with reference to health
VDI 3831 Schutzmaßnahmen gegen die Einwirkung mechanischer Schwingungen auf den Menschen
EN ISO 8041 Human response to vibration – Measuring instrumentation
EN ISO 14253 Mechanical vibration – Measurement and calculation of occupational exposure to whole-body vibration with reference to health

## Slide 37: Important literature for Module 3-3
EN ISO 5349-1 Mechanical vibration – Measurement and evaluation of human exposure to hand-transmitted vibration – Part 1: General requirements
EN ISO 5349-2 Mechanical vibrations - Measurement and evaluation of human exposure to hand-transmitted vibration - Part 2: Practical guidance for measurement at the workplace
BGIA Report 6/2006 – Vibrationseinwirkung an Arbeitsplätzen – Kennwerte der Hand-Arm und Ganzkörper-Schwingungsbelastung: Sankt Augustin, Hauptverband der Berufsgenossenschaften 2006
CEN Report CR 12349 Mechanical vibration – Guide to the health effects of vibration upon the human body: Berlin, Beuth 1996
For further standards, see KAN-Praxis – NoRA: Searching for standards

## Slide 38: Important literature for Module 3-3
Dresig, H.: Schwingungen und mechanische Antriebssysteme: Berlin Heidelberg, Springer Verlag 2006
Kaulbars, U.: Messung, Bewertung und Beurteilung der Hand-Arm-Vibrationsbelastung an Arbeitsplätzen. In: IFA-Handbuch Sicherheit und Gesundheitsschutz am Arbeitsplatz. Hrsg.: Deutsche Gesetzliche Unfallversicherung (DGUV). 2. Auflage. Erich Schmidt Verlag, Berlin 2003 - Loseblatt-Ausgabe https://www.ifa-handbuchdigital.de/
Riedel, S.; Kinne, J.: Prüfung von Schwingungsisolierten Fahrzeugsitzen mit mechanischen Mensch-Modellen - Laborversuche: Dortmund, GfA-Press 2002
Schnauber, H.; Herterich, J.: Auswirkung mechanischer Schwingungen auf den Menschen: Haufe Verlag 1989

## Slide 39: Impressum
Autor: Dipl.-Ing. Horst Böhmer
Chemnitz
horst.boemer@iapo-online.de
initiiert und finanziert durch
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de http://ergonomie.kan-praxis.de