## Slide 1: Work environment factors Part 3: Lighting colour
Module 3 – Learning ergonomics.

## Slide 2: Overview
© Michael Hüter
Significance of light
Physical principles
Measurement of illumination
Definition of contrast
Effect of light
Effect of colour
Lighting design
Design examples

## Slide 3: Significance of light
The eye
is the most important organ for the acquisition of information from the ! environment.
It receives over 80% of all stimuli.
In order to be seen, objects must either be luminous or must reflect light. (Based upon Luczak, 1993)
Besides its direct influence upon the visual faculty, light also has an influence upon the vegetative nervous system and upon many of the body's vital functions. Light controls the body's hormonal balance and the body clock. (Based upon Fisch, 2000)
Notes: Light may however be the root cause of harmful effects.
The UV and IR radiation (the components of light not visible to the human eye) are the reason. If adequate protective measures are not taken, these components can damage the cornea and conjunctiva of the eyes, and of course the rest of the skin.

## Slide 4: Significance of light
© Michael Hüter
eye
body clock
nerves
hormonal balance

## Slide 5: Physical principles
Visible radiation at wavelengths of between 380 nm and 730 nm
10
10
10
10
10
10
10
10
10
10
10
8
6
4
2
0
-2
-4
-6
-8
-10
-12
10
10
10
10
10
10
10
10
10
10
Cosmic radiation
Ultraviolet radiation
X-ray radiation
Infrared radiation
Ultra-high-frequency radiation
Very high-frequency radiation
High-frequency radiation
Medium-wave radiation
Long-wave radiation
(Electric) alternating current
Gamma rays
Wavelength
Frequency
[m]
[Hertz]
1 nm
1
µ
1 mm
1 m
1 km
Light
nm
700
600
550
500
450
400
2
4
6
8
10
12
14
16
18
20
Violet
Blue
Green
Yellow
Orange
Red

## Slide 6: Light-related units
© Michael Hüter
F
Lumen (lm)
Steradiant (sr)
Candela (cd)
Based upon Laurig 1992 (see also DIN EN 12464-1:2011)
Luminous flux
Solid angle
Luminous intensity
Surface area
Luminance
Notes: Luminous flux
Total quantity of light radiated by a light source
Luminous intensity
The luminous flux radiated in a defined solid angle in a defined direction
Luminance
Luminous intensity per square metre of the apparent surface of the radiator (this may be either a light source
or a reflecting surface)

## Slide 7: Light-related units
© Michael Hüter
F
Lumen (lm)
Illumination
Luminous flux
Solid angle
Surface area
Notes: Illuminance
Luminous flux generated per square metre of the illuminated area

## Slide 8: Light-related units
© Michael Hüter
Surface area A
Reflectivity
Luminance L =
Illuminance E
(ratio of the total luminous flux reflected back to the incident luminous flux)
Distance r
• E • r
A
r
Notes: The degrees of absorption and transmission can be calculated on the same principle as the degree of reflection.

## Slide 9: Measurement of illuminance
© Michael Hüter
Illuminance
meter

## Slide 10: Measurement and luminance
© Michael Hüter
Luminance meter
Notes: Illuminance
Luminous flux generated per square metre of the illuminated area

## Slide 11: Definition of contrast Contrast is a difference in the luminance of two adjacent areas.
A viewed object can be
recognized only when it exhibits
a minimum contrast to its
environment.
Contrast may take the form of
brightness contrast, colour contrast
or combined contrast.
© Michael Hüter
Notes: The contrast in the centre of the field of view should have a ratio of 1:3.
At the centre and edges of the field of view, the contrast must not exceed a ratio of 1:10.
Continual exposure to a ratio of 1:40 is harmful to the health.

## Slide 12: Definition of contrast
© Michael Hüter
Excessive contrast causes glare.
Notes: The contrast in the centre of the field of view should have a ratio of 1:3.
At the centre and edges of the field of view, the contrast must not exceed a ratio of 1:10.
Continual exposure to a ratio of 1:40 is harmful to the health.

## Slide 13: Effect of light
Demonstrated effect: The error rate falls with rising illumination as a function of the degree of difficulty of the work
Source: Gesellschaft für gutes Licht: Lichtforum issue 39: www.licht.de
Error rate
Illuminance in lux
Drilling
Insulation stripping
Punching
Cutting to size
Sawing
Notes: Further aspects for consideration during the assessment of adequate illuminance in work systems are the age of the employees, and shift work. Older employees require higher illuminance in order to attain vision comparable to that of their younger counterparts. More light must be provided during night shifts in order to reduce the release of melatonin, a hormone which controls the circadian rhythm and leads to fatigue.

## Slide 14: Negative effects - Visible light
Poor lighting design can result in glare, thereby impacting negatively upon recognizability at the workplace.
Poor lighting also increases the accident risk, since it induces fatigue and impairs the ability to see.
A particular hazard is that presented by laser radiation: the intense focusing of the light may cause damage to the retina.
Notes: Laser radiation may contain radiation from ultraviolet (180 nm) through visible light to infrared (up to 1 mm).
Lasers are classified according to EN 60825-1 „Safety of laser products – Equipment classification and requirements“. The lasers are classified according to the injury they are capable of causing.
An example of injury caused by UV light is opacity of the crystalline lens, which is a formally recognized occupational disease among workers at open hearths.

## Slide 15: Negative effects - Non-visible light
Light often contains IR and UV radiation components. They occur during welding, at hearths, and on laser installations.
These components can damage the skin and eyes. For example, if welding work is performed without eye protection, ultraviolet radiation leads to inflammation of the cornea and conjunctiva.
Like UV radiation, IR radiation can also lead to sunburn and an elevated risk of skin cancer.
Notes: Laser radiation may contain radiation from ultraviolet (180 nm) through visible light to infrared (up to 1 mm).
Lasers are classified according to EN 60825-1 „Safety of laser products – Equipment classification and requirements“. The lasers are classified according to the injury they are capable of causing.
An example of injury caused by UV light is opacity of the crystalline lens, which is a formally recognized occupational disease among workers at open hearths.

## Slide 16: Effect of colour
Colour is perceived when light in the visible spectrum falls on objects. Depending upon the material properties of the objects concerned, a part of the light spectrum is reflected or absorbed. The residual light is projected onto the retina. The "cones" in the retina enable human beings to distinguish between colours.
The use of colours in practice can be considered with regard to three aspects.
(based upon REFA 1993)
Safety: by the marking of sources of hazards by means of warning colours that are universally understood
Coding: by the colour-coding of work-related objects and the contents of containers
Design and order: by assignment to the functions and forms of equipment
Colour wheel, based upon Johannes Itten (1961)
Notes: Colour can also be used to produce intentional physical and mental effects upon human beings. Their attitude to their work task can be influenced positively as a result (based upon Gericke, A. 1990).

## Slide 17: Effect of colour
© Michael Hüter
Notes: Colour can also be used to produce intentional physical and mental effects upon human beings. Their attitude to their work task can be influenced positively as a result (based upon Gericke, A. 1990).

## Slide 18: Effect of colour
Source: Heller, E.: Wie Farben wirken. Hamburg: Rowohlt Taschenbuch Verlag GmbH 2004
Psychological effect
Symbolic effect
Cultural effect
Political effect
Traditional effect
Creative effect
By automatic, unconscious reactions
Generally caused by traditions passed down over the centuries
Caused by lifestyle differences
By special, known symbolism
By historical background
New effects caused by surprising colours
Left-wing politics
Cold
Stimulation
Rest
In order
Purity
Death
Saxony
Notes: Red = stop; Green = envy; Green=Islam; Black/red/gold = Germany; Gold = the colour of crowns

## Slide 19: Effect of colour
Colour | Distance effect | Temperature effect | Psychological effect
 | Distance | Cold | Calming
 | Distance | Very cold to neutral | Very Calming
 | Close | Warm | Very exciting Disturbing
 | Very close | Very warm | Stimulating
 | Close | Warm | Stimulating
 | Very close Restricting | Neutral | Stimulating
 | Very close | Cold | Aggressive, disturbing Discouraging
nach Based upon BGI 523 101

## Slide 20: Influence of colour
Influence of colour upon the perceived properties (1)
Perceived properties
Effects
Temperature
Hardness
Weight
Colours within the range from red to golden yellow give a "warm" impression; those in the range from cyan through blue to violet give a "cold" impression
Red, white, yellow and cyan appear hard;
green, blue, black and grey appear soft
Light-coloured objects appear to be lighter in weight; dark objects heavier

## Slide 21: Influence of colour
Perceived properties
Effects
Spread
Distance
Plasticity
Green and blue objects appear larger than red or yellow objects.
Green and blue surfaces appear to recede into the background; yellow and red surfaces appear to project into the foreground.
Colours with a short wavelength (violet, blue, cyan) cause objects to appear flatter.
Influence of colour upon the perceived properties (2)

## Slide 22: Lighting design
Objectives of lighting design:
Reduction of the risk of work-related accidents
Avoidance of adverse strain upon the eyes, such as head and neck ache
Increased productivity by better concentration upon the work task and the consequent reduction in the error rate
Requirements for lighting are determined by the:
Visual comfort (workers should have a feeling of well-being)
Visual performance (performance of the visual task over a long period of time)
Safety requirements under normal operating and hazard conditions
Source: Lehder, G.; Skiba, R.: Taschenbuch der Arbeitssicherheit. Berlin: Erich Schmidt Verlag 2005

## Slide 23: Results of selective lighting design
Sufficiently high brightness level
Harmonious brightness distribution
Greatest possible limitation of glare
Good reproduction of contrast
Correct direction of light incidence
Correct shadow
Correct light colour and appropriate colour reproduction
High energy efficiency
Pleasant atmosphere created by the light
Low energy consumption

## Slide 24: Minimum illuminance levels
Working premises, workplaces, tasks (examples) | Minimum value for the illuminance (lx
Traffic areas and passageways without vehicular traffic Break rooms Storage rooms for homogeneous or bulky materials | 50 200 50
Assembly tasks Coarse Medium Fine | 200 300 500
Car manufacture Bodyshell construction and assembly - Final inspection, Surface inspection | 500 1000
Required illuminance levels (selection from ASR 3.4)

## Slide 25: Example of lighting design
Excerpt from the Machinery Directive, 2006/42/EC
"1.1.4. Lighting
Machinery must be supplied with integral lighting suitable for the operations concerned where the absence thereof is likely to cause a risk despite ambient lighting of normal intensity.
Lighting integrated into the machine
(see also EN 1837)
© Michael Hüter
Notes: Machinery must be designed and constructed so that there is no area of shadow likely to cause nuisance, that there is no irritating dazzle and that there are no dangerous stroboscopic effects on moving parts due to the lighting.
Internal parts requiring frequent inspection and adjustment, and maintenance areas must be provided with appropriate lighting.

## Slide 26: Example: Use of LEDs in lighting design
© Michael Hüter
Comparison of lamps
Benefits of LEDs
Drawbacks of LEDs

## Slide 27: Comparison of lamps
© Michael Hüter

## Slide 28: Comparison of lamps
© Michael Hüter

## Slide 29: Benefits of LEDs (overview)

## Slide 30: Drawbacks of LEDs

## Slide 31: Examples from the field
© Michael Hüter

## Slide 32: Examples of colour design
© Michael Hüter
Selective use of colour in order to highlight problematic conditions on displays (psychological effect of colour)
Notes: Selection of colours for pushbuttons to EN 60204-1

## Slide 33: Examples of colour design
© Michael Hüter
Use of colour to differentiate important controls (symbolic effect of colour)
EN 60204-1
Notes: Selection of colours for pushbuttons to EN 60204-1

## Slide 34: Examples of colour design
© Michael Hüter
Selective use of colour for visual structuring of functional differences
Notes: Selection of colours for pushbuttons to EN 60204-1

## Slide 35: Example: Protection against hazardous effects of light
© Michael Hüter
Wearing personal protective equipment during welding work

## Slide 36: Example: UV radiation
© Michael Hüter
Service hatch
Closed for protection against UV radiation
Can be opened to permit maintenance

## Slide 37: Example: Viewing window provides screening against UV radiation
© Michael Hüter
Viewing window
Viewing window provides screening against UV radiation
Opening the window permits access to the machine

## Slide 38: Important literature for Module 3-4 (in German)
ASR 3.4 Beleuchtung
ASR 3.4/3 Sicherheitsbeleuchtung, optische Sicherheitssysteme
BGHM-I 101 Mensch und Arbeitsplatz. 2013
DGUV Information 203-035 Expositionsgrenzwerte für künstliche optische Strahlung. 2004
Machinery Directive 2006/42/EG
Verordnung zum Schutz der Beschäftigten vor Gefährdungen durch künstliche optische Strahlung - OStrV vom 19.07.2010
Verordnung über den Schutz vor Strahlen durch Röntgenstrahlen (Röntgenverordnung – RöV) vom 04.10.2011

## Slide 39: Important literature for Module 3-4
BGR 131-1 Natürliche und künstliche Beleuchtung von Arbeitsstätten. 2008
DGUV Vorschrift 11 UVV Laserstrahlung. 1997
DGUV Information 215-11 Tageslicht am Arbeitsplatz - leistungsfördernd und gesund. 2009
DIN 2403 Kennzeichnung von Rohrleitungen nach dem Durchflussstoff
DIN 25430 Sicherheitskennzeichnung im Strahlenschutz
DIN 5381 Kennfarben
DIN 4844 series Graphische Symbole und Sicherheitskennzeichen
DIN 5033 series Farbmessung
DIN 5035 series Beleuchtung mit künstlichem Licht
DIN 6163 series Farben und Farbgrenzen für Signallichter
DIN 6164 series DIN-Farbkarten

## Slide 40: Important literature for Module 3-4
DIN 6171-1 Aufsichtfarben für Verkehrszeichen und Verkehrseinrichtungen – Teil 1: Farbbereiche bei Beleuchtung mit Tageslicht
EN 1837 Safety of machinery – Integral lighting of machines
EN 12464-1: Light and lighting – Lighting of work places – Part 1: Indoor work places
EN 12665 Light and lighting – Basic terms and criteria for specifying lighting requirements
EN 60204-1 Safety of machinery – Electrical equipment of machines – Part 1: General requirements
EN 60825-1 Safety of laser products – Part 1: Equipment classification and requirements

## Slide 41: Important literature for Module 3-4
Fisch, J.: Licht und Gesundheit – Das Leben mit optischer Strahlung
Fördergemeinschaft gutes Licht (publisher): Licht. Wissen 05 - Industrie und Handwerk. Frankfurt am Main. licht.de 2009
Gericke, A.: Farbwirkung, Farbassoziation, Farbsymbolik. Berlin 1990
Heller, E.: Wie Farben wirken. Hamburg: Rowohlt Taschenbuch Verlag GmbH 2004
Horton, W.: Das Icon-Buch. Bonn: Addison-Wesley GmbH 1994
Lehder, G.; Skiba, R.: Taschenbuch der Arbeitssicherheit. Berlin: Erich Schmidt Verlag 2005
Licht. Wissen 05: Industrie und Handwerk. publisher
Luczak, H.: Arbeitswissenschaft. Berlin Heidelberg: Springer Verlag 1998
Meier, V.: Licht und Farbe im Industriebetrieb. Berlin: Duncker und Humblot GmbH 1996

## Slide 42: Important literature for Module 3-4
Saller, R.: Vitamin D, UV-Biologie und Heliotherapie. Stuttgart: Hippokrates Verlag GmbH 1992
Voelker, S.: Eignung von Methoden zur Ermittlung eines notwendigen Beleuchtungsniveau. Marburg: Tectum Verlag 1999
Practical aids
Calculation of illumination by the Institute of Occupational Health, Safety and Ergonomics (ASER) (in German)
http://www.institut-aser.de/out.php?idart=276

## Slide 43: Impressum
Author: Dipl.-Ing. Horst Böhmer
Chemnitz
horst.boemer@iapo-online.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de/en http://ergonomie.kan-praxis.de/en