## Slide 1: Work environment factors Part 5: Climate
Module 3 - Learning ergonomics

## Slide 2: Overview
Definition of climate parameters
Physiological principles
Adaptation by the human body
Measured variables and instruments
Cold and hot media
Technical design solutions
© Michael Hüter

## Slide 3: Definition of climate parameters
A human being's performance depends strongly upon their personal subjective well-being. This in turn depends upon effective thermoregulation and appropriate climatic conditions.
A drop in performance, indisposition, illness, and ultimately incapacity to work may be the consequences of poor climate parameters.
Climate parameters are:
Atmospheric temperature
Temperature of the surrounding walls, floor and ceiling (in indoor areas)
Atmospheric humidity
Airspeed
Thermal radiation
Notes: Workplaces in which climate is a significant factor in the working environment, e.g.:
Cold stores
Mill trains
Furnaces
Kitchens

## Slide 4: Physiological principles
© Michael Hüter
Temperature characteristics in the human body as a function of the atmospheric temperature
Atmospheric temperature
Atmospheric temperature

## Slide 5: Adaptation by the human body
© Michael Hüter
Evaporation of sweat
on the skin surface
(water vaporization approx. 60% of the emitted heat)
Thermal insulation
by clothing
Direct conduction, for example from the soles of the feet, through the soles of the shoes, to the floor
(approx. 5% of the emitted heat)
Thermal radiation
(approx. 20% of the emitted heat)
Heat generation
by the metabolism (muscel work)
Thermal convection to the surrounding air
(approx. 15% of the emitted heat)
Notes: When thermal energy is emitted by radiation, no substance is required for its transmission. As a result of their temperature, bodies may emit electromagnetic waves which take the form of thermal radiation. Solar radiation to the earth is an example. Thermal radiation does not raise the temperature of the air, but only of liquid or solid matter. Thermal radiation is the transport of thermal energy by electromagnetic radiation.
Thermal convection is the transport of thermal energy in the flow of matter (and therefore, in the example on the slide, transfer to the room air).

## Slide 6: Physical reactions to ambient temperatures
Low ambient temperature
High ambient temperature
Leads to surplus body heat
Physical reactions:
Causes the body to be cooled by
evaporative cooling
Leads to a rise in the blood-circulation
rate, which in turn increases the
conduction of heat through the skin and
respiratory tract
Increase in the heart rate
Evaporation of sweat
Leads to a deficit in body heat
Physical reactions:
:
Lowering of the heart rate
Increase in oxygen intake
Results in an increase in the production
of heat in the body
Results in lowering of the blood-
circulation rate, which in turn causes
a reduction in the emission of heat from
the body core to the environment

## Slide 7: Thermoregulation of the body

## Slide 8: Measured variables and instruments
Climate parameters
Measured quantity
Instrument
Unit of measurement
Trocken-
temperatur
Thermometer
Grad Celsius [°C]
Kelvin [K]
Luft
-
temperatur
Feucht
-
temperatur
Aspirations-
psychrometer
Prozent relativer
Feuchte [%]
Luftfeuchte
Luftströmungs-
geschwindigkeit
Flügelrad-,
thermisches
Anemometer
Meter pro
Sekunde [m/s]
Luftgeschwin-
digkeit
Wärmestrom-
dichte
Globethermo-
meter, Infrarot-
messsonden
Watt pro m²
[W/m²]
Wärme-
strahlung
Dry temperature
Thermometer
Degrees Celsius
[°C] / Kelvin [K]
Air temperature
-
Wet-bulb temperature
Aspirated psychrometer
Percentage of relative humidity [%]
Atmospheric humidity
Air velocity
Vane/thermal anemometers
Metres per second [m/s]
Air velocity
Heat flow density
Globe thermome-meters, infrared measuring probes
Watts per m²
[W/m²]
Thermal radiation

## Slide 9: Rules and regulations
Maximum temperatures (green/amber/red model to ASR 3.5)
< 26 °C | < 30 °C | < 35 °C
 | Measures | Work in hot environments
Notes: The German Ordinance on Working Premises requires working areas to have a room temperature that is conducive to good health, and to provide protection against excessive solar radiation.
Workplace rule A3.5 supports these general provisions.
A risk arises where heavy physical work is performed and thermally insulating work clothing worn at temperatures between 26 °C and 30 °C.
The same applies to persons of impaired health and employees requiring particular protection.
Measures for reducing the exposure can be implemented, for example by the provision of drinks, easing of the clothing regulations, ventilation during the morning hours, and flexitime arrangements.
At temperatures over 30 °C, the measures stated are mandatory.
At 35 °C and over: T-O-P
Minimum temperatures are dependent upon the arduousness of work and the prevailing body posture.

## Slide 10: Cold and hot media
Contact with cold and hot media in the work process can cause serious injury to the surface of the skin at exposed points in the form of frostbite or burns.
Examples:
Cold media | Hot media
Cold surfaces | Hot surfaces
Cold liquids | Hot vapour/hot air
Liquefied gases | Naked flames
Vaporizing refrigerants | Sprays of hot media

## Slide 11: Surface temperature threshold values
Surface temperature threshold values for various effects
(with a contact duration of 10 seconds to EN ISO 13732-1 Ergonomics of the thermal environment – Methods for the assessment of human responses to contact with surfaces – Part 1: Hot surfaces)
Effect
Frostbite
Numbing
Pain
Thermal inertia Fo
[106 J2/s m4 K2]
Material
Surface temperature To [°C]
Aluminium
-7.0
+3
15
449
Steel
-12.5
-1
15
52.9
Stone
-18.5
-15
3.5
4.35
Nylon
-
-40
-6
0.61
Wood
-
-
-10
0.27

## Slide 12: Threshold values for burns
Thresholds for burns To (°C) in the event of contact with the hot surfaces of various materials (to EN ISO 13732-1)
Material
Contact duration
1 minute 10 minutes 8 hours
Uncoated metals
51
48
43
Coated metals
51
48
43
Ceramic materials
56
48
43
Plastics
60
48
43
Wood
60
48
43
Notes: The long-term value of 43 °C over 8 hours and longer applies only when a small part of the body (up to 10% of the entire skin surface area) or of the head (below 10% of the total head surface area) is affected. If larger areas are affected, serious injury may occur even at temperatures below this value.

## Slide 13: Technical design solutions
Example: reduction of the dissipation of thermal radiation
Protective screens
Chain curtains
Water curtain
Absorbing or reflecting glass surfaces
Insulation of machine parts
Air-conditioning systems

## Slide 14: Example of a technical solution
Grab for the handling
of a hot workpieces at a furnace (with protective shield)
© Michael Hüter

## Slide 15: Important literature for Module 3-5
Arbeitsstättenrichtlinien ASR A3.5 (Raumtemperatur) und ASR A3.6 (Lüftung)
DGUV Information 213-022 Beurteilung von Hitzearbeit – eine Handlungshilfe für kleine und mittlere Unternehmen. 2011
DGUV Information 215-510 Beurteilung des Raumklimas. 2010
DIN 33403 series of standards Klima am Arbeitsplatz und in der Arbeitsumgebung
EN ISO 13732-1 Ergonomics of the thermal environment – Methods for the assessment of human responses to contact with surfaces – Part 1: Hot surfaces
EN ISO 11399 Ergonomics of the thermal environment – Principles and application of relevant international standards

## Slide 16: Important literature for Module 3-5
EN ISO 7730 Ergonomics of the thermal environment – Analytical termination and interpretation of thermal comfort using calculation of the PMV and PPD indices and local thermal comfort criteria
EN ISO 7933 Ergonomics of the thermal environment – Analytical determination and interpretation of heat stress using calculation of the predicted heat strain
EN ISO 9920 Ergonomics of the thermal environment – Estimation of thermal insulation and water vapour resistance of a clothing ensemble
EN 27243 Hot environments – estimation of the heat stress on working man, based on the WBGT index (wet bulb globe temperature)

## Slide 17: Important literature for Module 3-5
EN ISO 8996 Ergonomics of the thermal environment – Determination of metabolic rate
EN ISO 11079 Ergonomics of the thermal environment – Determination and interpretation of cold stress when using required clothing insulation (IREQ) and local cooling effects
Bux, K.: Klima am Arbeitsplatz (Forschungsprojekt F 1987). Dortmund: Bundesanstalt für Arbeitsschutz und Arbeitsmedizin 2006
Rechner des Institut für Arbeitsmedizin, Sicherheitstechnik und Ergonomie e.V. (ASER): Klimarechner https://www.institut-aser.de/out.php?idart=1607 Klima und Arbeitsschwere http://www.institut-aser.de/out.php?idart=246

## Slide 18: Impressum
Author: Dip.-Ing. Horst Böhmer Chemnitz E-Mail: horst.boehmer@iapo-online.de
Initiated and funded by:
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de/en http://ergonomie.kan-praxis.de/en