## Slide 1: Work environment factors Part 6-1: hazardous substances
Module 3 – Learning ergonomics

## Slide 2: Overview
Definition of hazardous substances
Classification
Technical solutions for protection against hazardous substances
© Michael Hüter
Gaseous emissions
Leakages
Casks containing hazardous substances
Vapours
Solid materials, dust
Liquids

## Slide 3: Definition of hazardous substances
Hazardous substances in the sense of the German chemicals act are: Hazardous substances and preparations in accordance with Section 3a
(substances which are explosive, oxidizing, extremely flammable, highly flammable, flammable, very toxic, toxic, harmful to health, corrosive, irritant, sensitizing, carcinogenic, reprotoxic, mutagenic or a hazard to the environment) and substances and preparations which possess other chronically harmful properties
Substances, preparations and products that are explosive
Substances, preparations and products the production or use of which could result in the formation or release of substances or preparations listed under Nos 1 or 2
Substances, preparations and products known to be capable of transferring pathogens

## Slide 4: Classification
Hazardous substances
Solid hazardous substances
Liquid hazardous substances
Hazardous substances in suspension in the air (atmospheric contaminants)
Solid hazardous substances
Flüssige Gefahrstoffe
Gaseous hazardous substances
Dusts
Fumes
Vapours
Gases
Mists

## Slide 5: Technical solutions for protection against hazardous substances
© Michael Hüter
Enclosure of machinery
Filtration and absorption of substances
Collection of exhausted hazardous substances
Generation of positive pressure and directed air supply

## Slide 6: Literature
Bundesimmissionsschutzgesetz vom 26.09.2002 zuletzt geändert 17.05.2013
Technische Anleitung Luft - TA Luft vom 20.07.2002
Chemikaliengesetz ChemG vom 20.06.2002 zuletzt geändert 07.11.2006
Gefahrstoffverordnung vom 23.12.2004 zuletzt geändert am 15.07.2013
Technische Regeln für Gefahrstoffe:
TRGS 001 Das technische Regelwerk zur Gefahrstoffverordnung – Allgemeines - Aufbau - Übersicht
TRGS 402 Ermittlung und Beurteilung der Konzentration gefährlicher Stoffe in der Luft in Arbeitsbereichen
TRGS 500 Technische Lösungen zum Schutz vor Gefahrstoffen
TRGS 600er Reihe - Ersatzstoffe und Ersatzverfahren
TRGS 900 Arbeitsplatzgrenzwerte

## Slide 7: Literature - Standards
EN 626-1 Safety of machinery - Reduction of risks to health from hazardous substances emitted by machinery
EN 689 Workplace atmospheres - Guidance for the assessment of exposure by inhalation to chemical agents for comparison with limit values and measurement strategy
EN 1093-11 Safety of machinery - Evaluation of the emission of airbone hazardous substances - Part 11: Decontamination index

## Slide 8: Practical aids
Institut für Arbeitsmedizin, Sicherheitstechnik und Ergonomie e.V. (ASER)
Spaltenmodell-Rechner zur Ersatzstoffprüfung
http://www.institut-aser.de/out.php?idart=497
GESTIS-Datenbank DGUV
http://gestisbio-en.itrust.de/nxt/gateway.dll/bioen/000000.xml?f=templates$fn=default.htm$vid=gestisbioeng:biosdbeng$3.0
Glossary of occupational exposure limits, issa (International social security association) www.grenzwertglossar.de

## Slide 9: Work environment factors Part 6-2: Radiation
Module 3 – Learning ergonomics

## Slide 10: Overview
© Michael Hüter
Classification
Effect of radiation
Technical solutions for protection against radiation
Notes: This sub-module provides only a brief introduction to radiation, since it is at most a peripheral area of ergonomics.

## Slide 11: Classification of radiation
Radiation
Ionizing radiation
e.g. X-rays
Neutron radiation
Non-ionizing radiation
Electromagnetic fields
Optical radiation
Low-frequency
(electrical and magnetic fields)
High-frequency
(high-frequency electromagnetic fields)
Notes: Optical radiation: example: visible light, UV radiation, IR radiation
Low-frequency fields: example: power supply, electric transport systems
High-frequency fields: example: wireless data transmission

## Slide 12: Effect of radiation
Ionizing | Low-frequency | High-frequency
Ionizing radiation leads at sufficiently high doses to: Deterministic effects Damage to or destruction of cells 2. Stochastic effects Damage to the cell nuclei (and therefore to the genes; carcinogenic action) | The electric field barely penetrates the body The magnetic field induces currents within the body; at higher levels, these can lead to cardiac fibrillation Possible long-term effects below the limit values have not been scientifically validated | High-frequency radiation is absorbed by human tissue; the energy of the radiation leads only to a local temperature rise The impact is dependent upon the penetration depth: high frequency = minor penetration depth If the frequency lies within the range of the body's own resonance frequency, more energy is transferred

## Slide 13: Technical solutions for protection against radiation
Ionizing radiation | Structural and technical measures for the avoidance of exposure to radiation Protection by suitable working procedures Measurement of the radiation exposure for the avoidance of overdosing (dosimeter)
Low-frequency radiation | Earthing of objects close to low-frequency, AC electric fields (risk of electrostatic charging) Insulation of electrical conductors
High-frequency radiation | Placing of equipment in service only when in perfect condition Screening of sources of microwave radiation Use of protective suits manufactured from metallized nylon De-energization of installations when not in use

## Slide 14: Literature
Gesetz über die elektromagnetische Verträglichkeit von Geräten EMVG vom 20.04.2012
Verordnung zum Schutz der Beschäftigten vor Gefährdungen durch künstliche optische Strahlung - OStrV vom 19.07.2010
Verordnung über den Schutz vor Strahlen durch Röntgenstrahlen (Röntgenverordnung – RöV) vom 04.10.2011
Bildschirmarbeitsverordnung – BildschArbV
EN ISO 12198 series of standards Safety of machinery – Assessment and reduction of risks arising from radiation emitted by machinery
DIN EN 50413 Basic standard on measurement and calculation procedures for human exposure to electric, magnetic and electromagnetic fields (0 Hz - 300 GHz)
DGUV Vorschrift 15 UVV Elektromagnetische Felder
DGUV Information 215-410 Bildschirm- und Büroarbeitsplätze, Leitfaden für die Gestaltung

## Slide 15: Practical aids
Technical information from the IFA of the DGUV
Optical radiation
http://www.dguv.de/ifa/Fachinfos/Strahlung/Optische-Strahlung/index-2.jsp
Electromagnetic fields
http://www.dguv.de/ifa/Fachinfos/Strahlung/Elektromagnetische-Felder/index-2.jsp

## Slide 16: Impressum
Author: Dip.-Ing. Horst Böhmer Chemnitz E-Mail: horst.boehmer@iapo-online.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de/en https://ergonomie.kan-praxis.de/en