## Slide 1: Work environment factors Exercises
Modul 3 – Learning ergonomics

## Slide 2: Work environment factors – exercises
Describe the work environment factors in the work system in terms of the relationship between emissions and exposure. State two examples of each.
State measures for optimizing exposure, with the correct ranking. Describe a concrete example for each measure.
Define and differentiate between noise and sound.
State 3 technical solutions for sound attenuation.
Why do sound and mechanical vibration generally occur in combination on work equipment?
Name two typical forms of harm caused by mechanical vibration (occupational disease, symptoms).

## Slide 3: Work environment factors – exercises
Define the term "contrast".
State three possible effects of colour, and for each effect, an example from the area of design.
State three possible ways by which the human body adapts to high ambient temperatures.
State three technical solutions for reducing the dissipation of thermal radiation.

## Slide 4
On the next slides:
Solutions

## Slide 5
At a workplace, machines exhibit emissions (constitute work environment factors) which impact upon human beings in the form of exposure (stress). Examples: sound (an emission) is perceived as noise (an exposure); vibration emitted from machinery causes vibration exposure in human beings, etc.
Technical solutions take precedence over organizational measures take precedence over personal protective measures (T-O-P). Example of a technical solution: selection of working processes with lower emissions; example of organizational measures: locating high-emission machinery away from workplaces; example of personal protective equipment: hearing protection.

## Slide 6
Noise is defined as a sound event which is undesired, intrusive, and damaging to the hearing. For the worker, it constitutes a form of exposure.
Example: selection of low-noise working procedures; reducing the ability of structures to transport sound (damping of structure-borne sound, grey cast iron in place of steel); elimination of resonancesSchall und Schwingungen haben in der Regel die gleichen physikalischen Ursachen.
Sound and vibration generally have the same physical causes.
Example: vibration white finger, caused by circulatory disturbances triggered by vibration, or carpal tunnel syndrome (tingling and numbness) caused by the squeezing of nerves.

## Slide 7
Contrast is the difference in luminance between two adjacent areas.
of the effect of colour: as a signal (red warniExamplesng lamp); for visual emphasis of machine elements (use of colour to distinguish between the machine bed and moving machine elements); distinction between different control elements (green switch for starting the machine).
Example: evaporation of sweat, thermal convection, direct conduction of heat.
Example: protective shields, water curtain, isolation of machine parts.

## Slide 8: Impressum
Author: Dip.-Ing. Horst Böhmer Chemnitz E-Mail: horst.boehmer@iapo-online.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de/en http://ergonomie.kan-praxis.de/en