## Slide 1: Ergonomic aspects of the IT design of human-machine interfaces (Human-Machine-Interface) Part 1: Selection and design of control actuators
Module 4 – Learning ergonomics

## Slide 2: Overview
General procedure
Forms of grip and coupling
Axis orientation and dimensions
Catalogue of solutions for the correct selection of control actuators
Specification of the dimensions for control actuators
Surface design
Principles of compatibility
© Michael Hüter
Notes: Control actuators are used for the operation of products. This lecture teaches the principles behind the correct selection and design of control actuators. For this purpose, the general procedure for the selection and design of control actuators is first explained. More detailed information is then provided on grip and coupling types and different axes of actuation of control actuators, and their dimensions.
A catalogue of solutions for selection of the correct control actuators is presented, and we examine the specification of control actuator dimensions, design of control actuator surfaces, and essential principles of compatibility.

## Slide 3: Procedure for the selection and design of control actuators
Determining of the basic and influencing parameters from the control task
Definition/selection of the control actuator geometry
Determining of dimensions
Selection of the material
Design of the surface
Type of movement (form, dimension and direction of movement)
Body position (type of grip, hand posture, form of coupling)
Time required for the control operation (frequency of operation, nature and duration of discrete actuation)
Determining the resistance to work (force/moment, progression)
Notes: Terminology, control actuator:
Control actuators (also termed controls or control elements) are elements on working equipment which are operated by the hands, fingers or feet. They are used to operate and control equipment, mainly technical in nature.
The control actuator is the part of an actuation system that is operated directly by the operator, for example by pressure.
Control actuators are operated or influenced in order to bring about a change within a system.
Based on: Institut für angewandte Arbeitswissenschaft e.V. (eds.): Arbeitsgestaltung in Produktion und Verwaltung und EN 894-1 and 3
Where suitable control actuators are to be selected for a work task, existing control actuators redesigned or new control actuators designed, the following methodical procedure is recommended:
1. Analysis of the control task, in order to determine the terms of reference and the conditions of use  The design objectives must be formulated, as must the wishes and requirements and the desired and undesired effects of the design condition
From the results, design characteristics can be derived:
2. With reference to the constraints formulated in Point 1, suitability criteria such as the safety, communicative and performance criteria can be used for selection of a particular control actuator geometry.
3. The actuator is then dimensioned in detail by definition of the dimensions for the user group of the control actuator.
4. Grip conditions and contact type and the corresponding design characteristics are derived from Point 1.

## Slide 4: influencing parameters – type of grip
(A) ) Contact grip
      Controls with a small time component
      Only one direction of movement
      Limited control granularity
(B) Pinch grip
      Positioning with a high degree of precision, since the actuator can be gripped at any point
      Limited range of movement
      High control granularity
(C) Clench grip
      Transmission of large forces
      Many directions of movement
      High control granularity
      Slow gripping and release
Type of grip = type of coupling between the part of the body and the control actuator
© Michael Hüter
Notes: Type of grip
Depending upon the purpose of the actuation, the desired grip is either enveloping or perfunctory, and involves either high mobility or rigid coupling for the fingers.
From a physiological perspective, a distinction can be drawn between the following grip types. The grip type determines the geometry of the control actuator.
(A) Contact grip
The coupling elements are located on the coupling surface. The grip is open.
(B) Pinch grip
The coupling elements consist of spot contacts on several sides of the coupling surface. The control actuator is held and guided without being enclosed by the hand.
(C) Clench grip
All coupling elements must fully surround the control actuator.
For examples, see Slides 6 to 8

## Slide 5: influencing parameters – form of coupling
Frictional coupling
    Force and torque act in the contact plane between the part of the body and the control actuator (tangentially and longitudinally with respect to the control actuator axis and to the axis of movement)
    Transmission of the force/torque by frictional coupling
    Climbing a climbing pole; withdrawing a key from a lock
    Operating a handwheel
Type of coupling = type of transmission of the force between the part of the body and the control actuator
    High coefficients of static friction, by means of:
      Materials with rough surfaces
      Soft materials
      Surface profiling:
      - Profiling oriented in the holding direction
      - Unidirectional profiles
Notes: The form of force coupling is of particular importance when greater forces are exerted.
In frictional coupling, the holding forces are perpendicular to the working force.
Couplings employing friction are generated on surfaces with an adequately high coefficient of static friction.  Materials with rough surfaces or profiling of the surface
Surface profiling:
The profiling must be suitably oriented for the holding direction
Unidirectional profiling is less problematic in this respect, but may result in a part of the generated static friction not being exploited
When soft materials (with high static friction) are used, a certain degree of play, spring-like in nature, is often unavoidable. Soft materials have the property of adapting well to the morphology of the human skin, however.
lower description field is animated

## Slide 6: influencing parameters – form of coupling
Direction of movement
Principle of action
Preferred application
Precise positioning
Rapid positioning
Continuous positioning
Positioning with regripping and clenching
For large actuation distances and angles
FN
FR=  *FN<FN
F = -FR
F: Actuating force
FN: Normal force
FR: Frictional force
 : Coefficient of friction
© Michael Hüter
Notes: Friction coupling:
Only indirect exertion of force, depending upon the coefficient of friction
Transmission of only a certain percentage of the required force
Greater thrust forces required
In order for a tool to remain in the hand, the fingers must exert a contact pressure upon the handle in order to generate sufficient static friction
The holding forces cancel each other out and do not therefore contribute to the work force
Advantage of frictional coupling:
The force coupling is released more easily
Mobility of the hand-handle coupling

## Slide 7: influencing parameters – form of coupling
Basic geometries of control actuators for frictional coupling
Source 1: Bullinger, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
Notes: Examples of basic geometries for frictional coupling:
Contact grip: slider for infinitely variable control
Pinch grip: steering wheel; the palm or proximal phalanges rest loosely on the steering wheel and drive it during rotation
Clench grip:
Rotary knob which is gripped by the finger pads
Screwdriver handle which is in contact with the entire palm

## Slide 8: influencing parameters – form of coupling
(B) Positive coupling
    Force and torque act perpendicularly (radially) to the contact plane between the part of the body and the control actuator
    Gymnastic exercises on wall bars; turning a key in a lock; opening a drawer by pulling a bow handle
F = FN
Preferred application
Transmission of large forces
Holding against resistance
Position can be determined by touch
Principle of action
Notes: With positive coupling, the holding forces are applied in the same direction as the working force; the force in the fingers is therefore only slightly greater than the exerted force.
Contact pressure on the control actuator contributes directly to the working force
Low thrust force requirement
A geometry with positive coupling contributes to better coupling conditions and to reduction of the grip forces

## Slide 9: influencing parameters – form of coupling
Basic geometries of control actuators for positive coupling
Source 1: Bullinger, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
Notes: Examples of control actuators with positive coupling:
Finger contact, rotational movement:
Dial on older telephones
Finger contact, translation:
Sliders with flat grip geometries: these provide a larger contact surface area and the control actuator is moved with the finger in the direction of movement when pressure is applied perpendicular to the contact surfaces
Pinch contact with the hand, translation:
Bow handles: perpendicular pressure of the middle phalanxes of the fingers upon the contact surfaces of the handle
Rotary knob:
Contact with the pads of the fingers owing to an adequately dimensioned contact surface, contact pressure on this contact surface and driving of the control actuator during the rotational movement
The length of the rotary lever influences the positions of the fingers in relation to each other and thereby the form and precision of the control operation. Longer lever lengths: fingers located offset from each other: discrete control processes, larger angles of rotation by re-gripping and clasping; short lever lengths: fingers located opposite each other; precise control in smaller ranges of rotation
Joystick (clench grip):
The spindle geometry of coupling surface areas is favourable owing to the even distribution over the entire palm
Spade grip (clench grip):
Good alignment of the longitudinal axis of the lower arm with the functional axis and even distribution of the fingers on the grip

## Slide 10: Geometry of the control actuator – example
Oval handle
      Positive and frictional coupling oriented towards the direction of work
      Approximately rectangular geometries: good compromise for a range of task types and movements
      Spherical geometry
      Random gripping
      Rapid change in direction
      Geometrical coding
      Translational one-dimensional movement
      Round and hexagon-section geometry
      Moulds to the curvature of the palm
      Easy re-gripping
      Application of high torques and pressures
© Michael Hüter

## Slide 11: Influencing variables – hand position
For translational and rotational movements:
 Alignment of the axes of the forearm and hand
For rotational movements, ideally:
 Alignment of the anatomical and functional axes
Assignment of the anatomical and functional axes
© Michael Hüter
Notes: The line of force exertion is straight from the forearm to the tool end (tip of the drill or screw)
Direct transfer of the contact pressures
Avoidance of tilting moments
A normal hand posture is favourable for stress reasons. If the wrist joint is angled, the tendons are deflected within the carpal tunnel, giving rise to friction  a risk of inflammation of the tendon sheath; in addition, force is not transmitted in the most efficient way when the wrist joint is angled, and the fine-motor movement of the fingers is impaired
Images, bottom: alignment of hand-finger axis and functional axis – force exertion in a straight line
Alignment of the hand-forearm axis to the functional axis
Avoidance of tilting moments

## Slide 12: Catalogue of solutions for preliminary selection of control actuators orientierenden Auswahl von Stellteilen
A) Performance criteria
    Force and moment of actuation position
    Accuracy of actuation
    Speed
    (B) Communicative criteria
      Tactile recognition of the
      Visual detection of the setting
      (C) Safety-related criteria
      Unintended actuation
      Slipping off the control actuator
      Actuation possible whilst wearing gloves
      Ease of cleaning
Evaluation of control actuators in EN 894-3 by means of criteria for suitability such as:
Notes: A suitable control actuator can be selected from catalogues of solutions with reference to suitability criteria.
The suitability criteria reflect the requirements deriving from the control task.

## Slide 13: Definition/selection of the control actuator geometry
Performance criteria:
+Z
-Z
Source: EN 894-3
Notes: Catalogue of solutions to EN 894-3
In consideration of the general requirements (performance criteria, movement characteristics), a suitable control family is first determined which can best satisfy the control task to be performed.
In the example shown, this is a slider which assures fast and precise execution for continual control in the z axis (up and down).
The slider is able to transmit very low forces, since the control movement is performed with a pinch grip.

## Slide 14: Definition/selection of the control actuator geometry
Performance criteria:
Quelle: DIN EN 894-3
Communicative and safety-related criteria
Notes: The control actuator family is then constrained further by additional criteria (communicative, safety-related, grip characteristics). For example, a slider with edge profile is then selected, since for example only the requirement "avoid unintended slipping of the fingers off the control actuator" was identified from the control task and this is adequately met by both sliders (with squared profile and with pointer geometry); the squared form was however preferred for other reasons (appearance, simplicity of construction, etc.).

## Slide 15: Determining of dimensions
Minimum dimensions to EN 894-3 (example)
Type of grip | Force applied by the part of the hand in contact | Width/diameter of the control actuator | Length of the control actuator along the linear or rotational axis
Contact grip | Finger Palm of the hand | ≥ 7 mm ≥ 40 mm | ≥ 7 mm ≥ 40 mm
Clench grip | Finger/hand | ≥ 15 mm to < 35 mm | ≥100 mm
Notes: In the hand-finger area, the contact surface is not a contiguous surface, but is made up of 14 finger joints.
The dimensions (length, diameter) selected for the control actuator influence the size of the contact surface area for the hand/the individual finger joints involved.
The dimensions selected for the control actuator also influence the joint angle of the fingers used for coupling: with a ball knob of too large a size, for example, the hand can maintain contact only with extreme spreading of the fingers: fine motor movement and the transmission of force deteriorate as a result, and the hand is subject to strong strain.

## Slide 16: Determining of dimensions
Minimum dimensions to EN 894-3 (example)
Notes: In order to permit unhindered execution of a control movement, minimum clearances must also be observed between control actuators of the same type.
In addition, minimum clearances must be observed between different control actuator families, owing to the actuation characteristics (for example between a pushbutton and a rocker switch).  For percentiled dimensions of the hand and phalanxes: refer also to anthropometric dimensions, for example in DIN 33402

## Slide 17: Selection of the material/design of the surface
Differentiation:
Smooth surfaces of different roughness depth
Profiled surfaces (morphology, dimensions, interval and direction of the profiling)
By raising the coefficient of friction = f (material property, profiling)
FR =  FN  increase 
Where contact pressures on the control actuator are low: by using smooth surfaces if possible
Where contact pressures on the control actuator are high: by using profiled/textured surfaces if possible
Profiling should always be perpendicular to the direction of movement
Combined movements (rotating and pulling): with knurled or pimpled profile geometry
Coarse profiles are not generally recommended (profile interval < 3 mm)
Increasing the frictional force between the hand and the handle:
Notes: Differentiation:
Smooth surfaces of different roughness depth
Profiled surfaces (by morphology, dimensions, interval and direction of the profiles)
Type of coupling: friction
Objective: highest possible frictional resistance
According to Coulomb's law: FR =  FN
Thus (simplified):
The frictional force is independent of the dimensions of the contact surfaces
The frictional force is independent of the velocity of motion (friction is normally greater during movement, but is assumed here to be approximately the same)
The frictional force is dependent upon the material properties of the two contact surfaces
Frictional force during static friction is greater than during dynamic friction (at a given normal force)
Coulomb's laws apply only to solids
Friction pairing: hand – rigid body
Coupling between rigid (work equipment) and resilient (hand) bodies
Coulomb's law cannot simply be applied to the hand/handle interface without consideration for the particular situation; direct proportionality cannot be expected
Firstly, overcoming of the internal friction: displacement of the epidermis relative to the bone structure; then overcoming of external friction between the skin surface and the surface of the solid body
The friction can be influenced in two ways:
Increasing of the coefficient of friction
The coefficient of friction is a function of the material property (smooth, rough) and of the form of the profiling.
b) Increasing of the normal force (by influencing of the contact surface area)
The widely held view that profiling of the handle surface increases the coefficient of friction under all circumstances is not correct. The profile characteristics must be differentiated according to the level of the required coupling force.
At high contact pressure forces of the coupling bodies on the control actuator, the coefficient of friction of profiled surfaces is greater than for smooth materials (a strong surface pressure upon the skin).
At low and medium contact pressures, coarse or fine profiling respectively reduces the contact surface area and therefore also the adhesion forces, causing the coefficient of friction to decrease. In this case, smooth materials have a higher coefficient of friction than profiled surfaces. Profiling is acceptable in this case only if unfavourable ambient conditions such as moisture, sweat, oil or dirt have a negative influence upon the contact surface. Conversely, profiling should be used when high contact pressures are anticipated or desirable.
Note:
Materials with a high coefficient of friction, such as surface-polished plastics or metals with a low peak-to-valley height, have a distinct stick-slip characteristic when sliding against another surface. Deformation of the skin and damage to it may therefore occur

## Slide 18: Select the material/design of the surface
Coefficients of friction of certain materials
High coefficient of friction | Low coefficient of friction
Contact grip: Smooth surfaces: Plexiglass, copper, enamel, hard rubber, chrome-plated brass, glass, soft PVC Profiled surfaces: Pimpled rubber, fine rubber Coarse aluminium lateral/longitudinal | Grained leather, cork Wood: ash, beech Rigid foam PVC, hard, fine/longitudinal
Pinch grip: Movement longitudinal to the fingers: Hard rubber, soft PVC Movement lateral to the fingers: Hard rubber, soft PVC | Painted wood, beech Brass, aluminium
Werte nach Bullinger (1994) und Bullinger, Kern, Solf (1979)
Notes: Hand contact:
Among smooth materials, plexiglass has the highest sliding coefficient of friction; it therefore serves as a reference for all other materials
Among profiled surfaces, pimpled rubber has the highest coefficient of friction, and therefore serves as a reference for all other materials
Two-finger pinching:
For smooth materials: hard rubber is the reference material
For profiled materials: fine-profiled rubber is the reference material
The value for dynamic friction is generally greater than that for static friction (contrary to Coulomb's law)
1: static friction
2: dynamic friction
 with smooth materials: 1 = 0.82
 with profiled materials: 1 = 0.92

## Slide 19: Select the material/design of the surface
(2) Icrease the normal force (contact pressure):
    By increasing the coupling area, contact area FR =  FN  increasing FN FN = p  A:
  By increasing the surface pressure, increasing the contact surface areadruckanthropomorphe Werkstoffe (z.B. Gummi)
Materials (such as rubber) which adapt under pressure to the morphology of the human body
For small and medium pressure forces: use smooth materials if possible
Pinching by two fingers: direction of movement perpendicular to the fingers
Increasing the frictional force between the hand and the handle:
Notes: Increasing of the normal force (contact pressure): increasing of the coupling surface area, contact surface area  increasing of FN
The normal force can be increased by an increase in the surface pressure and the contact surface area.
Increase in the surface pressure by greater contact pressure on smaller surface areas or lower contact pressure on larger surface areas
The contact surface area can be increased only by optimization of its morphology and dimensions, and not by anthropomorphic design (i.e. adaptation to the contours of the human body), since the latter differ for each individual.
Conversely, materials which adapt under pressure to the morphology of the human body (such as rubber) have a high coefficient of friction. They deform to some degree to match the contours of the hand and fingers, thus increasing the coupling surface area.

## Slide 20: Compatibility
Use is made of certain expectations of the user during the associated design of information input and output systems
Shortening of the learning phases
Reducing of maloperations
Reinforcement of stereotypes = responses are learnt automatically and largely unconsciously (stable behavioural patterns)
 Stereotypical images  Stereotypical interpretations
Stereotypical assignment of  Stereotypical responses signals and responses
Stereotypical anticipations
© Michael Hüter
Notes: Compatibility:
High level of correspondence and compatibility between the anticipated and actual sequence of events
Stereotypes:
Stereotypical behaviour modes within populations are highly ingrained reaction habits (stable patterns of behaviour), either learned or innate, which are either universal or present among large populations.
Stereotypes = learned, largely unconscious and automated reactions; deep-rooted, typical movement responses  important under fatigue conditions, under which human beings often revert to such stereotypes unconsciously
Stereotypical forms of presentation (reading from left to right, from top to bottom)
Stereotypical interpretations (up means increasing, down means decreasing)
Stereotypical assignment of signals and responses (logic of directions of movement, e.g. clockwise means to the right)
Stereotypical expectations (greater pressure means a greater effect)
Stereotypical responses (orientation responses)

## Slide 21: Compatibility – through coding of the information
Coding means:
Implementation of defined semantic content in a symbol agreed between human beings
Improved facility for visual and tactile distinction
© Michael Hüter
Notes: The symbols providing the information are specified by coding of the information. The technical signals received on the work equipment are linked to a specific constellation of symbols and thus made perceivable. Assignment of the symbols to an item of information (decoding of the information by the operator) is characterized by regulations, instructions and conventions.
Benefits of the compatibility of coding:
Reductions in errors and in the time required for cognitive processing
Information that is not required for a certain task can be hidden
Reduction in the number of presentations and in the volume of information presented
Colour coding:
Suitable: red/white; yellow/black; black/white
Geometry:
Use regular geometric forms (circle, triangle, square, rectangle); avoid sharp edges
Sizes:
Not more than three sizes; size differences exponential

## Slide 22: Forms of coding
Colour (red, yellow, green,…) Emphasizing of elements; for grouping; for status displays
Geometry (regular, irregular, round, square, etc.): For visual distinction, for location by touch; for grouping; for location at greater distances
Size: For the emphasizing of elements; searching for identical functions at greater distances; information on the significance of an element
Position: For emphasizing of significance, function, sequence of use, relationship to other elements
Einsatzes, Beziehung zu anderen Elementen
Examples: inconsistent use of colour, size, position of pushbuttons can reduce the speed of work by 10%-15%
Notes: The symbols providing the information are specified by coding of the information. The technical signals received on the work equipment are linked to a specific constellation of symbols and thus made perceivable. Assignment of the symbols to an item of information (decoding of the information by the operator) is characterized by regulations, instructions and conventions.
Benefits of the compatibility of coding:
Reductions in errors and in the time required for cognitive processing
Information that is not required for a certain task can be hidden
Reduction in the number of presentations and in the volume of information presented
Colour coding:
Suitable: red/white; yellow/black; black/white
Geometry:
Use regular geometric forms (circle, triangle, square, rectangle); avoid sharp edges
Sizes:
Not more than three sizes; size differences exponential

## Slide 23: Principles of compatibility
Compatibility
Compatibility between stimulus and response
Conceptual compatibility
Compatibility between the human-machine interface and the system image (expectations) in the user's mind
Spatial compatibility
compatibility with location and position)
Logic of location and assignment
Consideration for alternative, sequential and simultaneous use
Compatibility of the direction of motion
Logic of the direction of motion
Effect of the movement of the control actuator
Display consistent with the direction of motion

## Slide 24: Compatibility of location
Grouping of control actuators:
Grouping in lines and columns (regular assignment)
Principle of proximity: smaller distances between functionally related elements
Principle of symmetry (combination of different components of the same function within a system)
Principle of similarity (of the same type): elements identical in appearance are related in their function
nach E DIN EN 894-4
Notes: Structure of the arrangement:
Locate according to:
Function or dependency
Sequence of use
Frequency of use
Priority
Mode of operation (normal, emergency)
of the installation or machine implementation
Compatibility of the arrangement
If the control actuator is associated with a display, observe the following:
Arrange the control actuators in the same way as the associated displays
Design/position the control elements in relation to the displays
  According to importance
  According to frequency of use
  According to principles of operation
  According to sequence of use
Grouping of control actuators:
Grouping in lines and columns (regular assignment)
Smaller distances between elements (functional relationship) and greater distances between grouped units (separation)
Principle of symmetry (combination of different components of the same function within a system)
Principle of similarity (of the same type): elements of identical colour, geometry, size, behaviour (direction of movement) are regarded as belonging together functionally

## Slide 25: Compatibility of location
The location of the display and control elements corresponds to the layout in the installation itself
not compatible b) compatible
A
D
B
C
A B C D
A
D
B
C
A B C D
Based upon: CHAPANIS, A., & LINDENBAUM, I.E. (1959): A reaction time study of four control-display linkages. Human Factors, 1, 1-14.

## Slide 26: Compatibility of the direction of actuation (movement)
Compatibility of the direction between the direction of movement of the control element and the direction of the displayed change in measured value. The position and functionality of the display and control elements match the flow of material, energy or information
© Michael Hüter
Notes: Principles:
Locate control elements and their corresponding displays close together
Control element below/to the right of the display
If control elements and displays must be located on two different panels, arrange them with the same hierarchy and pattern
Same labelling visible above the control element and the display
Locate the control element and display from left to right in accordance with the specified (operating) sequence

## Slide 27: Compatibility of the direction of actuation (movement)
Push-pull knob:
Movement away from the control panel (pulling): increase
Movement towards the control panel (pushing): decrease
Raising, lowering with a lever in the horizontal direction of movement:
Lever forwards: Lowering
Lever backwards: Raising
On a vertical surface
On a horizontal surface
See E DIN EN 894-4
Observe the change in direction!
Source: based upon GRANDJEAN (1991)
Notes: Straight movements of levers, rocker switches, to the right, forwards or upwards mean on, increase.
Vertical switch panel: Up means increase
Horizontal switch panel: Away from the operator (forwards) means increase
Rotary selector switches: clockwise means increase
On overhead switch panels, switches should move from right to left rather than from top to bottom, since this is clearer and easier to distinguish.
As the images shows, when the switch is operated downwards, movement is in the opposite direction, which is less convenient.
The effect of push-pull buttons should be considered in relation to the surface into which they are fitted.

## Slide 28: Example: joystick on a wheel loader Source: IAG Dresden, in conjunction with the TU Dresden
Positive aspects:
Location of the buttons where they are reachable
Recessed arrangement of the buttons for prevention of inadvertent operation
Textured surface of the joystick, contributing to better tactile perception
Weak points include:
Compatibility of the selected direction of travel and the gear shift
No height-adjustable rest for the edge of the hand
Buttons for additional functions only partly distinguishable by touch
multi-purpose control actuators

## Slide 29: Example: joystick on a wheel loader
Proposal for improved design:
Exchange the buttons for preselection of the direction of travel, and design them in the form of arrows
Adapt the geometry of the buttons for shifting up/down (+ and -) to the function and exchange their locations, thus providing greater compatibility and better tactile distinction
Move the button for the neutral position (N) to a less readily accessible position, since it is used less frequently
Place the button for actuation of the horn in the index finger region of the joystick (i.e. on the rear face), thereby enabling the user to issue a warning signal to other persons without needing to take the hand off the multi-purpose control actuator
Height-adjustable rest for the edge of the hand can be implemented relatively easily
multi-purpose control actuators

## Slide 30: Fork-lift truck with rotating cab
Rotating cab for fork-lift trucks: can be rotated up to 180°
Provides the driver with a completely clear field of view; the load can be transported safely
Reversing with bulky loads no longer requires twisting of the trunk
Further ergonomic improvements to the seat
Jungheinrich: winner of the 2007 German OSH prize

## Slide 31: Important literature
EN 894-1 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Part 1: General principles for human interactions with displays and control actuators
EN 894-3 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Part 3: Control actuators
EN 894-4 Safety of machinery – Ergonomic requirements for the design of displays and control actuators – Part 4: Location and arrangement of displays and control actuators
EN ISO 13850 Safety of machinery – Emergency stop – Principles for design
ISO 1503 Spatial orientation and direction of movement – Ergonomic requirements
VDI/VDE 3850 Blatt 1 Gebrauchstaugliche Gestaltung von Benutzungsschnittstellen für technische Anlagen – Konzepte, Prinzipien und grundsätzliche Empfehlungen

## Slide 32: Important literature
EN 60447 Basic and safety principles for man-machine interface, marking and identification – Actuating principles
EN 61310-1 Safety of machinery – Indication, marking and actuation – Part 1: Requirements for visual, acoustic and tactile signals
EN 61310-2 Safety of machinery – Indication, marking and actuation – Part 2: Requirements for marking
EN 80416-4 Basic principles for graphical symbols for use on equipment – Part 4: Supplementary guidelines for the adaptation of graphical symbols for use on screens and displays (icons)
DIN 1410 Werkzeugmaschinen; Bewegungsrichtung und Anordnung der Stellteile
For further standards, see KAN-Praxis - NoRA: Normen recherchieren

## Slide 33: Important literature
BULLINGER, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
BULLINGER, H.-J.; KERN, P.; SOLF, J. J. (1979): Reibung zwischen Hand und Griff. Dortmund: Verlag für neue Wissenschaften GmbH. (Publications of the Bundesanstalt für Arbeitsschutz, Article 213)
BULLINGER, H.-J.; SOLF, J. J. (1979): Ergonomische Arbeitsmittelgestaltung. Dortmund: Verlag für neue Wissenschaften GmbH. (Publications of the Bundesanstalt für Arbeitsschutz, Articles 196-198)
GRANDJEAN, E. (1991): Physiologische Arbeitsgestaltung: Leitfaden der Ergonomie. 4th edition, Landsberg: Ecomed.
KIRCHNER, J.-H.; BAUM E. (1990): Ergonomie für Konstrukteure und Arbeitsgestalter. Munich: Carl Hanser.
LINDQVIST, B. (1997): Ergonomie bei Handwerkzeugen. Helsingborg: ABE Tryk.
SCHMAUDER, M.; SOLF, J. J. (1992): Einfluss der Händigkeit bei der Handhabung von Arbeitsmitteln. Bremerhaven: Wirtschaftsverlag NW Verlag für neue Wissenschaft. (Publications of the Bundesanstalt für Arbeitsmedizin und Arbeitsschutz, Article 661)
STRASSER, H. (2000): Ergonomische Qualität handgeführter Arbeitsmittel. Elektromyographische und subjektive Beanspruchungsermittlung. Stuttgart: Ergon Verlag.
.

## Slide 34: Impressum
Author: Dr.-Ing. Christiane Kamusella
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
Christiane.Kamusella@tu-dresden.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin www.kan.de/en http://ergonomie.kan-praxis.de/en