## Slide 1: Ergonomic aspects of the IT design of human-machine interfaces Part 2: Selection and design of displays
Module 4 – Learning ergonomics

## Slide 2: Overview
Indirect and direct information transfer
Sensory channels and suitable display types
Information types and suitable display types
Design of visual displays
© Michael Hüter
Notes: We need displays in order to obtain information on the progression and states of processes. This section deals with the correct selection and design of displays. It first teaches why we need indirect information transfer, and what displays are most suitable, with reference to the sensory channels used and the types of information concerned. The design of visual displays is then considered in more detail.

## Slide 3: Indication of information transfer
Direct transmission
of information
Rapid reception of information at high information densities
Indirect transmission of information
Direct reception of information by
human senses
Application desirable if indirect transmission of information ca
be avoided
Reception of information via displays
Decoding of the display required
Should be applied if:

The source of the information is inaccessible
Information not perceptible by human senses
Senses too imprecise
Information storage



Notes: Examples of direct transmission of information: vibration in moving parts or odours during overloading of machines

## Slide 4: Sensory channels and types of display
Visual displays
Analogue displays
Digital displays
Acoustic displays
Output systems
Tactile displays
Notes: The modality of possible display facilities must be geared to human sensory organs.
The possible modalities are:
Visual (sight)
Acoustic (hearing)
Tactile (feeling and touch)
Olfactory (smell)
Gustatory (taste)
Vestibular (balance)
Thermal
At present, the first three of these are primarily those suitable for technical displays. We therefore distinguish in the first instance between visual, acoustic and tactile displays.
Methods for selecting the type of displays  see next slide

## Slide 5: Aspects concerning the selection of displays
Criteria for visual displays
Criteria for acoustic displays
Large-scale, complex information
Local and temporal, discrete and continuous information
Information required several times
Information to be called up by the
observer
Information to be displayed simultaneously or sequentially
Constrained area of observation
Selective transmission of messages to individual observers or to a group
Space requirement in the field of fixation
A high ambient noise level is permissible
Small volume of information
Information is simple
Temporal, discrete information
Information is required only once
Information is to be observed immediately
Information is to be displayed sequentially
Observer location is variable
Transmission of information to a group High prominence
No space requirement in the field of fixation
Low or high lighting levels are permissible
Notes: The properties of acoustic perception are exceptionally well suited owing to its facility for clear differentiation between a large number of different signals. For the perception of highly complex information (such as a graph or image), visual perception is at least as good as acoustic perception; this does not hold true however for clear differentiation between certain signals.
Additional information on tactile displays (not shown on the slide):
– Perception is dependent upon physical contact
+ The only modality for sensing the properties of mechanical objects
– Only information of low complexity can be transferred
+ Intuitive incorporation into movement controls
+ Reaction time 20-150 ms
The details below focus upon the design of visual displays.

## Slide 6: Aspects concerning the selection of displays
Information type | Suitable visual displays | Suitable acoustic displays
Binary (two states) | Signal lamps | Horns, simple warning tones
Continuous (metric scale) | Traditional scale instruments | Machine speed (frequency audible)
Discrete (several fixed states) | Alphanumeric displays | Sirens, warning tones, noises of various kinds
Complex information | VDU displays (graphs, flow charts) | Speech, sounds and noises (e.g. monitoring by electrocardiograph in hospitals)

## Slide 7: Design of visual displays
Requirements concerning detectability
Positioning: areas A,B,C (ranking) to EN 894-2
Importance: most important displays in the optimum field of fixation (area A)
Warning signals: flashing or in combination with acoustic signals
A
A
B
A
A
B
B
B
C
C
-30°
C
C
-55°
Recommended visual fields to EN 894-2 for surveillance tasks
© Michael Hüter

## Slide 8: Design of visual displays
Criteria for identification
High image quality
Contrast at least 3:1; preferably 6:1
Anti-reflective cover glass
Select simple, familiar shapes for letters and figures
Use colours and grouping to prevent confusion between displays located close together
Observe different forms of perception task
Design and grouping in accordance with compatibility principles
Notes: For compatibility, see the following slides

## Slide 9: Suitable displays for different perception tasks
Based on: EN 894-2 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Displays
Notes: Relationship between the type of task and the type of display

## Slide 10: Compatibility
A display is compatible or logical when the design of the action or information output aspect of work equipment satisfies certain expectations on the part of the human operator
with regard to static/spatial assignment and location of the displays and control actuators and
regarding the assignment of dynamic processes to them
Notes: The essential goal during the design of displays is to permit use and readability that is clear and easy to learn. Compatibility is used to reach this aim.
Compatibility as such is an abstract concept which relates to widely disparate forms of similarity. By far the most frequently applied forms of compatibility are directional compatibility and spatial compatibility.
A map for example presents routes as if viewed from the air: we can find our way independently of our location and direction of view.
An analogy of this kind cannot however be made in all cases. If compatibility cannot be attained, conventions are used to define certain information in a way which, though arbitrary, is "universal". By this means, at least knowledge that has already been learnt can be transferred.
The most important conventions are:
a) Conventions of direction
b) Conventions of colour  next slide: this is described as conceptional compatibility.
Consideration of stereotypical behaviour which is conducive to compatibility during the design of work equipment leads to:
  Shortening of the learning and practice phase
  Enhancement of the qualitative and quantitative work performance
  Reduced risk of error

## Slide 11: Conceptual Compatibility
Consistency between the design of the display or control actuator with the system image in the user's mind
Free
Go
Neutral
Cool
Hazard
Hot
Caution
Light
Notes: Caution:
colours do not have the same significance in all cultures. This example relates to the German context.

## Slide 12: Compatibility principles for displays
Several displays: Angles for normal states are the same
Arrangement of displays in the same order (from left to right, from top to bottom) as the associated machines/control elements
Display of increase: to the right or upwards
Anzeige von Abnahme: Display of decrease: to the left or downwards
Source: DIN EN 894-2

## Slide 13: Design of visual displays
Criteria for the possible interpretation
Use the simplest signal possible (where possible, two states)
Display the simplest possible qualitative information
Only if this is not possible, select continuous displays: the smallest possible number of division marks, support by colouring of the scale, reference marks, adjustable marks
Group related displays
Source: DIN EN 894-2

## Slide 14: Literature
EN 894-1 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Part 1: General principles for human interactions with displays and control actuators
EN 894-2 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Part 2: Displays
EN 894-4 Safety of machinery – Ergonomic requirements for the design of displays and control actuators – Location and arrangement of displays and control actuators
EN 60447 Basic and safety principles for man-machine interface, marking and identification – Actuating principles
EN 61310-1 Safety of machinery – Indication, marking and actuation – Requirements for visual, acoustic and tactile signals
ISO 80416-4 Basic principles for graphical symbols for use on equipment – Supplementary guidelines for the adaptation of graphical symbols for use on screens and displays (icons)
EN ISO 11064-5 Ergonomic design of control centres – Displays and controls
DIN-Taschenbuch 354 Software-Ergonomie
Weitere Normen finden Sie unter KAN-Praxis – NoRA: Normen recherchieren.

## Slide 15: Literature
BULLINGER, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
BULLINGER, H.-J.; SOLF, J. J. (1979): Ergonomische Arbeitsmittelgestaltung. Dortmund: Verlag für neue Wissenschaften GmbH. (Publications of the Bundesanstalt für Arbeitsschutz, Articles 196-198)
GÖBEL, M. (2000): Von der Ärgonomie zur ERGONOMIE. Lehrunterlagen. Berlin: Technische Universität Berlin.
GRANDJEAN, E. (1991): Physiologische Arbeitsgestaltung: Leitfaden der Ergonomie. 4th edition, Landsberg: Ecomed.
GREIL, H.; SCHEFFLER, C. (eds.) (2001): Mensch-Technik-Umwelt. Potsdam: Universität Potsdam. (Publications of the Zentrum für Umweltwissenschaften der Universität Potsdam, Brandenburgische Umweltberichte 10/2001).
KIRCHNER, J.-H.; BAUM E. (1990): Ergonomie für Konstrukteure und Arbeitsgestalter. Munich: Carl Hanser.
LANDAU, K. (eds.) (2003): Arbeitsgestaltung und Ergonomie. Good Practice. Stuttgart: ergonomia Verlag.
LAURIG, W. (1992): Grundzüge der Ergonomie. Erkenntnisse und Prinzipien. 4th edition. Berlin: Beuth Verlag.

## Slide 16: Impressum
Author: Dipl.-Ing. Silke Paritschkow
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
silke.paritschkow@tu-dresden.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin http://www.kan.de/en/
http://ergonomie.kan-praxis.de/en