## Slide 1: Ergonomic aspects of the IT design of human-machine interfaces Part 3: Analogue and digital displays
Module 4 -Learning ergonomics

## Slide 2: Overview
Application cases for analogue and digital displays
Possible displays
Types of analogue display
Design of VDU displays
© Michael Hüter
Notes: Visual displays can be divided into analogue and digital displays. In this part of the lecture, we will look at the following issues relating to the selection and design of analogue and digital displays:
Application cases for analogue and digital displays
Possible displays
Types of analogue display
Design of VDU displays

## Slide 3: Application cases for analogue and digital displays
Quantitative
reading off
Comparing
of displays
Setting
of values
Adjusting
Qualitative
reading off
Analogue display
Digital display
Description
Round
scale
display
Sectoral
scale
display
Strip
display
scale
Rotating
drum
display
LED
numerical
display
VDU
Pointer
Pointer
Pointer
Scale
Figure
Character
0
10
2
0
30
4
0
50
60
70
80
90
100
0
10
20
30
40
50
60
0
10
20
30
40
50
0
10
20
3
LED
bar
display
Bar
0
10
20
30
40
2 3 4 5
3
Reliable
reading off
Unsuitable
Partly
suitable
Suitable
Very suitable
Highly
suitable
Active element
Selection criteria
Image
Legend:
Notes: A task frequently encountered is that of displaying measured quantities (such as speeds, temperatures or time) expressed in the form of a numerical value. An essential distinction is drawn here between analogue and digital display types. In analogue displays, quantities are displayed in infinitely variable form.
Instruments with a moving pointer or moving scale are generally employed for this purpose. Analogue displays are therefore suitable for continually changing processes, since they enable not only the measured value to be viewed, but also changes to it, and operating states therefore to be presented effectively.
Digital displays essentially display only discrete, i.e. stepped values. If multiple discrete digits are chained, however, numerical values can be presented with high granularity and the values consequently displayed with much greater precision than is possible on analogue displays.
However, changes in values are much harder to observe on digital than on analogue displays. This applies to both the direction (measured value increasing or decreasing) and rate of change. Values changing rapidly cannot generally be read at all. Conversely, where sufficient time is available, values can be read off very reliably. Digital displays also generally occupy less space.
Digital displays are generally preferred in cases in which a final value must be read off reliably and with a high degree of precision, such as on filling station pumps, scales and stopwatches.

## Slide 4: Possible displays
Setpoint display
Actual value display
Difference display
-
-333
Integrated display
-333
Range display
Notes: Integrated displays aim to combine the benefits of both analogue and digital displays by using two different elements to display the absolute display value and changes to it.

## Slide 5: Types of analogue display
Types of analogue display (from SCHMIDTKE, H. (1993): Ergonomie. 3rd edition. Munich: Carl Hanser)
Round scales
Strip scales
Moving pointer
Moving scale
Sector scale
Full-circle scale
Notes: Instruments may employ either a moving pointer or a moving scale. The moving pointer assures fast and reliable orientation, but requires a larger area. The moving scale generally allows the value to be read off more reliably; however, the magnitude of the value read off cannot be determined as easily, owing to the absence of reference information. (This can be redressed for example by means of different colour backgrounds for the scale.)
Strip scales can be used in place of round scales for both of the display types. Where a general impression of a value's magnitude is needed, however, strip scales with moving pointer are inferior to round scales, since the former lack the information provided by the angular position of the pointer (on the round scale, the reference point of the pointer remains fixed, whereas the viewer must first locate the pointer on the strip scale).
In continually changing processes (such as the time), a full-circle scale is used. For measured values with a defined beginning and end state (such as vehicle speeds), a sector scale is employed.

## Slide 6: Examples of scale divisions and markings
Source: EN 894-2: Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Displays

## Slide 7: Design of VDU displays
VDU displays suitable for the display of complex information
    Graphs
    Flow charts
    Diagrams
    Interactive dialogs
Note:
  Content easily recognizable
  Owing to diversity of possible display content, facility for interpretation is a requirement
  Assure that the desired information can be selected
Notes: VDUs are preferred for the display of complex information (such as graphs, flow charts or diagrams). Their advantage is their huge flexibility in the display of information. This permits concentration on the relevant information at a particular location, according to the state. This is at the same time their drawback, since:
The content must be recognized for what it is, and cannot be identified by virtue of its location
(as is the case with signal lamps).
Owing to the great diversity of possible display content, users may be confronted with new
forms of information which they are not immediately able to interpret (unless they have been
trained for all possible display permutations).
3. Owing to the constraints of the display area, it may not be possible to display all relevant
information simultaneously. In such cases, a means for selection is required.

## Slide 8: Design of VDU displays
Source: Kraus, L. (2003): Entwicklung und Evaluation einer Methodik zur Untersuchung von Interaktionsgeräten für Maschinen- und Prozessbedien- systeme mit grafischen Benutzungsoberflächen. Dissertation. Fortschritt-Berichte pak Vol. 7 Kaiserslautern: Verlag Universität Kaiserslautern.
Design dimensions
Office context
Industrial context
Tasks
Logical dialog design
Graphical dialog design
Generalized
Content and sequence not consistent
Multi-document interface
User-driven dialog
Dialogs barely modal
Substantial menu depth
Undefined layout areas
Information obscured (windows)
Specialized
Content and sequence consistent
Single-document interface
System-driven and user-driven dialog
Dialogs partly modal
Shallow menu depth
Defined layout areas
No covering of information (screen forms, tiling)
© Michael Hüter

## Slide 9: Literature
EN 894-1 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Part 1: General principles for human interactions with displays and control actuators
EN 894-2 Safety of machinery – Ergonomics requirements for the design of displays and control actuators – Part 2: Displays
EN 894-4 Safety of machinery - Ergonomic requirements for the design of displays and control actuators – Part 4: Location and arrangement of displays and control actuators
EN 60447 Basic and safety principles for man-machine interface, marking and identification – Actuating principles
EN 61310-1 Safety of machinery – Indication, marking and actuation – Part 1: Requirements for visual, acoustic and tactile signals
EN 80416-4 Basic principles for graphical symbols for use on equipment – Part 4: Supplementary guidelines for the adaptation of graphical symbols for use on screens and displays (icons)
EN ISO 11064-5 Ergonomic design of control centres – Part 5: Displays and controls
For further standards, see KAN-Praxis – NoRA: Searching for standards.

## Slide 10: Literature
BULLINGER, H.-J. (1994): Ergonomie: Produkt- und Arbeitsplatzgestaltung. Stuttgart: Teubner.
BULLINGER, H.-J.; SOLF, J. J. (1979): Ergonomische Arbeitsmittelgestaltung. Dortmund: Verlag für neue Wissenschaften GmbH. (Publications of the Bundesanstalt für Arbeitsschutz, Articles 196-198)
GÖBEL, M. (2000): Von der Ärgonomie zur ERGONOMIE. Lehrunterlagen. Berlin: Technische Universität Berlin.
GRANDJEAN, E. (1991): Physiologische Arbeitsgestaltung: Leitfaden der Ergonomie. 4th edition, Landsberg: Ecomed.
GREIL, H.; SCHEFFLER, C. (eds.) (2001): Mensch-Technik-Umwelt. Potsdam: Universität Potsdam. (Publications of the Zentrum für Umweltwissenschaften der Universität Potsdam, Brandenburgische Umweltberichte 10/2001).
HUELKE, M. (2005): Gestaltung von Stellteilen und Anzeigen, lecture at the symposium „Anforderungen an die ergonomische Gestaltung von Maschinen der Metallbearbeitung“ of FA MFS, Lengfurt, 2005: http://www.dguv.de/medien/ifa/de/pra/checkliste/gestaltung_stellteile_und_anzeigen.pdf,
recalled June 23th 2011
KIRCHNER, J.-H.; BAUM E. (1990): Ergonomie für Konstrukteure und Arbeitsgestalter. Munich: Carl Hanser.
LANDAU, K. (eds.) (2003): Arbeitsgestaltung und Ergonomie. Good Practice. Stuttgart: ergonomia Verlag.

## Slide 11: Impressum
Author: Dipl.-Ing. Silke Paritschkow
TU Dresden – Fakultät Maschinenwesen
Institut für Technische Logistik und Arbeitssysteme
Professur für Arbeitswissenschaft
silke.paritschkow@tu-dresden.de
Initiated and funded by
Kommission Arbeitsschutz und Normung (KAN) Alte Heerstraße 111 53757 Sankt Augustin http://www.kan.de/en/ http://ergonomie.kan-praxis.de/en/tuition-modules/